HEC-RAS September 1998 Version 2.2

U.S. Army Corp of Engineers

Hydrologic Engineering Center

609 Second Street, Suite D

Davis, California 95616-4687

(916) 756-1104

X     X  XXXXXX    XXXX        XXXX       XX      XXXX

X     X  X        X    X       X   X     X  X    X

X     X  X        X            X   X    X    X   X

XXXXXXX  XXXX     X       XXX  XXXX     XXXXXX    XXXX

X     X  X        X            X  X     X    X        X

X     X  X        X    X       X   X    X    X        X

X     X  XXXXXX    XXXX        X    X   X    X   XXXXX

PROJECT DATA

Project Title: Peterborough 1979 FIS Import - ConMulti

Project File : 79ConM.prj

Run Date and Time: 12/13/00 10:20:32 AM

Project in English units

Project Description:

1979 PETERBOROUGH NH FIS (HEC2 IMPORT)

Direct 1979 RAS Import 01:

-Converted dams from HEC2 bridges to Inline Weirs

-Adjusted bridge modeling parameters to match Duplicate HEC2

PLAN DATA

Plan Title: Imported Plan 01

Plan File : d:\My Documents\H&H\Pboro\ConRAS\79ConM.p01

Geometry Title: Imported Geom 01

Geometry File : d:\My Documents\H&H\Pboro\ConRAS\79ConM.g01

Flow Title    : Imported Flow 01

Flow File     : d:\My Documents\H&H\Pboro\ConRAS\79ConM.f01

Plan Summary Information:

Number of:  Cross Sections =   82    Mulitple Openings =    0

Culverts       =    0    Inline Weirs      =    3

Bridges        =    6

Computational Information

Water surface calculation tolerance =  0.01

Critical depth calculaton tolerance =  0.01

Maximum number of interations       =  20

Maximum difference tolerance        =  0.3

Flow tolerance factor               =  0.001

Computation Options

Critical depth computed only where necessary

Conveyance Calculation Method: Between every coordinate point (HEC2 Style)

Friction Slope Method:         Average Conveyance

Computational Flow Regime:     Subcritical Flow

Encroachment Data

Equal Conveyance = True

Left Offset      =        0

Right Offset     =        0

River = RIVER-1          Reach = Reach-1

RS      Profile           Method  Value1  Value2

1       PF 6                   1     880    1930

2       PF 6                   1   866.2 1126.07

3       PF 6                   1     948 1140.63

4       PF 6                   1     840    2215

5       PF 6                   1    1030    2550

6       PF 6                   1     970    1730

7       PF 6                   1     945    1580

8       PF 6                   1 1314.76    2090

9       PF 6                   1  875.81 1220.63

10      PF 6                   1  736.65 1348.68

11      PF 6                   1 1219.87    2052

12      PF 6                   1    1957    2052

13      PF 6                   1     945    1250

14      PF 6                   1     900    1140

15      PF 6                   1  1900.5    2083

16      PF 6                   1    1917    2064

17      PF 6                   1  1943.1  2056.9

18      PF 6                   1  1943.1  2056.9

19      PF 6                   1   943.1  1056.9

20      PF 6                   1     923    1064

21      PF 6                   1     913    1090

22      PF 6                   1     889    1099

22.5    PF 6                   0

23      PF 6                   1     889    1099

24      PF 6                   1     876    1106

25      PF 6                   1     946    1054

26      PF 6                   1     925 1119.21

27      PF 6                   1     790    1030

28      PF 6                   1    1320    2070

29      PF 6                   1     900    1062

30      PF 6                   1     940    1067

31      PF 6                   1     935    1060

32      PF 6                   1     926  1054.1

33      PF 6                   1   962.2  1037.8

33.5    PF 6                   0

34      PF 6                   1   962.2  1037.8

35      PF 6                   1     950 1073.15

36      PF 6                   1     944  1077.8

37      PF 6                   1     944    1078

37.5    PF 6                   0

38      PF 6                   1     944    1078

39      PF 6                   1     871    1075

40      PF 6                   1     932    1075

41      PF 6                   1     928    1080

42      PF 6                   1    1941    2083

43      PF 6                   1    1926    2068

43.5    PF 6                   0

44      PF 6                   1    1926    2068

45      PF 6                   1    1950    2040

46      PF 6                   1     550    1670

47      PF 6                   1     970    1027

48      PF 6                   1     960    1060

49      PF 6                   1   962.5  1037.5

49.5    PF 6                   0

50      PF 6                   1   962.5  1037.5

51      PF 6                   1     948 1044.66

52      PF 6                   1     885    1063

53      PF 6                   1     967    1035

54      PF 6                   1     830    1025

55      PF 6                   1     828    1025

56      PF 6                   1     782    1036

56.5    PF 6                   0

57      PF 6                   1     782    1037

58      PF 6                   1     782    1045

59      PF 6                   1   895.5    1071

60      PF 6                   1    1880    2115

61      PF 6                   1     888  1060.5

61.5    PF 6                   0

62      PF 6                   1     686  1060.5

63      PF 6                   1    1780    2100

64      PF 6                   1    1810    2200

65      PF 6                   1    1966 2188.35

66      PF 6                   1     720    1031

67      PF 6                   1     917    1450

68      PF 6                   1     943    1070

68.5    PF 6                   0

69      PF 6                   1     872    1109

70      PF 6                   1     955    1500

71      PF 6                   1     955    1500

72      PF 6                   1     950    1200

73      PF 6                   1     745    1090

74      PF 6                   1     705    1090

75      PF 6                   1     950    1080

76      PF 6                   1     950    1035

77      PF 6                   1  967.25    1032

77.5    PF 6                   0

78      PF 6                   1  967.25    1032

79      PF 6                   1     957    1059

80      PF 6                   1     775    1029

81      PF 6                   1     900    1040

82      PF 6                   1     960    1025

FLOW DATA

Flow Title: Imported Flow 01

Flow File : d:\My Documents\H&H\Pboro\ConRAS\79ConM.f01

Flow Data (cfs)

River           Reach           RS                   PF 1            PF 2            PF 3            PF 4            PF 5            PF 6

RIVER-1         Reach-1         82                   1850            3470            4300            7950            4300            4300

RIVER-1         Reach-1         80                   2300            4310            5700            9890            5700            5700

RIVER-1         Reach-1         53                   2660            4990            7150           11430            7150            7150

RIVER-1         Reach-1         40                   2890            5420            7500           12415            7500            7500

RIVER-1         Reach-1         14                   3235            6065            9150           13900            9150            9150

Boundary Conditions

River           Reach           Profile                       Upstream                 Downstream

RIVER-1         Reach-1         PF 1                                               Known WS = 685.27

RIVER-1         Reach-1         PF 2                                               Known WS = 687.73

RIVER-1         Reach-1         PF 3                                               Known WS = 689.39

RIVER-1         Reach-1         PF 4                                               Known WS = 692.31

RIVER-1         Reach-1         PF 5                                               Known WS = 689.39

RIVER-1         Reach-1         PF 6                                               Known WS = 690.39

GEOMETRY DATA

Geometry Title: Imported Geom 01

Geometry File : d:\My Documents\H&H\Pboro\ConRAS\79ConM.g01

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 82

INPUT

Description: 12.704

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

726     880   732.4   878.2   747.2   877.6   769.2   870.8   790.4   870.2

818   868.8     850   859.2   878.8   857.4     906   856.2   906.1   856.2

920   851.9     970   852.3     982     848     984   846.2    1000     846

1016   846.1    1018     848    1055   855.6  1055.1   855.6  1055.2   855.6

1072.9   858.3  1127.3   862.8  1196.5   870.8  1232.9   875.8  1233.7   875.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

726     .06     982    .037    1018     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

982    1018             2350    2445    2400             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 81

INPUT

Description: 12.271

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

545.6     850   564.4   838.1   579.2   830.9     588   833.6   622.8   834.8

642.8   831.6     686   827.4     738   824.4   817.6   824.7   881.2   822.9

910   817.6     943   818.2     965   816.1     967   815.1    1000   814.6

1033   814.9    1035   816.1    1050   825.8  1050.1   825.8  1050.2   825.8

1081.2   825.8  1158.8   850.3  1158.9   850.3    1159   850.3  1159.1   850.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

545.6     .07     965    .037    1035     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

965    1035             2450    2555    2500             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 80

INPUT

Description: 11.809

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

722   835.4   729.6   833.9   774.4     803   788.8   800.6   839.8   802.1

880.4   801.2   889.2   804.4     912   805.6   944.4   806.2   944.5   806.2

959     807     985   795.3     987   794.3    1000   793.5    1013   794.3

1015   795.3    1034   806.6  1034.1   806.6  1034.2   806.6  1034.3   806.8

1068.5   829.4  1085.7   837.4  1085.8   837.4  1085.9   937.4    1086   837.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

722     .06     985    .037    1015    .055

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

985    1015             1795    2200    2270             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 79

INPUT

Description: 11.43

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

684   819.3   721.6   819.3   772.8   793.1   794.4   786.9   829.2   791.4

862   792.2   893.6   788.4   919.6   785.1   919.7   785.1   919.8   785.1

944   793.2     957   793.1     973     782     976   780.5    1000   778.2

1024   779.3    1027   782.1    1049   783.5    1059   787.8    1080   788.7

1100   807.4  1126.8   818.7  1153.2     836  1169.2     844  1194.4   848.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

684     .09     973    .037    1027     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

973    1027               40      40      40             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 78

INPUT

Description: 11.422

This is a REPEATED section.

Station Elevation Data    num=      34

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

880   793.9     928   793.4     950   793.2   955.5   792.9     958   790.2

958.3   794.2   958.9   786.2   959.8   785.2     962   783.7   967.2   782.7

967.25   782.7   969.5   782.4   971.9   782.2     976   781.8   981.5   781.7

988   779.8   991.8   779.6   994.5   779.5     996   779.5  997.25   779.5

1002   778.8    1004   778.8    1006  778.45    1008   778.3  1012.5   778.2

1018.5   777.9 1023.75   777.9    1026   777.9    1030   777.9    1032   779.6

1032.1   779.7  1051.5  792.25    1080   792.2    1100   807.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

880     .09  967.25    .037    1032     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

967.25    1032             22.5    22.5    22.5             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

880  967.25  792.26    1032    1100     792

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 77.5

INPUT

Description: Bridge #9

Distance from Upstream XS =       0

Deck/Roadway Width        =    22.5

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      28

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

880   793.7       0     928   793.2       0     950     793       0

955.5   792.7       0     958   792.5       0   967.2  792.26       0

967.25  792.28   782.5   971.9  792.26   786.5     976  792.26     788

981.5  792.26   789.1     988  792.25     788   991.8  792.24   786.8

994.5  792.23     785     996  792.22     783  997.25  792.22   779.3

1002  792.21   778.8    1004   792.2     783    1006  792.19     785

1008  792.18   786.5  1012.5  792.17   788.7  1018.5  792.16   789.1

1023.75  792.13     788    1026  792.11   786.5    1030  792.09     783

1032  792.08   779.4  1032.1  792.06       0  1051.5  792.03       0

1080     792       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      34

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

880   793.9     928   793.4     950   793.2   955.5   792.9     958   790.2

958.3   794.2   958.9   786.2   959.8   785.2     962   783.7   967.2   782.7

967.25   782.7   969.5   782.4   971.9   782.2     976   781.8   981.5   781.7

988   779.8   991.8   779.6   994.5   779.5     996   779.5  997.25   779.5

1002   778.8    1004   778.8    1006  778.45    1008   778.3  1012.5   778.2

1018.5   777.9 1023.75   777.9    1026   777.9    1030   777.9    1032   779.6

1032.1   779.7  1051.5  792.25    1080   792.2    1100   807.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

880     .09  967.25    .037    1032     .07

Bank Sta: Left   Right    Coeff Contr.   Expan.

967.25    1032             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

880  967.25  792.26    1032    1100     792

Downstream  Deck/Roadway Coordinates

num=      28

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

880   793.7       0     928   793.2       0     950     793       0

955.5   792.7       0     958   792.5       0   967.2  792.26       0

967.25  792.28   782.5   971.9  792.26   786.5     976  792.26     788

981.5  792.26   789.1     988  792.25     788   991.8  792.24   786.8

994.5  792.23     785     996  792.22     783  997.25  792.22   779.3

1002  792.21   778.8    1004   792.2     783    1006  792.19     785

1008  792.18   786.5  1012.5  792.17   788.7  1018.5  792.16   789.1

1023.75  792.13     788    1026  792.11   786.5    1030  792.09     783

1032  792.08   779.4  1032.1  792.06       0  1051.5  792.03       0

1080     792       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      34

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

880   793.7     928   793.2     950     793   955.5   792.7     958     790

958.3     794   958.9     786   959.8     785     962   783.5   967.2   782.5

967.25   782.5   969.5   782.2   971.9     782     976   781.6   981.5   781.5

988   779.6   991.8   779.4   994.5   779.3     996   779.3  997.25   779.3

1002   778.6    1004   778.6    1006  778.25    1008   778.1  1012.5     778

1018.5   777.7 1023.75   777.7    1026   777.7    1030   777.7    1032   779.4

1032.1   779.5  1051.5  792.05    1080     792    1100     807

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

880     .09  967.25    .037    1032     .07

Bank Sta: Left   Right    Coeff Contr.   Expan.

967.25    1032             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

880  967.25   789.1    1032    1100   789.1

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =     792

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Piers =  1

Pier Data

Pier Station     Upstream= 999.625    Downstream= 999.625

Upstream     num=       2

Width   Elev    Width   Elev

8   777.9       8   789.1

Downstream     num=       2

Width   Elev    Width   Elev

8   777.7       8   789.1

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Yarnell                KVal =    1.25

Selected Low Flow Methods = Yarnell

High Flow Method

Energy Only

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 77

INPUT

Description: 11.418

Station Elevation Data    num=      34

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

880   793.7     928   793.2     950     793   955.5   792.7     958     790

958.3     794   958.9     786   959.8     785     962   783.5   967.2   782.5

967.25   782.5   969.5   782.2   971.9     782     976   781.6   981.5   781.5

988   779.6   991.8   779.4   994.5   779.3     996   779.3  997.25   779.3

1002   778.6    1004   778.6    1006  778.25    1008   778.1  1012.5     778

1018.5   777.7 1023.75   777.7    1026   777.7    1030   777.7    1032   779.4

1032.1   779.5  1051.5  792.05    1080     792    1100     807

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

880     .09  967.25    .037    1032     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

967.25    1032               30      30      30             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

880  967.25   789.1    1032    1100   789.1

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 76

INPUT

Description: 11.412

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

722   799.1     773   792.8     795     787     830     791     862   791.9

890     790     945     785     970   782.9     973     781     976   778.7

1000   777.9    1024   777.5    1027   780.3    1047   783.5    1050     785

1060     790    1090     791    1110     791    1125   792.5    1140     800

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

722     .09     970    .037    1027     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

970    1027             1000     955     900             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 75

INPUT

Description: 11.223

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

738     795     788     790     826   786.2     830     789     855     789

865   785.6     888     785     917     782     972     780     973     776

1000   774.3    1049     776    1060     780    1103     781    1110   783.2

1130   783.2    1140     785    1160     790    1170     795    1205     800

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

738     .09     972    .037    1049     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

972    1049              880     930     970             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 74

INPUT

Description: 11.04

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

551.6   785.1     578   785.1   603.2   785.1   624.8   784.8   661.2   777.7

741.6   776.5   813.6   776.5     872   776.5   872.1   776.5   872.2   776.5

880   775.9     934   776.4     968     773     970   772.2    1000     772

1029     771    1032     773    1037   776.6    1065   777.9  1065.1   777.9

1088.2   778.6  1127.8   780.9  1195.4   782.4    1220     785    1308     790

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

551.6     .08     934    .035    1037     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

934    1037              750     880     855             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 73

INPUT

Description: 10.97

Station Elevation Data    num=       9

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

655     783     675     780     970     775     975   771.4    1000   770.2

1025   771.4    1030     775    1150     780    1368     785

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

655     .08     975    .035    1025     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

975    1025              500     540     480             .4       .8

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 72

INPUT

Description: 10.866

Station Elevation Data    num=      18

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

884     790     885     781     915     781     930     780     960     775

986   770.5    1000   768.8    1020   770.7    1030     773    1050     775

1340   776.5    1365   776.5    1370     775    1677     780    2030     785

2190     790    2290     795    2335     800

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

884     .08     960    .035    1050     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

960    1050              570     565     470             .4       .8

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 71

INPUT

Description: 10.752

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

824     790     830     779     936     775     955     770     972     769

984   767.4    1000     767    1017   767.8    1022     769    1038     770

1050     775    1170   774.5    1190   774.5    1200     775    1201     790

1462   767.5    1528   767.7  1563.6   766.1  1587.6   772.3  1674.4   770.8

1784.4   769.3  1842.4   770.8    1918   772.3  1956.4   774.7  2003.2   779.6

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

824     .07     955    .035    1038     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

955    1038              460     340     225             .5        1

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 70

INPUT

Description: 10.681

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

791.6   801.5   807.2     797     808     785     930     780     967     775

970     770     972   773.3     973   767.7     976   766.3    1000   766.3

1026   767.3    1029   767.7    1055   776.2    1095   771.3  1095.1   771.3

1134.4   774.1    1152   774.1  1206.4     772  1293.2   770.2  1374.8   767.6

1462   767.6    1528   767.6  1563.6   766.1  1587.6   772.3  1674.4   770.8

1764.4   769.3  1842.4   770.8    1918   772.3  1956.4   774.7  2003.2   779.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

791.6     .07     973    .033    1055     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

973    1055               40      40      40             .4       .8

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 69

INPUT

Description: 10.677

This is a REPEATED section.

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

871.8   774.8     894     775     950   773.4     970   767.7   971.7   767.6

971.8   767.5   973.4   767.4   973.5   767.4    1000   766.3  1026.5   767.8

1026.6   767.8  1028.2   767.9  1028.3   767.9    1083   775.4    1109   775.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

871.8     .07   973.5    .033  1026.5     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

973.5  1026.5               24      24      24             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

871.8   973.5   774.8  1026.5    1109   775.3

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 68.5

INPUT

Description: Bridge #8

Distance from Upstream XS =       0

Deck/Roadway Width        =      24

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      13

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

871.8   774.8       0     894     775       0   971.7   775.7       0

971.8   778.4       0   973.4   778.4       0   973.5   778.4   772.7

1000   778.4   772.7  1026.5   778.4   772.7  1026.6   778.4       0

1028.2   778.4       0  1028.3   775.7       0    1083   775.4       0

1109   775.3       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

871.8   774.8     894     775     950   773.4     970   767.7   971.7   767.6

971.8   767.5   973.4   767.4   973.5   767.4    1000   766.3  1026.5   767.8

1026.6   767.8  1028.2   767.9  1028.3   767.9    1083   775.4    1109   775.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

871.8     .07   973.5    .033  1026.5     .09

Bank Sta: Left   Right    Coeff Contr.   Expan.

973.5  1026.5             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

871.8   973.5   774.8  1026.5    1109   775.3

Downstream  Deck/Roadway Coordinates

num=      13

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

871.8   774.8       0     894     775       0   971.7   775.7       0

971.8   778.4       0   973.4   778.4       0   973.5   778.4   772.7

1000   778.4   772.7  1026.5   778.4   772.7  1026.6   778.4       0

1028.2   778.4       0  1028.3   775.7       0    1083   775.4       0

1109   775.3       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

871.8   774.6     894   774.8     950   773.2     970   767.5   971.7   767.4

971.8   767.3   973.4   767.2   973.5   767.2    1000   766.1  1026.5   767.6

1026.6   767.6  1028.2   767.7  1028.3   767.7    1083   775.2    1109   775.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

871.8     .07   973.5    .033  1026.5     .09

Bank Sta: Left   Right    Coeff Contr.   Expan.

973.5  1026.5             .4       .8

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

871.8   973.5   772.7  1026.5    1109   772.7

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   774.8

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =    1.17

Selected Low Flow Methods = Energy

High Flow Method

Energy Only

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 68

INPUT

Description: 10.673

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

871.8   774.6     894   774.8     950   773.2     970   767.5   971.7   767.4

971.8   767.3   973.4   767.2   973.5   767.2    1000   766.1  1026.5   767.6

1026.6   767.6  1028.2   767.7  1028.3   767.7    1083   775.2    1109   775.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

871.8     .07   973.5    .033  1026.5     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

973.5  1026.5               55      55      55             .4       .8

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

871.8   973.5   772.7  1026.5    1109   772.7

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 67

INPUT

Description: 10.667

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

690     800     715     795     720     790     735     785     770     780

890     775     952     770     974     768     984   765.5    1000     765

1013   765.5    1017   768.1    1038     770    1080   768.8    1120     770

1129   770.3    1147     770    1270     768    1410     770    1495     775

1530     777    1570     775    1620     770    1640   769.3    1665     770

1685     775    1805     780    1812     785    1845     790    1855     795

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

690     .07     952    .033    1038     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

952    1038              360     830     450             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 66

INPUT

Description: 10.567

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

60     800      70     795      75     790      83     785     115     780

245     775     350     770     380   768.6     430     768     560     768

600     770     680     770     740     770     775     770     890     770

909     770     938     770     940     770     982   762.7    1000     762

1018   763.1    1031     770    1043     775    1052     780    1069     785

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

60     .07     940     .03    1031     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

940    1031              510     915     825             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 65

INPUT

Description: 10.456

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1380     785    1420     780    1560     775    1570     773    1600     773

1670     770    1687   769.2    1700     770    1838   771.7    1915     770

1968     765    1972   761.3    2000     761    2028   761.3    2031   764.1

2278   764.8    2300     770    2320     775    2355     780    2390     785

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1380     .06    1968     .03    2031     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1968    2031              565     625     690             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 64

INPUT

Description: 10.366

Station Elevation Data    num=      24

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

860     790     990     765    1020     780    1115     775    1263     771

1410   768.5    1680   768.5    1719   768.5    1761     770    1775   770.3

1778     770    1810   769.4    1840   765.3    1988     763    1990   760.8

2000   760.5    2010   760.8    2012     763    2128   765.3    2200   768.5

2720   768.5    2730     770    2750     775    2755     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

860     .06    1810     .03    2200     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1810    2200             1100    1120    1025             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 63

INPUT

Description: 10.26

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1079   786.6  1151.8   779.8  1241.8   780.4  1269.8   778.9  1324.6   776.4

1352.2   775.2    1375   774.4  1392.2   769.4  1540.2     768  1670.2     768

1705.8     768  1725.8     768  1755.4   767.9  1755.5   767.9  1755.6   767.9

1768   767.8    1817   767.4    1823   764.1    1840   762.7    1980   762.7

2000   759.2    2080     760    2103     760    2120     770    2150     775

2209   777.6  2209.1   777.6  2209.2   777.6  2209.3   777.6  2209.4   777.6

2224.8   779.8  2256.8     781  2298.4   779.5  2358.4   785.1    2422     792

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1079     .05    1817     .03    2120     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1817    2120               40      40      40             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 62

INPUT

Description: 10.253

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

555     777     613   776.3     650     773     689   768.5     705   768.5

750     768     790     768     809   766.8   888.4   765.6   888.5   765.6

940     765   940.1   760.7     950   759.2     968   758.7     997   759.8

1030   759.6  1060.5   762.7  1060.6     765    1114   765.7    1133   767.5

1170   773.8    1250   776.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

555     .05   940.1     .03  1060.5     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

940.1  1060.5               20      20      20             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

555   940.1   768.5  1060.5    1250   772.6

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 61.5

INPUT

Description: Bridge #7

Distance from Upstream XS =       0

Deck/Roadway Width        =      20

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      15

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

555     777       0     613   776.3       0     650     773       0

689   768.5       0     705   768.5       0     750   768.5       0

790   768.5       0   888.5   768.5       0     940   772.6       0

940.1   772.6     769  1060.5   772.6     769  1060.6   772.6       0

1133   772.6       0    1170   773.8       0    1250   776.5       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

555     777     613   776.3     650     773     689   768.5     705   768.5

750     768     790     768     809   766.8   888.4   765.6   888.5   765.6

940     765   940.1   760.7     950   759.2     968   758.7     997   759.8

1030   759.6  1060.5   762.7  1060.6     765    1114   765.7    1133   767.5

1170   773.8    1250   776.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

555     .05   940.1     .03  1060.5     .06

Bank Sta: Left   Right    Coeff Contr.   Expan.

940.1  1060.5             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

555   940.1   768.5  1060.5    1250   772.6

Downstream  Deck/Roadway Coordinates

num=      15

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

555     777       0     613   776.3       0     650     773       0

689   768.5       0     705   768.5       0     750   768.5       0

790   768.5       0   888.5   768.5       0     940   772.6       0

940.1   772.6     769  1060.5   772.6     769  1060.6   772.6       0

1133   772.6       0    1170   773.8       0    1250   776.5       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

555     777     613   776.3     650     773     669   768.5     705     768

750     768   888.4     768   888.5     771     890     771   890.1   765.6

940     765   940.1   760.7     950   759.2     968   758.7     997   759.8

1030   759.6  1060.5   762.7  1060.6     765    1114   765.7    1133   767.5

1170   773.8    1250   776.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

555     .06   940.1     .03  1060.5     .06

Bank Sta: Left   Right    Coeff Contr.   Expan.

940.1  1060.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

555   940.1     768  1060.5    1250     769

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   768.5

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Piers =  1

Pier Data

Pier Station     Upstream=  1000.3    Downstream=  1000.3

Upstream     num=       2

Width   Elev    Width   Elev

4   758.7       4   768.5

Downstream     num=       2

Width   Elev    Width   Elev

4   758.7       4   768.5

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Yarnell                KVal =    1.25

Selected Low Flow Methods = Yarnell

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =.9245003

Max Low Cord                =   760.5

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 61

INPUT

Description: 10.249

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

555     777     613   776.3     650     773     669   768.5     705     768

750     768   888.4     768   888.5     771     890     771   890.1   765.6

940     765   940.1   760.7     950   759.2     968   758.7     997   759.8

1030   759.6  1060.5   762.7  1060.6     765    1114   765.7    1133   767.5

1170   773.8    1250   776.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

555     .06   940.1     .03  1060.5     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

940.1  1060.5               32      32      32             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

555   940.1     768  1060.5    1250     769

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 60

INPUT

Description: 10.246

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1431.8   776.5    1485   777.1  1553.8   777.4    1613   776.8  1659.8   774.7

1697.4   769.7  1720.6   766.7  1742.6     767    1815     767  1815.1     767

1830   767.7    1880   768.2    1890   768.2  1890.1   764.1  1890.2   760.2

1950   760.2    2000   758.2    2050   758.1    2090   758.1    2110   764.1

2115   768.3    2165   768.3  2165.1   768.3  2165.2   768.3  2165.3   768.3

2190.3   776.2  2230.3   780.7  2261.5   787.5  2300.3   795.9  2343.5   801.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1431.8     .06    1890     .03    2115     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1890    2115              220     225     230             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 59

INPUT

Description: 10.158

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

555     777     613   776.7     660   774.5     670     770     720     767

760     767   767.1     778     860     778   860.1     768     894     768

894.1     770   895.5     770   896.5     760     950     760    1000     758

1060   755.6    1068   768.5    1095     770    1110     775    1130     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

555     .06   895.5     .03    1068     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

895.5    1068               50     110      80             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 58

INPUT

Description: 10.113

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

782     779   782.1   766.1     802   766.1     803   768.2     834   768.2

834.1   765.6     843   765.6   843.1   763.8   843.2   755.5    1025     755

1025.1   763.8    1040   768.5    1177     775

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

782     .08     843     .03  1025.1     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

843  1025.1                5       5       5             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 57

INPUT

Description: 10.112

This is a REPEATED section.

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

782     779   782.1   766.1     802   766.1     803   768.2     834   768.2

834.1   765.6     843   765.6   843.1   763.8     956   763.8   956.1   765.3

974   765.3   974.1   763.8    1026   763.8    1040   768.5    1177     775

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

782      .1     843     .05    1026     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

843    1026                2       2       2             .3       .5

INLINE WEIR            RIVER: RIVER-1

REACH: Reach-1            RS: 56.5

INPUT

Description:

Distance from Upstream XS =       0

Deck/Roadway Width        =       2

Weir Coefficient          =       3

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =       15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

782     779   782.1   766.1     802   766.1     803   768.2     834   768.2

834.1   765.6     843   765.6   843.1   763.8     956   763.8   956.1   765.3

974   765.3   974.1   763.8    1026   763.8    1040   768.5    1177     775

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   763.8

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 56

INPUT

Description: 10.112

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

782     779   782.1   766.1     802   766.1     803   768.2     834   768.2

834.1   765.6     843   765.6   843.1   763.8     956   763.8   956.1   765.3

974   765.3   974.1   763.8    1026   763.8    1040   768.5    1177     775

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

782      .1     843     .05    1026     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

843    1026                5       5       5             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 55

INPUT

Description: 10.111

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

782     779   782.1   766.1     802   766.1     804     763     855   749.8

1009   749.8    1024   754.2    1026   763.8    1040   768.5    1177     775

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

782      .1     855     .05    1024     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

855    1024               57      57      57             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 54

INPUT

Description: 10.11

Station Elevation Data    num=      24

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

480     775     578     770     731   766.7     732     775     813     775

814   756.2     825     755     835   750.8     853   750.2     872   751.2

880   754.7     887   750.8     894   749.3     915   750.8     932     760

941     762     970     755     982   750.9    1000     750    1020   750.8

1045     760    1052     765    1093     770    1108     775

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

480     .07     835     .05    1020     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

835    1020             1150    1075    1035             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 53

INPUT

Description: 9.958

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

878     750     921     745     948     740     967   737.4     973   732.9

1000   732.7    1028   732.9    1035   737.3    1085     738    1097     740

1157     745    1211     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

878     .09     967    .035    1035     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

967    1035              230     225     212             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 52

INPUT

Description: 9.925

Station Elevation Data    num=       8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

838     750     845   746.7     885   746.7     962   730.7    1038   730.6

1063   738.9    1160     745    1220     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

838     .07     885    .035    1063     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

885    1063              620     560     500             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 51

INPUT

Description: 9.847

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

556.4   772.9   599.6   769.6   624.4   764.3   651.6   762.8   684.4   755.3

720.4   753.6   746.4   743.1     785     740   785.1     740   785.2     740

908   734.3     948   734.5     966   730.1     972   726.5    1000   726.3

1029   726.8    1034   730.1    1094   733.5  1094.1   733.5  1094.2   733.5

1102.8   741.7  1162.8   743.7  1255.2   745.8  1348.8   745.8    1438     747

1540   749.7  1570.8   752.1  1626.8   755.9  1668.8   756.5  1669.3   756.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

556.4     .07     948    .035    1029     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

948    1029               50      50      50             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 50

INPUT

Description: 9.84

This is a REPEATED section.

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

716   753.7     749     743     805   742.2     855   740.1     910   734.7

950   734.8   962.4     733   962.5   732.9     965   732.7     967   728.2

973   726.7    1000   726.1    1028   726.8  1034.5   728.2    1035   730.2

1037.5   730.4  1037.6   730.4    1095   733.7    1102     740    1104   741.6

1162   743.6    1257   745.6

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

716     .07   962.5    .035  1037.5     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

962.5  1037.5               21      21      21             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

716   962.5  740.05  1037.5    1257     740

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 49.5

INPUT

Description: Bridge #5

Distance from Upstream XS =       0

Deck/Roadway Width        =      21

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      15

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

716   753.7       0     749     743       0     805   742.2       0

855   740.1       0     910   740.1       0     950  740.05       0

962.4  740.05       0   962.5  740.05   736.4  1037.5     740   736.4

1037.6     740       0    1095   733.7       0    1102     740       0

1104   741.6       0    1162   743.6       0    1257   745.6       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

716   753.7     749     743     805   742.2     855   740.1     910   734.7

950   734.8   962.4     733   962.5   732.9     965   732.7     967   728.2

973   726.7    1000   726.1    1028   726.8  1034.5   728.2    1035   730.2

1037.5   730.4  1037.6   730.4    1095   733.7    1102     740    1104   741.6

1162   743.6    1257   745.6

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

716     .07   962.5    .035  1037.5     .06

Bank Sta: Left   Right    Coeff Contr.   Expan.

962.5  1037.5             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

716   962.5  740.05  1037.5    1257     740

Downstream  Deck/Roadway Coordinates

num=      15

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

716   753.7       0     749     743       0     805   742.2       0

855   740.1       0     910   740.1       0     950  740.05       0

962.4  740.05       0   962.5  740.05   736.4  1037.5     740   736.4

1037.6     740       0    1095   733.7       0    1102     740       0

1104   741.6       0    1162   743.6       0    1257   745.6       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

716   753.5     749   742.8     805     742     855   739.9     910   734.5

950   734.6   962.4   732.8   962.5   732.7     965   732.5     967     728

973   726.5    1000   725.9    1028   726.6  1034.5     728    1035     730

1037.5   730.2  1037.6   730.2    1095   733.5    1102   739.8    1104   741.4

1162   743.4    1257   745.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

716     .08   962.5    .035  1037.5     .06

Bank Sta: Left   Right    Coeff Contr.   Expan.

962.5  1037.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

716   962.5  740.05  1037.5    1257     740

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =     740

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =    1.14

Selected Low Flow Methods = Highest Energy Answer

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =.9365858

Max Low Cord                =   736.4

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 49

INPUT

Description: 9.836

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

716   753.5     749   742.8     805     742     855   739.9     910   734.5

950   734.6   962.4   732.8   962.5   732.7     965   732.5     967     728

973   726.5    1000   725.9    1028   726.6  1034.5     728    1035     730

1037.5   730.2  1037.6   730.2    1095   733.5    1102   739.8    1104   741.4

1162   743.4    1257   745.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

716     .08   962.5    .035  1037.5     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

962.5  1037.5               50      50      50             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

716   962.5  740.05  1037.5    1257     740

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 48

INPUT

Description: 9.827

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

590     750     650     745     720     740     825     735     847   733.7

960     735     968   730.5     973   725.9    1000   725.6    1030     726

1035     731    1060     735    1070     740    1085     745    1100     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

590     .08     960    .035    1060    .035

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

960    1060              350     720     670             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 47

INPUT

Description: 9.685

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

795     750     900     745     948     740     958     735     970     730

975     723    1000   722.5    1020     723    1037     730    1070     735

1152     740    1170     745    1188     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

795    .055     970    .033    1020     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

970    1020              990     950    1000             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 46

INPUT

Description: 9.495

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

255     735     290     730   317.2   727.4     389   725.7     390     735

460     735     461   728.3     478   729.1     550     730     600   731.8

640     730     720   727.5     750   725.1     860   723.5     900   723.1

963   723.9     964   721.6     967   718.8    1000   719.3    1034   719.6

1036   721.6    1040   724.3    1065     730    1080     731    1098     730

1124.4   726.4  1198.4   727.6  1278.8   727.6  1367.2   726.4    1476   726.1

1784.4   726.1  1859.2   726.4  1923.2   726.1    2157   726.1    2195     735

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

255     .06     860    .033    1040     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

860    1040             1635    1760    1950             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 45

INPUT

Description: 9.132

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1495     735    1525     730    1535     725    1620     723    1890     723

1935     722    1969   715.3    1974  713.55    2000  713.55    2029  713.55

2031   715.3    2079   737.9

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1495     .06    1969    .033    2031     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1969    2031              120      40      40             .7       .9

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 44

INPUT

Description: 9.126

This is a REPEATED section.

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1500  727.56    1700  730.06  1904.9  730.56    1905  730.56    1950  717.56

1965  715.26    2000   713.5    2042  714.06    2095  735.06  2095.1  735.06

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1500     .04    1950    .033    2042     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1950    2042             43.5    43.5    43.5             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

1500    1950     731    2042  2095.1     739

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 43.5

INPUT

Description: Bridge #4

Distance from Upstream XS =       0

Deck/Roadway Width        =    43.5

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=       6

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

1500     731       0    1700     731       0  1904.9   734.5       0

1905   734.5   730.5    2095     739     735  2095.1     739       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1500  727.56    1700  730.06  1904.9  730.56    1905  730.56    1950  717.56

1965  715.26    2000   713.5    2042  714.06    2095  735.06  2095.1  735.06

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1500     .04    1950    .033    2042     .04

Bank Sta: Left   Right    Coeff Contr.   Expan.

1950    2042             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

1500    1950     731    2042  2095.1     739

Downstream  Deck/Roadway Coordinates

num=       6

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

1500     731       0    1700     731       0  1904.9   734.5       0

1905   734.5   730.5    2095     739     735  2095.1     739       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1500   727.5    1700     730  1904.9   730.5    1905   730.5    1950   717.5

1965   715.2    2000  713.44    2042     714    2095     735  2095.1     735

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1500     .08    1950    .033    2042    .055

Bank Sta: Left   Right    Coeff Contr.   Expan.

1950    2042             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

1500    1950     731    2042  2095.1     735

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =     731

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Piers =  1

Pier Data

Pier Station     Upstream=    1996    Downstream=    1996

Upstream     num=       2

Width   Elev    Width   Elev

4   713.5       4     735

Downstream     num=       2

Width   Elev    Width   Elev

4  713.44       4     735

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Yarnell                KVal =    1.25

Selected Low Flow Methods = Yarnell

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =.9284767

Max Low Cord                =     735

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 43

INPUT

Description: 9.117

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1500   727.5    1700     730  1904.9   730.5    1905   730.5    1950   717.5

1965   715.2    2000  713.44    2042     714    2095     735  2095.1     735

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1500     .08    1950    .033    2042    .055

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1950    2042               30      30      30             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

1500    1950     731    2042  2095.1     735

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 42

INPUT

Description: 9.112

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1178.4     735  1209.6     735    1250     728    1800     725    1801     725

1802     725    1803     725    1956     721  1956.4   715.1    1960   713.4

2000   713.4    2040   713.4    2044   715.1    2055   720.6    2090     725

2100     730  2211.8   741.1  2252.2   741.4  2286.2   749.4  2328.2   757.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1178.4     .08    1956    .033    2044     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1956    2044             1375    1485    1540             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 41

INPUT

Description: 8.807

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

698   750.4   739.6   736.4     776   735.5   804.4   735.5   826.4   736.4

882.8   728.4   891.8   722.9   903.6   720.1   903.7   720.1   903.8   720.1

907   715.8     957   715.2     962   711.8     965   709.8    1000   706.3

1035   708.8    1036   711.9    1040   715.4    1090   713.3  1090.1   713.3

1104.2   720.9  1136.2   723.9  1183.4     729  1213.4   747.1  1241.4   749.2

1267.4   749.2  1279.8   752.8  1302.2   755.1  1337.8   756.3  1337.9   756.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

698     .08     957     .03    1040     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

957    1040             1430    1500    1495             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 40

INPUT

Description: 8.513

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

349.6   727.5   371.2   729.9   398.4   730.2   473.6   724.5     514   723.6

580.4     723   654.4   722.7   661.6   722.5   756.4   722.4   871.6   722.4

932   722.3     938     713     970   710.6    1000   709.7    1030   710.8

1071   711.6    1075   714.6    1096   734.6  1096.1   734.6    1110   736.8

1111.2   737.3  1130.4   737.3  1166.8   746.8  1232.4   755.4  1262.8   759.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

349.6    .035     932     .03    1075     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

932    1075               45      45      45             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 39

INPUT

Description: 8.5

Station Elevation Data    num=      18

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

349.6   727.5   371.2   729.9   398.4   730.2   473.6   724.5     510   723.6

580.4     723   654.4   722.7   661.6   722.5   756.4   722.4   871.6   722.4

925   714.7     926   713.4     970   710.4    1000   709.5    1030   710.6

1071   711.4    1075   714.4    1096   734.6

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

349.6    .035   871.6     .03    1075     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

871.6    1075                5       5       5             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 38

INPUT

Description: 8.499

This is a REPEATED section.

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

923.9     735     926   722.3   939.3   722.3   939.4   719.4     944   719.4

944.1   715.4    1052   715.4  1052.1   717.7    1068   717.7  1068.1   719.5

1077.8   720.8  1077.9   733.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

923.9     .04     944     .03  1077.8     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

944  1077.8                2       2       2             .1       .3

INLINE WEIR            RIVER: RIVER-1

REACH: Reach-1            RS: 37.5

INPUT

Description:

Distance from Upstream XS =       0

Deck/Roadway Width        =       2

Weir Coefficient          =     3.3

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =       12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

871.6   722.4     924   722.3   939.3   722.3   939.4   719.4     944   719.4

944.1   715.4    1052   715.4  1052.1   717.7    1068   717.7  1068.1   719.5

1077.8   720.6    1096   722.4

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   715.4

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 37

INPUT

Description: 8.498

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

923.9     735     926   722.3   939.3   722.3   939.4   719.4     944   719.4

944.1   715.4    1052   715.4  1052.1   717.7    1068   717.7  1068.1   719.5

1077.8   720.8  1077.9   733.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

923.9     .04     944     .03  1077.8     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

944  1077.8                5       5       5             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 36

INPUT

Description: 8.498

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

923     735     924   722.3   939.3   722.3   939.4   719.4     944   719.4

944.1   715.4   944.2     708    1053     708  1077.8   720.6  1077.9   733.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

923     .04     944    .032  1077.8     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

944  1077.8               50      50      50             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 35

INPUT

Description: 8.494

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

401.8   731.4   449.2   731.4     510   728.7   557.2   725.1   667.2   723.9

684   721.5   711.2   722.1   814.4   722.4   906.8   723.9   906.9   723.9

920     723     950   724.1     952   709.6   952.1   708.9    1000   706.5

1048   708.7    1090   709.6  1090.1   727.6    1100   730.3    1101   730.3

1108.5     732  1132.5   739.4  1182.5   743.5  1229.3   750.7  1283.3   756.9

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

401.8     .04     950    .032  1090.1     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

950  1090.1               40      40      40             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 34

INPUT

Description: 8.486

This is a REPEATED section.

Station Elevation Data    num=      44

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

875   723.5     928   727.6     930   725.1     932   720.1     939   715.1

944   710.1   956.7   710.6   956.8   710.6   962.1   707.7   962.2   707.6

963   707.6     964   707.6     965   707.5     966   707.4     967   707.3

968   707.3     969  707.25     970  707.25     975   706.9     980   706.5

990  706.35    1000  706.35    1010  706.35    1020  706.35    1025   707.2

1030   708.1    1031   708.4    1032   708.6    1033   708.8    1034   708.9

1035   709.1    1036   709.4    1037     710  1037.8   710.1  1037.9   710.1

1039.5   715.1    1040   720.1  1041.5   725.1    1044   726.4  1044.1   726.5

1049   727.5    1078   730.1    1110   732.1    1118   734.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

875     .04   962.2    .032  1037.8     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

962.2  1037.8               43      43      43             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

875   962.2   723.5  1037.8    1118   731.7

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 33.5

INPUT

Description: Bridge #2

Distance from Upstream XS =       0

Deck/Roadway Width        =      43

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      33

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

875   723.5       0     928   727.8       0     944   728.4       0

956.7     727       0   956.8   729.1       0   962.1   729.1       0

962.2   729.1     714     963   729.1   716.5     964   729.2     718

965   729.2   719.4     966   729.3   720.1     967   729.3   720.6

968   729.3   721.2     969   729.4   721.8     970   729.4     722

975   729.7   723.1     980     730     724     990   730.4   725.1

1000   730.7   725.8    1010     731   725.5    1020   731.2     725

1030   731.4   723.7    1031   731.4   723.2    1032   731.5     723

1033   731.5   722.5    1034   731.6   721.9    1035   731.6     721

1036   731.7   719.9    1037   731.7     716  1037.8   731.7     714

1037.9   731.7       0    1044   732.2       0  1044.1     730       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      44

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

875   723.5     928   727.6     930   725.1     932   720.1     939   715.1

944   710.1   956.7   710.6   956.8   710.6   962.1   707.7   962.2   707.6

963   707.6     964   707.6     965   707.5     966   707.4     967   707.3

968   707.3     969  707.25     970  707.25     975   706.9     980   706.5

990  706.35    1000  706.35    1010  706.35    1020  706.35    1025   707.2

1030   708.1    1031   708.4    1032   708.6    1033   708.8    1034   708.9

1035   709.1    1036   709.4    1037     710  1037.8   710.1  1037.9   710.1

1039.5   715.1    1040   720.1  1041.5   725.1    1044   726.4  1044.1   726.5

1049   727.5    1078   730.1    1110   732.1    1118   734.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

875     .04   962.2    .032  1037.8     .04

Bank Sta: Left   Right    Coeff Contr.   Expan.

962.2  1037.8             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

875   962.2   723.5  1037.8    1118   731.7

Downstream  Deck/Roadway Coordinates

num=      33

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

875   723.5       0     928   727.8       0     944   728.4       0

956.7     727       0   956.8   729.1       0   962.1   729.1       0

962.2   729.1     714     963   729.1   716.5     964   729.2     718

965   729.2   719.4     966   729.3   720.1     967   729.3   720.6

968   729.3   721.2     969   729.4   721.8     970   729.4     722

975   729.7   723.1     980     730     724     990   730.4   725.1

1000   730.7   725.8    1010     731   725.5    1020   731.2     725

1030   731.4   723.7    1031   731.4   723.2    1032   731.5     723

1033   731.5   722.5    1034   731.6   721.9    1035   731.6     721

1036   731.7   719.9    1037   731.7     716  1037.8   731.7     714

1037.9   731.7       0    1044   732.2       0  1044.1     730       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      44

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

875   723.4     928   727.5     930     725     932     720     939     715

944     710   956.7   710.5   956.8   710.5   962.1   707.6   962.2   707.5

963   707.5     964   707.5     965   707.4     966   707.3     967   707.2

968   707.2     969  707.15     970  707.15     975   706.8     980   706.4

990  706.25    1000  706.25    1010  706.25    1020  706.25    1025   707.1

1030     708    1031   708.3    1032   708.5    1033   708.7    1034   708.8

1035     709    1036   709.3    1037   709.9  1037.8     710  1037.9     710

1039.5     715    1040     720  1041.5     725    1044   726.3  1044.1   726.4

1049   727.4    1078     730    1110     732    1118     734

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

875     .04   962.2    .032  1037.8     .04

Bank Sta: Left   Right    Coeff Contr.   Expan.

962.2  1037.8             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

875   962.2   723.4  1037.8    1118   725.8

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   723.5

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =   1.154

Selected Low Flow Methods = Highest Energy Answer

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =.9308873

Max Low Cord                =   725.8

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 33

INPUT

Description: 8.478

Station Elevation Data    num=      44

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

875   723.4     928   727.5     930     725     932     720     939     715

944     710   956.7   710.5   956.8   710.5   962.1   707.6   962.2   707.5

963   707.5     964   707.5     965   707.4     966   707.3     967   707.2

968   707.2     969  707.15     970  707.15     975   706.8     980   706.4

990  706.25    1000  706.25    1010  706.25    1020  706.25    1025   707.1

1030     708    1031   708.3    1032   708.5    1033   708.7    1034   708.8

1035     709    1036   709.3    1037   709.9  1037.8     710  1037.9     710

1039.5     715    1040     720  1041.5     725    1044   726.3  1044.1   726.4

1049   727.4    1078     730    1110     732    1118     734

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

875     .04   962.2    .032  1037.8     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

962.2  1037.8               30      30      30             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

875   962.2   723.4  1037.8    1118   725.8

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 32

INPUT

Description: 8.472

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

494.4   735.2   524.4   735.2   585.2   731.4   674.4   726.7     736     723

804   722.4     854   722.7     886   723.3   886.1   723.3   886.2   723.3

890   722.8     926   722.9     954   709.1     956   708.4    1000   706.1

1043   707.4    1046   709.1    1054   711.6  1054.1   731.3    1090   728.6

1111.4   729.3  1157.8     729    1205   734.9  1284.6   737.6  1312.2   751.6

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

494.4     .04     926    .032  1054.1     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

926  1054.1             1880    1898    1840             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 31

INPUT

Description: 8.136

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

425.2     740   478.8   721.5   521.6   716.8     608   715.6   628.4   716.8

650.8   716.8   717.2   714.4     776   714.4   846.4   712.9   871.6   713.8

880   714.1     935   714.3     963     708     967   706.7    1000   703.9

1033   706.5    1037     708    1060   724.4  1060.1   724.4  1060.2   724.4

1087.2   722.1  1102.4   722.1  1169.2   726.9  1228.4   731.4  1304.8   737.6

1344.8   740.9    1396     745  1446.4   751.3  1479.2   757.8  1479.3   757.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

425.2      .1     935    .032    1060      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

935    1060             2050    2277    2050             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 30

INPUT

Description: 7.733

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

372.4   734.9   406.4   716.7   427.6   713.5   448.8   715.2   533.2   714.9

615.2     714   647.6   713.2   705.2   713.2   791.2   712.3     880   711.7

920   706.9     949   709.3     960   707.8     962   703.7     964   702.2

1000   700.2    1035   700.9    1038   703.7    1067   719.7    1110   719.1

1135.2   720.9  1158.4   731.9  1179.2   743.8  1200.8   749.7  1200.9   749.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

372.4     .08     960    .032    1067     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

960    1067             1125    1135    1125             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 29

INPUT

Description: 7.533

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

780     725     795     720     798     715     850     710     863   705.9

958     705     962   699.5    1000   698.8    1043   699.5    1050     705

1055     710    1069   712.3    1585     715

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

780     .07     958    .032    1055     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

958    1055             1555    1920    1500             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 28

INPUT

Description: 7.186

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

946.8   735.6   980.8     718  1017.2   711.5  1062.4   711.5    1092   711.5

1120   706.7  1167.2   706.4  1206.4   707.9  1222.8   710.3  1278.8   706.7

1340.8   708.2  1400.8   706.7    1532   707.3  1628.4   708.5  1777.2   708.5

1822   707.3  1885.6   704.3  1905.2   704.3  1905.3   704.3  1905.4   704.3

1930   704.9    1966     705    1970   701.9    1973   700.4    2000   697.4

2027   700.9    2030   701.9    2037   706.2    2099   708.3    2139   718.4

2145.4   720.1  2186.6     721  2226.2   715.3  2275.4     718    2323     725

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

946.8     .05    1966    .032    2037     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1966    2037             1580    1235    1175             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 27

INPUT

Description: 6.975

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

644     730   644.5     725     645   706.8     778   708.8     821   707.8

887   704.6     908   704.6     930   705.2     967   705.2     970   702.2

973   700.8     980     698    1000     697    1020     698    1028   701.2

1030     705    1050     710    1060     715    1095     720    1190     725

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

644     .04     967    .032    1030     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

967    1030              530     465     300             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 26

INPUT

Description: 6.889

Station Elevation Data    num=      22

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

595     720     685     715     797     715     830     720     870     720

895     715     905     710     930     705     952   704.6     964     705

983   705.2     985   702.1     987   700.9    1000     698    1012     701

1015   702.4    1017   706.4    1128     705    1235     710    1245     715

1280     720    1350     725

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

595     .07     983    .032    1017     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

983    1017              525     500     500             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 25

INPUT

Description: 6.823

Station Elevation Data    num=      18

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

685     730     780     725     805     720     860     715     905     710

934   701.3     946   701.1     950   697.2    1000     697    1049   697.2

1054   701.1    1095     705    1105     710  1131.9   715.8  1186.3   715.8

1216.3   727.7  1236.3   735.1    1255   741.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

685     .07     946    .032    1054     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

946    1054               45      45      45             .4       .7

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 24

INPUT

Description: 6.814

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

865   713.9     876     709   876.5   708.2     883     704     890   703.3

896.5   698.3     908   698.3     909     698    1085     698    1095  705.79

1110     710    1112   710.2    1133   710.5    1136   712.7    1140   712.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

865     .06     890     .03    1095     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

890    1095                4       4       4             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 23

INPUT

Description: 6.813

This is a REPEATED section.

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

865   713.9     876     709   876.5   708.2     888   708.2   890.8   705.6

922.9   705.6     923  702.69  1077.8  702.69  1077.9  705.79    1095  705.79

1110     710    1112   710.2    1133   710.5    1136   712.7    1140   712.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

865     .06   922.9     .03  1077.9     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

922.9  1077.9                2       2       2             .1       .3

INLINE WEIR            RIVER: RIVER-1

REACH: Reach-1            RS: 22.5

INPUT

Description:

Distance from Upstream XS =       0

Deck/Roadway Width        =       2

Weir Coefficient          =    3.32

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =       15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

865   713.9     876     709   876.5   708.2     888   708.2   890.8   705.6

922.9   705.6     923  702.69  1077.8  702.69  1077.9  705.79    1095  705.79

1110     710    1112   710.2    1133   710.5    1136   712.7    1140   712.8

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =  702.69

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 22

INPUT

Description: 6.812

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

865   713.9     876     709   876.5   708.2     888   708.2   890.8   705.6

922.9   705.6     923  702.69  1077.8  702.69  1077.9  705.79    1095  705.79

1110     710    1112   710.2    1133   710.5    1136   712.7    1140   712.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

865     .06   922.9     .03  1077.9     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

922.9  1077.9                5       5       5             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 21

INPUT

Description: 6.811

Station Elevation Data    num=      32

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

865   713.9     875     709   876.5   708.2     883     704     890   703.3

900   701.9     910     702   915.5   700.9   922.9     702     923   705.6

927.5   705.6   927.6   692.3     940     690     955   691.8     962     692

973   691.5     980   692.3    1000   692.7  1000.1   692.7  1000.2   692.7

1000.3   692.7    1050     693    1076   693.5  1077.8     694  1077.9     694

1092   702.4    1095   705.8    1110     710    1112   710.2    1133   710.5

1136   712.7    1140   712.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

865     .09   927.5     .03  1077.8     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

927.5  1077.8              140     120     110             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 20

INPUT

Description: 6.785

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

174.8   726.4   225.6   721.4   283.2   722.2   333.6   722.2   386.4   717.2

480.8   714.5   533.2   713.9   574.4   710.9     628   711.2   716.8   708.9

776.4   710.1   818.4   708.9   818.5   708.9   818.6   708.9   818.7   706.9

880   714.2     923   712.9     938   694.7     945   692.7     970   693.7

1000   692.2    1030   692.7    1062   693.7  1062.1   694.7    1064   713.6

1094   713.7  1094.1   713.7  1094.2   713.7  1094.3   713.7  1094.4   713.7

1147.6   714.2    1182   719.3    1212   727.6    1266   738.3  1299.2   744.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

174.8     .07     938     .03  1062.1     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

938  1062.1              100      74      35             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 19

INPUT

Description: 6.766

Station Elevation Data    num=       8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

943   708.4   943.1   691.9     975   691.9     986   691.9  997.75   691.9

1002.45   691.9  1056.9   691.9    1057   708.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

943     .05   943.1     .03  1056.9     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

943.1  1056.9                5       5       5             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 18

INPUT

Description: 6.765

This is a REPEATED section.

Station Elevation Data    num=      11

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1880   712.4    1943   708.7  1943.1   695.1    1950   691.9    1986   691.9

1997.75   691.9  1997.8   708.7  2002.4   708.7 2002.45   691.9  2056.9   691.9

2057   708.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1880     .03  1943.1     .03  2056.9     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1943.1  2056.9               83      83      83             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 17

INPUT

Description: 6.749

Station Elevation Data    num=      11

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1880   712.1    1943   708.4  1943.1   694.8    1950   691.6    1986   691.6

1997.75   691.6  1997.8   708.4  2002.4   708.4 2002.45   691.6  2056.9   691.6

2057   708.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1880     .03  1943.1     .03  2056.9     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1943.1  2056.9                5       5       5             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 16

INPUT

Description: 6.748

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1880   712.1    1902   704.2    1928   697.5  1943.1   694.8    1950   691.6

1985   691.6  1997.7   691.6  2002.4   691.6  2056.9   691.6    2057     697

2090     712    2105   713.4    2122   714.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1880     .03  1943.1     .03  2056.9     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1943.1  2056.9               65      65      65             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 15

INPUT

Description: 6.736

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

950   725.2   995.6   723.4  1052.8   720.5  1115.2   715.4  1171.2   715.1

1223.2   710.3    1336   709.2  1364.8   709.2  1423.2     705  1530.8   704.4

1632.8   705.3    1696   710.9    1748   712.1  1812.4     713  1812.5     713

1852.1   712.7  1878.1   712.7  1900.5   704.7  1926.5   697.9  1926.6   697.9

1947   694.5    1950   691.3    2000   691.1    2048     691    2053   694.5

2083   711.5    2105   713.6  2105.1   713.6  2105.2   713.6  2105.3   713.6

2121.7   714.5  2141.3   723.1  2186.9   732.1  2214.9   733.8  2234.9   736.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

950     .07    1947     .03    2053     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1947    2053             2930    3051    3320             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 14

INPUT

Description: 6.258

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

580.4   724.9     646   722.5     736   720.5     754   718.1   802.8   698.2

832   694.3   874.4   693.1   874.5   693.1   874.6   693.1   874.7   693.1

905     691     945   690.7     963   687.7     968   686.1    1000   685.4

1034   686.4    1037   687.7    1073   695.8    1123   694.5  1123.1   694.5

1161.5   694.9  1218.3   695.2  1283.9   696.1  1358.3   699.9  1403.1   703.5

1474.3   706.2  1541.9     705  1666.7   707.4  1764.7   709.5  1803.1   706.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

580.4     .07     945     .03    1073    .055

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

945    1073              980     980     900             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 13

INPUT

Description: 6.11

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

580     710     645     705     933     700     955     695     968     690

969   686.9     970   685.3    1000   684.6    1034   685.6    1037   686.9

1073     695    1123   693.7    1320     694    1655     695    1711     700

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

580     .06     968     .03    1073     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

968    1073             2350    2420    2190             .4       .7

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 12

INPUT

Description: 5.748

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

104   715.1     172   709.2   241.6   704.1   355.2   703.5   408.4   704.4

518.8   704.7   615.6   705.6   718.4   707.1   804.8   709.5   873.6   707.4

959.6   701.2  1058.8   700.6  1226.8   701.8  1301.2   701.8  1396.8   697.9

1620.8   697.9  1848.4   697.9  1892.8   699.1  1902.4   699.1  1916.8     694

1939   690.2    1957   691.9  1957.1     686  1957.2     683    2000     683

2041     683    2043     686    2052   692.6    2090     691  2090.4     691

2131.2   690.5  2207.6     691  2280.4   695.2  2359.2   702.6  2469.2   710.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

104     .05    1957     .03    2052     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1957    2052             3120    3143    3300             .4       .7

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 11

INPUT

Description: 5.256

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

720     700     770     695     872     690    1300     687    1555     685

1580     682    1610     685    1800   685.5    1960     685    1961   689.7

1961.2   683.8  1961.3   680.8    2000   680.8    2041   680.8    2043   683.8

2052   690.4    2090   688.8    2112     685    2228     690    2280     700

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

720     .05    1961     .03    2052     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1961    2052              692    1936    1864             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 10

INPUT

Description: 4.953

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

344   698.7   393.2   694.5     561   692.1   691.2   687.1     794   685.6

882   686.2     900   688.8     944   688.2     960     683     965     682

1000   679.5    1035   681.6    1040     683    1045   687.3    1100   687.5

1144   686.5    1229   686.2    1440   686.8    1471     688    1516   698.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

344     .06     944     .03    1045     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

944    1045              956     870     787             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 9

INPUT

Description: 4.817

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

412     700     550     695     775     690     940     685     944   687.6

960   682.4     965   680.4    1000   678.9    1035     681    1057   685.5

1075   687.5    1105     685    1400     690    1455     695    1560     700

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

412     .05     944     .03    1057     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

944    1057              729    1130   12000             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 8

INPUT

Description: 4.64

Station Elevation Data    num=      17

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

530     700     610     695     750     690    1913     685    1944   687.1

1960   681.9    1965   679.9    2000   678.4    2035   680.5    2057     685

2075     687    2102     685    2115     683    2125     685    2165     690

2180     695    2225     700

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

530     .08    1944     .03    2057     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1944    2057             1214    1814    1060             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 7

INPUT

Description: 4.356

Station Elevation Data    num=      33

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

640     705     670     700     745     695   758.4   692.7   800.8   691.5

813.2   696.3   829.2   696.6   836.8   688.3   874.8   688.3   894.8   690.6

900     691     938   689.8     952   680.5     957   677.8    1000   677.4

1043   677.7    1048   680.5    1064   687.8    1094   686.9  1094.1   686.9

1105.9   688.3  1143.1   687.4  1209.5   685.3  1263.1   688.8  1336.3   688.3

1439.9   688.6  1551.5   688.8  1637.5   688.8  1703.1   690.9  1767.1     693

2120     694    2430     695    2735     700

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

640     .04     938     .03    1064     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

938    1064             1870    1815    1795             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 6

INPUT

Description: 4.072

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

880     700     900     696     940     695     960     690     970   689.2

980   677.2    1000   676.8    1020   677.2    1060     685    2440     690

2820     694    3085     695    3390     700

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

880     .08     970     .03    1060     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

970    1060             1600    2191    1450             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 5

INPUT

Description: 3.729

Station Elevation Data    num=      50

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

430   699.3     490   696.9     690     688     769   688.3     838   690.6

891.6     690   937.6   685.9  1039.6   685.3  1069.2   682.9  1149.6   682.9

1229.6   683.2  1268.8   684.7  1281.2   689.4    1308     685  1338.8   684.4

1350   682.5    1395   679.5    1455   679.4    1497     693    1585     691

1606   680.5  1640.4   679.9    1665     685    1698   680.2    1848   681.4

1862.4   685.3    1900   684.7    1920   686.2    1961   685.2    1969     679

1974   677.8    2000     676    2026   677.5    2031     679    2064   685.5

2097   683.9  2112.9   683.2    2257   683.5    2289   680.5    2314     682

2348.9   684.4  2453.3   685.9  2553.3   686.5  2636.5   686.2  2704.5   686.2

2803.7   690.3  2921.3   690.9  3081.3   691.8  3209.3   694.2  3329.7   695.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

430     .05    1961     .03    2064     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1961    2064             3115    3654    3511             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 4

INPUT

Description: 3.157

Station Elevation Data    num=      18

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

290     700     350     695     425     690     730     685     970     685

1200     686    1480     685    1952     680    1962   678.3    1967   676.3

2000   673.5    2035   676.7    2040   678.3    2055     680    2335     685

2365     690    2642     695    3150     700

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

290     .07    1952     .03    2055     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1952    2055            18480    1910    2000             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 3

INPUT

Description: 2.858

Station Elevation Data    num=      24

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

850     705     881   691.8     893   691.5     905   687.7   905.5   687.7

912   692.1     948     678     953     676    1000   673.2    1047   676.4

1052     678    1058   683.4    1090   681.7  1090.1   681.7  1090.2   681.7

1106.4   680.8  1154.4   682.3  1209.6   684.4  1282.4   686.2    1332   692.1

1390     695    1442     699    1451     700    1518     705

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

850     .08     948     .03    1052     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

948    1052             1431    1463    1405             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 2

INPUT

Description: 2.629

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

652     700     685     695     740     690     782     685     913     680

948   677.1     953   675.1    1000   673.1    1047   676.3    1052   677.9

1058     680    1210     685    1270     690    1290     695    1310     700

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

652     .08     948     .03    1052     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

948    1052             1105    1130    1225             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 1

INPUT

Description: 2.452

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

432     700     525     695   733.2   689.7     782   683.5   901.2     682

944   681.9     946   677.9     956   674.9    1000   674.5    1044   673.4

1054   677.9    1061     682    1545   684.9  1680.5     687  1745.3   684.4

1822.1   684.4  1872.1   685.6  1915.3   686.5  1957.7   692.1    2050     695

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

432      .1     944     .06    1061      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

944    1061                0       0       0             .1       .3

SUMMARY OF MANNING'S N VALUES

River:RIVER-1

Reach          River Sta.       n1        n2        n3

Reach-1              82                 .06      .037       .09

Reach-1              81                 .07      .037       .09

Reach-1              80                 .06      .037      .055

Reach-1              79                 .09      .037       .07

Reach-1              78                 .09      .037       .07

Reach-1              77.5         Bridge

Reach-1              77                 .09      .037       .07

Reach-1              76                 .09      .037       .07

Reach-1              75                 .09      .037       .09

Reach-1              74                 .08      .035       .09

Reach-1              73                 .08      .035       .09

Reach-1              72                 .08      .035       .09

Reach-1              71                 .07      .035       .07

Reach-1              70                 .07      .033       .07

Reach-1              69                 .07      .033       .09

Reach-1              68.5         Bridge

Reach-1              68                 .07      .033       .09

Reach-1              67                 .07      .033       .09

Reach-1              66                 .07       .03       .08

Reach-1              65                 .06       .03       .07

Reach-1              64                 .06       .03       .07

Reach-1              63                 .05       .03       .07

Reach-1              62                 .05       .03       .06

Reach-1              61.5         Bridge

Reach-1              61                 .06       .03       .06

Reach-1              60                 .06       .03       .06

Reach-1              59                 .06       .03       .06

Reach-1              58                 .08       .03       .07

Reach-1              57                  .1       .05       .09

Reach-1              56.5         Inline Weir

Reach-1              56                  .1       .05       .09

Reach-1              55                  .1       .05       .09

Reach-1              54                 .07       .05       .09

Reach-1              53                 .09      .035       .09

Reach-1              52                 .07      .035       .09

Reach-1              51                 .07      .035       .09

Reach-1              50                 .07      .035       .06

Reach-1              49.5         Bridge

Reach-1              49                 .08      .035       .06

Reach-1              48                 .08      .035      .035

Reach-1              47                .055      .033       .09

Reach-1              46                 .06      .033       .07

Reach-1              45                 .06      .033       .08

Reach-1              44                 .04      .033       .04

Reach-1              43.5         Bridge

Reach-1              43                 .08      .033      .055

Reach-1              42                 .08      .033       .07

Reach-1              41                 .08       .03       .07

Reach-1              40                .035       .03       .05

Reach-1              39                .035       .03       .05

Reach-1              38                 .04       .03       .05

Reach-1              37.5         Inline Weir

Reach-1              37                 .04       .03       .05

Reach-1              36                 .04      .032       .05

Reach-1              35                 .04      .032       .05

Reach-1              34                 .04      .032       .04

Reach-1              33.5         Bridge

Reach-1              33                 .04      .032       .04

Reach-1              32                 .04      .032       .04

Reach-1              31                  .1      .032        .1

Reach-1              30                 .08      .032       .05

Reach-1              29                 .07      .032       .06

Reach-1              28                 .05      .032       .06

Reach-1              27                 .04      .032       .06

Reach-1              26                 .07      .032       .06

Reach-1              25                 .07      .032       .06

Reach-1              24                 .06       .03       .04

Reach-1              23                 .06       .03       .04

Reach-1              22.5         Inline Weir

Reach-1              22                 .06       .03       .04

Reach-1              21                 .09       .03       .04

Reach-1              20                 .07       .03       .04

Reach-1              19                 .05       .03       .04

Reach-1              18                 .03       .03       .04

Reach-1              17                 .03       .03       .04

Reach-1              16                 .03       .03       .04

Reach-1              15                 .07       .03       .07

Reach-1              14                 .07       .03      .055

Reach-1              13                 .06       .03       .06

Reach-1              12                 .05       .03       .07

Reach-1              11                 .05       .03       .08

Reach-1              10                 .06       .03       .07

Reach-1              9                  .05       .03       .07

Reach-1              8                  .08       .03       .09

Reach-1              7                  .04       .03       .07

Reach-1              6                  .08       .03       .07

Reach-1              5                  .05       .03       .06

Reach-1              4                  .07       .03       .07

Reach-1              3                  .08       .03       .08

Reach-1              2                  .08       .03       .08

Reach-1              1                   .1       .06        .1

SUMMARY OF REACH LENGTHS

River: RIVER-1

Reach          River Sta.      Left     Channel    Right

Reach-1              82                2350      2445      2400

Reach-1              81                2450      2555      2500

Reach-1              80                1795      2200      2270

Reach-1              79                  40        40        40

Reach-1              78                22.5      22.5      22.5

Reach-1              77.5         Bridge

Reach-1              77                  30        30        30

Reach-1              76                1000       955       900

Reach-1              75                 880       930       970

Reach-1              74                 750       880       855

Reach-1              73                 500       540       480

Reach-1              72                 570       565       470

Reach-1              71                 460       340       225

Reach-1              70                  40        40        40

Reach-1              69                  24        24        24

Reach-1              68.5         Bridge

Reach-1              68                  55        55        55

Reach-1              67                 360       830       450

Reach-1              66                 510       915       825

Reach-1              65                 565       625       690

Reach-1              64                1100      1120      1025

Reach-1              63                  40        40        40

Reach-1              62                  20        20        20

Reach-1              61.5         Bridge

Reach-1              61                  32        32        32

Reach-1              60                 220       225       230

Reach-1              59                  50       110        80

Reach-1              58                   5         5         5

Reach-1              57                   2         2         2

Reach-1              56.5         Inline Weir

Reach-1              56                   5         5         5

Reach-1              55                  57        57        57

Reach-1              54                1150      1075      1035

Reach-1              53                 230       225       212

Reach-1              52                 620       560       500

Reach-1              51                  50        50        50

Reach-1              50                  21        21        21

Reach-1              49.5         Bridge

Reach-1              49                  50        50        50

Reach-1              48                 350       720       670

Reach-1              47                 990       950      1000

Reach-1              46                1635      1760      1950

Reach-1              45                 120        40        40

Reach-1              44                43.5      43.5      43.5

Reach-1              43.5         Bridge

Reach-1              43                  30        30        30

Reach-1              42                1375      1485      1540

Reach-1              41                1430      1500      1495

Reach-1              40                  45        45        45

Reach-1              39                   5         5         5

Reach-1              38                   2         2         2

Reach-1              37.5         Inline Weir

Reach-1              37                   5         5         5

Reach-1              36                  50        50        50

Reach-1              35                  40        40        40

Reach-1              34                  43        43        43

Reach-1              33.5         Bridge

Reach-1              33                  30        30        30

Reach-1              32                1880      1898      1840

Reach-1              31                2050      2277      2050

Reach-1              30                1125      1135      1125

Reach-1              29                1555      1920      1500

Reach-1              28                1580      1235      1175

Reach-1              27                 530       465       300

Reach-1              26                 525       500       500

Reach-1              25                  45        45        45

Reach-1              24                   4         4         4

Reach-1              23                   2         2         2

Reach-1              22.5         Inline Weir

Reach-1              22                   5         5         5

Reach-1              21                 140       120       110

Reach-1              20                 100        74        35

Reach-1              19                   5         5         5

Reach-1              18                  83        83        83

Reach-1              17                   5         5         5

Reach-1              16                  65        65        65

Reach-1              15                2930      3051      3320

Reach-1              14                 980       980       900

Reach-1              13                2350      2420      2190

Reach-1              12                3120      3143      3300

Reach-1              11                 692      1936      1864

Reach-1              10                 956       870       787

Reach-1              9                  729      1130     12000

Reach-1              8                 1214      1814      1060

Reach-1              7                 1870      1815      1795

Reach-1              6                 1600      2191      1450

Reach-1              5                 3115      3654      3511

Reach-1              4                18480      1910      2000

Reach-1              3                 1431      1463      1405

Reach-1              2                 1105      1130      1225

Reach-1              1                    0         0         0

SUMMARY OF CONTRACTION AND EXPANSION COEFFICIENTS

River: RIVER-1

Reach          River Sta.     Contr.    Expan.

Reach-1              82              .1        .3

Reach-1              81              .1        .3

Reach-1              80              .1        .3

Reach-1              79              .3        .5

Reach-1              78              .1        .3

Reach-1              77.5     Bridge

Reach-1              77              .3        .5

Reach-1              76              .2        .4

Reach-1              75              .2        .4

Reach-1              74              .2        .4

Reach-1              73              .4        .8

Reach-1              72              .4        .8

Reach-1              71              .5         1

Reach-1              70              .4        .8

Reach-1              69              .1        .3

Reach-1              68.5     Bridge

Reach-1              68              .4        .8

Reach-1              67              .3        .5

Reach-1              66              .3        .5

Reach-1              65              .1        .3

Reach-1              64              .1        .3

Reach-1              63              .3        .5

Reach-1              62              .1        .3

Reach-1              61.5     Bridge

Reach-1              61              .3        .5

Reach-1              60              .1        .3

Reach-1              59              .3        .5

Reach-1              58              .2        .4

Reach-1              57              .3        .5

Reach-1              56.5     Inline Weir

Reach-1              56              .3        .5

Reach-1              55              .3        .5

Reach-1              54              .2        .4

Reach-1              53              .1        .3

Reach-1              52              .3        .5

Reach-1              51              .3        .5

Reach-1              50              .1        .3

Reach-1              49.5     Bridge

Reach-1              49              .3        .5

Reach-1              48              .1        .3

Reach-1              47              .2        .4

Reach-1              46              .2        .4

Reach-1              45              .7        .9

Reach-1              44              .1        .3

Reach-1              43.5     Bridge

Reach-1              43              .3        .5

Reach-1              42              .3        .5

Reach-1              41              .3        .5

Reach-1              40              .3        .5

Reach-1              39              .3        .5

Reach-1              38              .1        .3

Reach-1              37.5     Inline Weir

Reach-1              37              .1        .3

Reach-1              36              .1        .3

Reach-1              35              .3        .5

Reach-1              34              .3        .5

Reach-1              33.5     Bridge

Reach-1              33              .3        .5

Reach-1              32              .3        .5

Reach-1              31              .2        .4

Reach-1              30              .3        .5

Reach-1              29              .3        .5

Reach-1              28              .3        .5

Reach-1              27              .2        .4

Reach-1              26              .2        .4

Reach-1              25              .4        .7

Reach-1              24              .1        .3

Reach-1              23              .1        .3

Reach-1              22.5     Inline Weir

Reach-1              22              .1        .3

Reach-1              21              .1        .3

Reach-1              20              .3        .5

Reach-1              19              .3        .5

Reach-1              18              .3        .5

Reach-1              17              .3        .5

Reach-1              16              .3        .5

Reach-1              15              .1        .3

Reach-1              14              .1        .3

Reach-1              13              .4        .7

Reach-1              12              .4        .7

Reach-1              11              .2        .4

Reach-1              10              .2        .4

Reach-1              9               .2        .4

Reach-1              8               .2        .4

Reach-1              7               .2        .4

Reach-1              6               .2        .4

Reach-1              5               .1        .3

Reach-1              4               .1        .3

Reach-1              3               .1        .3

Reach-1              2               .1        .3

Reach-1              1               .1        .3