CONTOOCOOK RIVER MULTI

262910 PETERBORO NH

HEC-RAS September 1998 Version 2.2

U.S. Army Corp of Engineers

Hydrologic Engineering Center

609 Second Street, Suite D

Davis, California 95616-4687

(916) 756-1104

X     X  XXXXXX    XXXX        XXXX       XX      XXXX

X     X  X        X    X       X   X     X  X    X

X     X  X        X            X   X    X    X   X

XXXXXXX  XXXX     X       XXX  XXXX     XXXXXX    XXXX

X     X  X        X            X  X     X    X        X

X     X  X        X    X       X   X    X    X        X

X     X  XXXXXX    XXXX        X    X   X    X   XXXXX

PROJECT DATA

Project Title: Peterborough 2000 - Contoocook River

Project File : Con2000Final.prj

Run Date and Time: 1/8/00 6:42:12 PM

Project in English units

Project Description:

Contoocook River

PLAN DATA

Plan Title: Contoocook River 2000 Final Floodway

Plan File : D:\My Documents\H&H\Pboro\ConRAS\Final\Con2000Final.p03

Geometry Title: Contoocook River 2000 Final Geometry

Geometry File : D:\My Documents\H&H\Pboro\ConRAS\Final\Con2000Final.G01

Flow Title    : 1979 FIS Contoocook Floodway

Flow File     : D:\My Documents\H&H\Pboro\ConRAS\Final\Con2000Final.f03

Plan Summary Information:

Number of:  Cross Sections =   76    Mulitple Openings =    0

Culverts       =    0    Inline Weirs      =    3

Bridges        =    6

Computational Information

Water surface calculation tolerance =  0.01

Critical depth calculaton tolerance =  0.01

Maximum number of interations       =  20

Maximum difference tolerance        =  0.3

Flow tolerance factor               =  0.001

Computation Options

Critical depth computed only where necessary

Conveyance Calculation Method: Between every coordinate point (HEC2 Style)

Friction Slope Method:         Average Conveyance

Computational Flow Regime:     Subcritical Flow

Encroachment Data

Equal Conveyance = True

Left Offset      =        0

Right Offset     =        0

River = Contoocook River Reach = 001

RS      Profile           Method  Value1  Value2

12.704  Floodway               1    4910    5033

12.271  Floodway               1  4969.2  5040.4

11.809  Floodway               1    4966    5056

11.430  Floodway               1    4930  5036.5

11.422  Floodway               1  4955.5    5032

11.418  Floodway               1  4955.5    5032

11.412  Floodway               1    4934    5046

11.223  Floodway               1    4930    5100

11.040  Floodway               1  4644.3    5080

10.970  Floodway               1    4650    5800

10.866  Floodway               1    4920    6050

10.752  Floodway               1    4800    5320

10.681  Floodway               1    4800    5500

10.677  Floodway               1    4800    5500

10.673  Floodway               1    4872    5109

10.667  Floodway               1  4872.4    5400

10.567  Floodway               1    4510    5034

10.456  Floodway               1    4917    5190

10.366  Floodway               1    4850    5150

10.260  Floodway               1    4720    5081

10.253  Floodway               1  4738.6  5072.9

10.249  Floodway               1  4905.4  5096.8

10.246  Floodway               1  4885.6  5117.7

10.158  Floodway               1  4911.7  5106.3

10.113  Floodway               1  4908.9    5102

10.111  Floodway               1    4905    5096

10.110  Floodway               1    4875    5096

9.958   Floodway               1    4942    5042

9.925   Floodway               1    4900    5049

9.847   Floodway               1    4805    5200

9.840   Floodway               1    4945    5045

9.836   Floodway               1    4951    5043

9.827   Floodway               1    4800    5058

9.685   Floodway               1    4962    5094

9.495   Floodway               1    4620    5860

9.132   Floodway               1    4960    5051

9.126   Floodway               1    4928    5073

9.117   Floodway               1    4940    5080

9.112   Floodway               1    4945    5055

8.807   Floodway               1    4920    5070

8.513   Floodway               1    4930    5069

8.500   Floodway               1    4940    5060

8.498   Floodway               1    4944    5072

8.494   Floodway               1 4946.44 5053.56

8.486   Floodway               1    4960    5039

8.478   Floodway               1    4943    5057

8.472   Floodway               1    4947    5051

8.136   Floodway               1    4950    5053

7.733   Floodway               1    4900    5050

7.533   Floodway               1    4880    5060

7.186   Floodway               1    4584    5114

6.975   Floodway               1    4720    5250

6.889   Floodway               1    4868    5135

6.823   Floodway               1    4829    5007

6.814   Floodway               1    4883    5104

6.811   Floodway               1    4912    5090

6.785   Floodway               1    4901    5010

6.766   Floodway               1    4782    5011

6.765   Floodway               1    4814    5012

6.749   Floodway               1    4847    5007

6.748   Floodway               1    4832    5005

6.736   Floodway               1    4935    5066

6.258   Floodway               1    4835    5170

6.110   Floodway               1    4950    5300

5.748   Floodway               1    4915    5277

5.256   Floodway               1    4220    5100

4.953   Floodway               1    4730    5340

4.817   Floodway               1    4820    5180

4.640   Floodway               1    4260    5070

4.356   Floodway               1    4900    5500

4.072   Floodway               1    4917    5860

3.729   Floodway               1    4020    5460

3.157   Floodway               1    3680    5260

2.858   Floodway               1  4904.1    5120

2.629   Floodway               1    4865    5135

2.452   Floodway               1    4860    5580

FLOW DATA

Flow Title: 1979 FIS Contoocook Floodway

Flow File : D:\My Documents\H&H\Pboro\ConRAS\Final\Con2000Final.f03

Flow Data (cfs)

River           Reach           RS               100-year        Floodway

Contoocook River001             12.704               4300            4300

Contoocook River001             11.809               5700            5700

Contoocook River001             9.958                7150            7150

Contoocook River001             8.513                7500            7500

Contoocook River001             6.258                9150            9150

Boundary Conditions

River           Reach           Profile                       Upstream                 Downstream

Contoocook River001             100-year                                           Known WS = 689.39

Contoocook River001             Floodway                                           Known WS = 690.39

GEOMETRY DATA

Geometry Title: Contoocook River 2000 Final Geometry

Geometry File : D:\My Documents\H&H\Pboro\ConRAS\Final\Con2000Final.G01

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 12.704

INPUT

Description: South Townline

Station Elevation Data    num=      49

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4695.74     898 4700.29     896 4704.56     894  4709.1     892  4713.4     890

4716.31     888 4719.08     886 4722.05     884 4724.82     882 4727.75     880

4734.29     878 4756.82     876 4759.28     874 4763.97     872 4794.97     870

4802.91     868 4806.96     866 4812.83     864 4818.94     862 4838.37     860

4862.33     858 4873.47     856  4908.8     854 4969.42     852 4977.98  852.87

4982     848    4984   846.2    5000     846    5016   846.1    5018     848

5022.02  852.87 5031.29     854 5054.74     858 5069.96     860 5076.78     862

5083.53     864 5089.82     866 5102.78     870 5109.45     872 5115.58     874

5122.19     876 5128.78     878 5134.95     880 5142.09     882 5148.72     884

5155.83     886 5162.59     888 5169.66     890 5175.79     892

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4695.74     .06 4977.98    .037 5022.02     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4977.98 5022.02             2350    2445    2400             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 12.271

INPUT

Description: FEMA R

Station Elevation Data    num=      48

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4482.99     8704488.345     8684497.395     8664506.305     8644515.705     862

4518.845     8604524.865     8584547.425     8564556.345     8544560.275     852

4563.425     8504569.295     8484574.755     8464580.705     8444586.145     842

4591.895     8404594.725     8384598.445     8364601.845     8344605.435     832

4616.275     8324674.655     8324694.955     8304741.785     8284770.485     826

4820.465     8244836.565     8244871.005     8244966.815     822  4977.8  819.93

4977.8814.9364    5000   814.6  5022.2814.8018  5022.2  819.545062.545     824

5095.755     8285120.315     8325123.455     8345126.595     8365129.715     838

5132.745     8405135.605     8425147.485     8505149.335     8525151.235     854

5153.155     8565155.085     8585156.955     860

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4482.99     .07  4977.8    .037  5022.2     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4977.8  5022.2             2450    2555    2500             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 11.809

INPUT

Description:

Station Elevation Data    num=      44

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4408.495     8404412.805     8384417.125     8364421.435     8344426.045     832

4430.415     8304433.315     8284436.965     8264441.975     8244447.125     822

4449.995     8204496.575     8184552.525     8164622.065     8144708.285     812

4737.905     8104771.705     8084810.065     8064921.015     8064958.605     806

4961.195     8044964.715     8024967.765     8004971.375     7984974.765     796

4978.13  794.53    4987   794.3    5000   793.5 5021.88  793.745030.345     796

5041.715     7985053.235     8005057.775     8025061.965     8045072.635     806

5080.515     8085085.935     8105091.945     8145094.785     8165097.745     818

5100.525     8205112.405     8305123.565     8365130.795     840

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4408.495     .064974.765    .0375030.345    .055

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4974.7655030.345             1795    2200    2270             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 11.430

INPUT

Description: FEMA Q - Drury Road Bridge XS4

Station Elevation Data    num=      52

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4624.25     820 4639.23     818 4645.94     816 4652.67     814 4660.18     812

4674.2     810 4679.74     808 4685.08     806 4690.12     804 4694.67     802

4698.74     800 4703.64     798 4708.31     796 4712.98     794  4717.6     792

4722.71     790 4730.52     788 4747.87     788 4772.09     790 4813.84     790

4825.83     788  4930.6     786 4941.94     784    4975  781.24    4976   780.5

5000   778.2    5024   779.3    5025  781.77 5025.88     784 5035.44     786

5038.31     788 5041.89     790 5043.23     792 5076.03     792 5084.89     790

5097.92     790 5106.27     792 5109.27     794 5113.97     796    5121     798

5127.09     800 5143.15     804 5150.51     806 5158.11     808 5165.62     810

5173.42     812    5182     814 5189.93     816 5216.79     824 5222.28     826

5227.77     828 5233.19     830

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4624.25     .09    4975    .037    5025     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4975    5025             28.5    28.5    28.5             .3       .5

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 11.422

INPUT

Description: Drury Road Bridge XS3

Station Elevation Data    num=      64

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4652.66     8204684.105     8184689.955     8164698.305     8144709.285     812

4722.115     8104725.185     8084728.315     8064731.225     8044734.175     802

4737.245     8004742.625     7984747.825     7964752.695     7944756.795     792

4760.345     7904769.925     7884796.555     7884805.595     7904815.885     792

4835.005     7924894.845     7904943.805     7884952.685     7864954.865     784

4968.15  781.24    4978   779.8    4982   779.6    4986   779.5  4986.5   779.5

4987   779.5    4992   778.8    4994   778.8    4996  778.45    4998   778.3

5003   778.2    5009   777.9    5014   777.9    5016   777.9    5020   777.9

5022   779.6  5022.5   779.7 5031.85  781.77    5037     7865039.045     788

5040.685     7905046.295     7925080.295     7925086.645     790  5100.3  789.01

5116.645     7905121.505     7925135.235     7985146.585     8025152.555     804

5158.665     8065170.085     8105202.095     8165212.565     8185222.985     820

5229.845     8225237.075     8245243.845     8265250.575     828

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4652.66     .09 4968.15    .037 5031.85     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4968.15 5031.85             45.5    45.5    45.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4652.66  4955.5  792.26  5043.55250.575     792

BRIDGE                 RIVER: Contoocook River

REACH: 001                RS: 11.420

INPUT

Description:

Distance from Upstream XS =    11.5

Deck/Roadway Width        =    22.5

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      28

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4835.005  792.26            4880  792.26       0    4928  792.26       0

4950  792.26       0  4955.5  792.26       0    4958  792.26       0

4967.2  792.26       0 4967.25  792.28   782.5  4971.9  792.26   786.5

4976  792.26     788  4981.5  792.26   789.1    4988  792.25     788

4991.8  792.24   786.8  4994.5  792.23     785    4996  792.22     783

4997.25  792.22   779.3    5002  792.21   778.8    5004   792.2     783

5006  792.19     785    5008  792.18   786.5  5012.5  792.17   788.7

5018.5  792.16   789.1 5023.75  792.13     788    5026  792.11   786.5

5030  792.09     783    5032  792.08   779.4  5032.1  792.06       0

5046.295     792       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      64

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4652.66     8204684.105     8184689.955     8164698.305     8144709.285     812

4722.115     8104725.185     8084728.315     8064731.225     8044734.175     802

4737.245     8004742.625     7984747.825     7964752.695     7944756.795     792

4760.345     7904769.925     7884796.555     7884805.595     7904815.885     792

4835.005     7924894.845     7904943.805     7884952.685     7864954.865     784

4968.15  781.24    4978   779.8    4982   779.6    4986   779.5  4986.5   779.5

4987   779.5    4992   778.8    4994   778.8    4996  778.45    4998   778.3

5003   778.2    5009   777.9    5014   777.9    5016   777.9    5020   777.9

5022   779.6  5022.5   779.7 5031.85  781.77    5037     7865039.045     788

5040.685     7905046.295     7925080.295     7925086.645     790  5100.3  789.01

5116.645     7905121.505     7925135.235     7985146.585     8025152.555     804

5158.665     8065170.085     8105202.095     8165212.565     8185222.985     820

5229.845     8225237.075     8245243.845     8265250.575     828

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4652.66     .09 4968.15    .037 5031.85     .07

Bank Sta: Left   Right    Coeff Contr.   Expan.

4968.15 5031.85             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4652.66  4955.5  792.26  5043.55250.575     792

Downstream  Deck/Roadway Coordinates

num=      28

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4829.63  792.26            4880  792.26       0    4928  792.26       0

4950  792.26       0  4955.5  792.26       0    4958  792.26       0

4967.2  792.26       0 4967.25  792.28   782.5  4971.9  792.26   786.5

4976  792.26     788  4981.5  792.26   789.1    4988  792.25     788

4991.8  792.24   786.8  4994.5  792.23     785    4996  792.22     783

4997.25  792.22   779.3    5002  792.21   778.8    5004   792.2     783

5006  792.19     785    5008  792.18   786.5  5012.5  792.17   788.7

5018.5  792.16   789.1 5023.75  792.13     788    5026  792.11   786.5

5030  792.09     783    5032  792.08   779.4  5032.1  792.06       0

5043.66     792       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      60

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4740.75     820 4752.21     818 4761.02     816 4766.02     814 4770.63     812

4781.12     810 4819.95     798 4825.15     796 4829.63     794 4833.97     792

4838.25     790 4859.82  788.61 4879.49     790 4905.41   790.5 4937.24     790

4946.25     788 4948.34     786 4958.75     784 4969.45  780.58  4978.5   779.6

4982   779.4    4984   779.3    4986   779.3    4987   779.3    4992   778.6

4994   778.6    4996  778.25    4998   778.1    5003     778    5009   777.7

5014   777.7    5016   777.7    5020   777.7    5022   779.4  5022.5   779.5

5030.55  780.93 5032.24     786 5034.12     788 5035.82     790 5043.66     792

5082.22     792 5091.03     790  5102.3   788.5 5117.45  788.61 5127.96     790

5133.18     792 5138.02     794 5142.89     796 5147.68     798  5158.2     802

5163.56     804 5169.45     806  5174.7     808 5178.86     810 5188.75     812

5229.96     820 5238.02     822 5246.61     824 5254.67     826 5262.73     828

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4740.75     .09 4969.45    .037 5030.55     .07

Bank Sta: Left   Right    Coeff Contr.   Expan.

4969.45 5030.55             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4740.75  4955.5   789.1  5043.5 5262.73   789.1

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Piers =  1

Pier Data

Pier Station     Upstream=4999.625    Downstream=4999.625

Upstream     num=       2

Width   Elev    Width   Elev

8   777.9       8   789.1

Downstream     num=       2

Width   Elev    Width   Elev

8   777.7       8   789.1

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Yarnell                KVal =    1.25

Selected Low Flow Methods = Yarnell

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =      .8

Max Low Cord                =   789.1

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 11.418

INPUT

Description: Drury Road Bridge XS2

Station Elevation Data    num=      60

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4740.75     820 4752.21     818 4761.02     816 4766.02     814 4770.63     812

4781.12     810 4819.95     798 4825.15     796 4829.63     794 4833.97     792

4838.25     790 4859.82  788.61 4879.49     790 4905.41   790.5 4937.24     790

4946.25     788 4948.34     786 4958.75     784 4969.45  780.58  4978.5   779.6

4982   779.4    4984   779.3    4986   779.3    4987   779.3    4992   778.6

4994   778.6    4996  778.25    4998   778.1    5003     778    5009   777.7

5014   777.7    5016   777.7    5020   777.7    5022   779.4  5022.5   779.5

5030.55  780.93 5032.24     786 5034.12     788 5035.82     790 5043.66     792

5082.22     792 5091.03     790  5102.3   788.5 5117.45  788.61 5127.96     790

5133.18     792 5138.02     794 5142.89     796 5147.68     798  5158.2     802

5163.56     804 5169.45     806  5174.7     808 5178.86     810 5188.75     812

5229.96     820 5238.02     822 5246.61     824 5254.67     826 5262.73     828

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4740.75     .09 4969.45    .037 5030.55     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4969.45 5030.55             18.5    18.5    18.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4740.75  4955.5   789.1  5043.5 5262.73   789.1

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 11.412

INPUT

Description: Drury Road Bridge XS1

Station Elevation Data    num=      45

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4775.245     8184786.595     8164796.455     8144819.545     8084825.015     806

4830.065     8044835.245     8024840.495     8004842.215     7984843.975     796

4845.695     7944849.255     7904863.655     7884881.975     7884932.745     786

4948.235     784 4962.59  780.58  4977.5   778.7  5001.5   777.9  5025.5   777.5

5037.41  780.525039.655     7845046.655     7865051.895     7885058.345     790

5064.21  790.26 5075.06  790.26 5079.62   790.15145.225     7905150.025     792

5159.275     7965163.895     7985168.535     8005174.845     8025180.405     804

5185.965     8065191.585     8085194.635     8105232.475     8185241.435     820

5249.975     8225258.925     8245267.405     8265275.795     8285284.135     830

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4775.245     .09 4962.59    .037 5037.41     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4962.59 5037.41             1000     955     900             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 11.223

INPUT

Description:

Station Elevation Data    num=      48

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4683.135     8204686.815     8184690.645     8164694.575     8144698.655     812

4702.575     8104705.655     8084734.535     8064739.135     8044741.345     802

4746.315     8004750.985     7984753.815     7964756.525     7944765.995     792

4788.075     7904858.145     7884875.615     7864897.905     7844934.525     782

4950.635     7804957.095     778 4968.74  774.72    4984   774.3 5031.26  775.14

5039.835     7785058.765     7805082.585     7825183.755     7845216.095     786

5222.815     7885226.895     7905232.465     7925237.595     7945242.725     796

5247.745     7985252.745     8005260.035     8025266.835     8045273.615     806

5280.275     8085286.855     8105292.425     8125298.385     8145303.925     816

5309.485     8185314.975     8205330.465     822

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4683.135     .094957.095    .0375039.835     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4957.0955039.835              880     930     970             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 11.040

INPUT

Description: FEMA P

Station Elevation Data    num=      67

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4171.265     8204177.385     8184186.085     8164194.875     8144197.685     812

4203.045     8104208.555     8084212.235     8064219.165     8044224.625     802

4234.725     8004252.665     7984261.785     7964268.125     7944272.775     794

4297.655     7944334.155     7924344.755     7904395.005     788 4417.37  787.71

4436.975     788 4451.13  788.364462.355     7884471.525     7864477.805     782

4495.98  781.564513.395     7824524.115     786 4532.94  786.424546.345     786

4551.535     7844555.895     7824561.685     7824573.675     7844621.665     784

4629.505     7824637.315     7804645.185     7784938.095     7764958.675     774

4978.09  772.28  4984.5   772.2  5014.5     772 5021.91  771.245037.495     774

5047.725     7765079.565     7785088.825     7805124.305     7825199.175     784

5229.855     7845512.845     7845528.075     7905535.495     7925539.255     794

5545.355     7965550.935     7985556.155     8005564.595     8025574.845     804

5591.555     8065608.305     8085620.175     8105640.875     8125660.035     814

5711.215     8185731.095     820

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4171.265     .084958.675    .0355037.495     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4958.6755037.495              750     880     855             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.970

INPUT

Description:

Station Elevation Data    num=      58

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4099.415     8204109.345     8184124.745     8164137.095     8144144.775     812

4149.995     8104157.555     8084165.285     8064173.205     8044179.235     802

4182.485     8004191.715     7984201.955     7964207.795     7944214.335     792

4220.425     7904273.265     7884335.425     7864406.755     7844445.465     782

4561.105     7824622.675     7824633.785     7804645.465     7784652.905     776

4681.215     7764715.015     7764743.125     7744759.065     7744955.515     774

4973.25  772.28    4975   771.4    5000   770.2 5026.75  770.855089.905     774

5348.735     774 5531.53  773.225689.785     7745799.255     7765828.435     778

5882.2  778.64 6025.65  778.84 6089.41  780.036146.365     7826183.695     784

6215.955     7866229.775     7886249.685     7906253.095     7926327.895     800

6352.585     8026369.055     8046378.825     8066395.225     8086410.105     810

6416.255     8126422.215     8146435.285     818

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4099.415     .084955.515    .0355089.905     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4955.5155089.905              500     540     480             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.866

INPUT

Description:

Station Elevation Data    num=      55

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3737.375     8223760.435     8203767.365     8183773.105     8163777.245     814

3784.225     8123791.625     8103796.645     8083801.715     8063809.905     804

3814.575     8023822.305     8003827.855     798 4214.71  793.964256.035     786

4306.985     7844375.255     7824503.955     7804516.125     7784524.455     776

4530.065     774 4552.91  773.784578.675     774 4623.65  774.384665.755     774

4733.68  773.264797.945     774 4820.13  774.294845.835     7744864.775     774

4869.865     7764880.985     7784924.115     7784941.125     7764953.725     774

4962.185     772 4969.76  768.89 5030.24  769.415036.765     7725369.865     774

5490.935     774 5895.13  772.716119.995     7746242.615     7766284.795     778

6442.525     7826576.345     7866664.375     7906694.655     7926731.545     794

6786.005     7966806.705     7986840.785     8006866.235     8026883.745     804

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3737.375     .084962.185    .0355036.765     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4962.1855036.765              570     565     470             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.752

INPUT

Description:

Station Elevation Data    num=      69

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3946.845     8203979.455     8184004.445     8164028.565     8144067.435     812

4079.795     8104094.065     8084104.555     8064116.605     8044129.745     802

4140.425     8004152.415     7984163.025     7964189.555     7884201.645     786

4217.315     7844227.225     7824237.725     7804246.165     7784252.505     776

4259.775     7744264.485     7724644.755     7724646.855     7744663.095     774

4673.495     7724751.255     7724754.605     7744765.225     7764791.605     776

4921.095     7744924.325     7724927.485     7704933.705     7684965.905     768

4975.385     768 4981.49  767.57    4985   767.4    5001     767    5018   767.4

5018.51  767.595027.415     7685069.215     7705183.405     7725321.005     772

5418.405     7705472.695     7705509.305     7726202.305     7746295.605     776

6337.485     7786384.205     7786399.165     7786510.945     7826536.315     784

6563.845     7866619.625     7886784.965     7926811.155     7946831.745     796

6859.375     7986903.495     8006911.185     8026939.245     8066955.215     808

6983.355     8126994.785     8147001.695     8167014.745     818

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3946.845     .074975.385    .0355027.415     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4975.3855027.415              460     340     225             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.681

INPUT

Description: FEMA O - Sharon Road Bridge XS4

Station Elevation Data    num=      70

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4271.45     820 4275.73     818 4279.56     816  4287.5     814 4293.92     812

4298.04     810 4302.28     808 4307.72     806 4312.67     804 4316.89     802

4322.29     800 4327.81     798 4334.53     796 4337.64     794 4342.17     792

4345.43     790 4349.44     788 4353.24     786 4358.87     784 4363.71     782

4371.15     780 4377.49     778 4387.05     776 4398.25     774 4405.72     772

4415.34     772 4510.64     774 4650.82     774 4949.62     772 4958.69     770

4967.14     768    4973   767.7    4976   766.3    5000   766.3    5026   767.3

5029   767.7 5034.19     768 5044.83     770  5048.6     772  5057.2     774

5067.56     774 5075.29     772 5079.54     770 5152.25     768 5205.72     768

5224.18     770  5303.9     772 5377.86  772.42 5447.62     772 5585.92     770

5602.69     768 5636.08     768 5667.73     772 6362.91     774 6452.44     776

6569.28     778 6621.39     780 6654.24     782 6690.49     784 6789.57     786

6869.01     788 6949.67     792 6962.22     794 6981.67     796 7006.65     798

7048.9     800 7082.58     804  7098.9     806 7138.25     810 7190.14     818

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4271.45     .07 4967.14    .033 5034.19     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4967.14 5034.19               33      33      33             .3       .5

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.677

INPUT

Description: Sharon Road Bridge XS3

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4871.8   774.8    4894     775    4950   773.4    4970   767.7  4971.7   767.6

4971.8   767.5  4973.5   767.4    5000   766.3  5026.5   767.8  5028.2   767.9

5028.3   767.9    5083   775.4    5109   775.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4871.8     .07  4973.5    .033  5026.5     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4973.5  5026.5               38      38      38             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4871.8  4966.5   774.8  5033.5    5109   775.3

BRIDGE                 RIVER: Contoocook River

REACH: 001                RS: 10.675

INPUT

Description:

Distance from Upstream XS =       7

Deck/Roadway Width        =      24

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      12

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4871.8   774.8            4894     775          4971.7   775.7       0

4971.8   778.4       0  4973.4   778.4       0  4973.5   778.4   772.7

5000   778.4   772.7  5026.5   778.4   772.7  5026.7   778.4       0

5028.3   775.7            5083   775.4            5109   775.3

Upstream Bridge Cross Section Data

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4871.8   774.8    4894     775    4950   773.4    4970   767.7  4971.7   767.6

4971.8   767.5  4973.5   767.4    5000   766.3  5026.5   767.8  5028.2   767.9

5028.3   767.9    5083   775.4    5109   775.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4871.8     .07  4973.5    .033  5026.5     .09

Bank Sta: Left   Right    Coeff Contr.   Expan.

4973.5  5026.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4871.8  4966.5   774.8  5033.5    5109   775.3

Downstream  Deck/Roadway Coordinates

num=      12

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4871.8   774.8            4894     775          4971.7   775.7       0

4971.8   778.4       0  4973.4   778.4       0  4973.5   778.4   772.7

5000   778.4   772.7  5026.5   778.4   772.7  5026.7   778.4       0

5028.3   775.7            5083   775.4            5109   775.3

Downstream Bridge Cross Section Data

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4871.8   774.6    4894   774.8    4950   773.2    4970   767.5  4971.7   767.4

4971.8   767.3  4973.5   767.2    5000   766.1  5026.5   767.6  5028.2   767.7

5028.3   767.7    5083   775.2    5109   775.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4871.8     .07  4973.5    .033  5026.5     .09

Bank Sta: Left   Right    Coeff Contr.   Expan.

4973.5  5026.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4871.8  4966.5   772.1  5033.5    5109   772.1

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   774.8

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =    1.17

Selected Low Flow Methods = Highest Energy Answer

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =      .8

Max Low Cord                =   772.7

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.673

INPUT

Description: Sharon Road Bridge XS2

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4871.8   774.6    4894   774.8    4950   773.2    4970   767.5  4971.7   767.4

4971.8   767.3  4973.5   767.2    5000   766.1  5026.5   767.6  5028.2   767.7

5028.3   767.7    5083   775.2    5109   775.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4871.8     .07  4973.5    .033  5026.5     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4973.5  5026.5               48      48      48             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4871.8  4966.5   772.1  5033.5    5109   772.1

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.667

INPUT

Description: Sharon Road Bridge XS1

Station Elevation Data    num=      73

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3929.035     8203941.125     8183952.655     8163959.845     8143966.965     812

3973.955     8103978.215     8083986.075     8063993.315     8044000.805     802

4008.235     8004012.165     7984021.045     7964026.125     7944029.505     792

4035.625     7904038.495     7884041.575     7864046.685     7844049.845     782

4053.605     7804057.415     7784061.735     7764067.075     7744076.095     772

4090.365     7724096.075     7724106.845     772    4165  772.344349.755     772

4386.785     7724412.395     7724759.185     772 4833.41  772.434868.455     772

4875.665     7704892.955     7684962.985     766 4967.28  765.87    4989   765.5

5005     765    5018   765.5 5032.72  765.875040.335     7665051.555     768

5074.485     770 5236.63  770.395391.825     7705428.225     7685433.825     770

5506.21   770.35583.335     7706005.125     7726028.835     7746049.525     774

6087.83   773.1 6280.71  772.55 6445.46  773.766512.965     7766531.455     778

6542.795     7806591.505     7866604.615     7886615.025     7906621.105     792

6627.005     7946632.725     7966644.595     8006649.435     8026654.455     804

6660.035     8066666.805     8086674.455     810

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3929.035     .07 4967.28    .033 5032.72     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4967.28 5032.72              360     830     450             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.567

INPUT

Description:

Station Elevation Data    num=      64

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

2691.135     8202698.175     8182706.645     8162727.105     8142754.545     812

2788.995     8102826.905     8082856.655     8062888.745     8042949.625     802

3003.375     8003031.225     7983076.485     7963084.295     7943107.775     792

3191.375     7903253.355     7883265.575     7863273.415     7863299.475     788

3314.855     7903328.425     7923357.865     7923507.695     7903548.455     788

3573.675     7863609.875     7843626.755     7823632.395     7803656.395     778

3667.805     7763673.695     7743917.945     772 3958.49  771.07 3979.83  771.07

4022.975     770 4048.77  769.21 4069.49  769.224099.765     7684144.705     768

4268.89  768.57 4384.79  768.314427.065     7684451.655     766 4483.65  765.79

4558.555     7664575.515     766 4827.94  765.594900.405     766 4937.02  767.21

4963.585     766 4976.68  764.69    4982   762.7    5000     762    5018   763.1

5026.28     7665029.155     7685045.055     7745048.745     7765052.865     778

5056.615     7805069.505     7825086.235     7845094.335     786

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

2691.135     .07 4976.68     .03 5026.28     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4976.68 5026.28              510     915     825             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.456

INPUT

Description:

Station Elevation Data    num=      61

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3347.54     820  3366.3     818 3376.56     816 3398.05     814 3432.08     812

3456.94     810 3516.53     808  3557.7     806 3619.79     804 3631.07     802

3642.77     800 3667.33     798 3696.43     796 3763.97     794 3781.55     792

3836.48     790 3906.33     788 3924.72     786 3936.18     784 3951.38     782

3972.52     782 3986.37     784 3997.54     786 4015.16     788 4103.59     788

4124.02     786 4167.35     784 4195.98     782 4221.79     780 4255.25     778

4297.49     776 4323.18     774 4475.86     772 4900.84     772 4909.76     772

4913.99     770 4919.39     768 4937.58     766 4970.03     764    4972  763.52

4972.5   761.3  5000.5     761  5028.5   761.3    5029  763.67 5034.64     764

5053.83  764.36 5071.42     764  5105.6  763.64 5253.38     764 5267.18     766

5282.3     768 5325.34     772 5355.18     774 5367.15     776 5378.21     778

5387.51     780 5406.96     782  5420.7     784 5437.22     788 5441.41     790

5453.79     792

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3347.54     .06    4972     .03    5029     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4972    5029              565     625     690             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.366

INPUT

Description:

Station Elevation Data    num=      73

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3336.47     820 3369.02     818 3451.96     816 3525.23     814 3583.15     812

3645.49     810 3679.57     808  3700.9     806  3723.5     804 3733.84     802

3746.48     800 3758.81     798 3775.97     796 3856.29     794 3872.71     792

3891.66     790 3903.82     788 3917.81     786 3927.96     784 3937.59     782

3949.1     780 3964.65     778 3973.19     776 3984.57     774 3995.16     772

4009.53     770 4042.13     768 4116.61  767.61 4184.88  767.85 4236.73     768

4301.91  768.33 4351.81  768.21 4400.39  768.01 4444.72     768    4478     766

4492.64     764 4547.11  763.76 4600.28     764 4654.45     766 4700.44     766

4718.58     764 4808.78  763.91 4970.47  764.05    4983     763    4985   760.8

4995   760.5    5005   760.8    5007     763 5029.53  763.67 5218.72     764

5245.43     764 5345.53  763.83 5701.28     764 5705.26     766 5710.91     768

5714.2     770 5715.27     772 5716.36     774 5717.45     776 5718.55     778

5719.68     780  5720.9     782 5722.18     784 5723.47     786 5724.75     788

5727.15     792 5728.33     794 5729.51     796 5730.69     798 5735.18     802

5741.84     804  5746.4     806 5750.25     808

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3336.47     .06 4970.47     .03 5029.53     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4970.47 5029.53             1100    1120    1025             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.260

INPUT

Description: FEMA N - Old Powers Bridge Road XS4

Station Elevation Data    num=      54

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3649.49     810 3666.76     808 3688.04     806  3700.8     804 3715.09     802

3729.31     800 3743.67     798 3765.12     796 3768.46     794 3773.35     792

3778.42     790 3821.67     788 3836.94     786 3845.87     784 3854.17     782

3861.36     780  3871.5     778 3889.71     776 3930.25     774    3987     772

4073.94     770 4127.99     768 4234.67     766 4447.97  764.85 4634.54     766

4720.81     766 4724.24     764 4811.85   762.7 4951.85   762.7 4971.85   759.2

5051.85     760 5074.85     760 5080.36  764.11 5091.85     770 5110.78     772

5114.37     774 5117.79     776  5121.4     778 5126.52     780 5298.16     782

5362.42     784  5488.2     786  5670.4     788 5810.52     790 5885.09     792

5940.97     794 5996.48     796 6067.57     798    6102     800  6124.9     802

6146.02     804 6164.73     806 6187.41     808 6202.83     810

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3649.49     .05 4724.24     .03 5080.36     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4724.24 5080.36             29.5    29.5    29.5             .3       .5

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.253

INPUT

Description: Old Powers Bridge Road XS3

Station Elevation Data    num=      58

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3679.435     8103710.515     8083722.675     8063732.685     8043741.445     802

3749.575     8003765.095     7983776.585     7963783.345     7943789.985     792

3798.815     7903842.385     7883892.135     7863899.755     7843903.725     782

3911.395     7803921.225     7783926.745     7763938.355     7743992.155     772

4093.655     7704143.205     7684237.505     766 4427.93  765.144626.685     766

4735.715     7664738.605     764 4759.34  762.23  4939.8   760.7  4949.7   759.2

4967.7   758.7  4996.7   759.8  5029.7   759.6  5060.2   762.75072.895     764

5076.705     7665082.625     7685090.785     7705112.845     7725137.695     774

5162.535     7765192.685     7785264.195     7805306.605     7825341.135     784

5501.665     7865630.855     7885832.175     7905916.965     7925993.105     794

6046.095     7966090.105     7986133.735     8006165.215     8026184.235     804

6202.775     8066230.525     8086256.865     810

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3679.435     .054738.605     .035072.895     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4738.6055072.895               41      41      41             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3679.435    4735   768.5 5079.746256.865  764.03

BRIDGE                 RIVER: Contoocook River

REACH: 001                RS: 10.251

INPUT

Description:

Distance from Upstream XS =    10.5

Deck/Roadway Width        =      20

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      14

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4093.655     770            4689   768.5            4705   768.5

4750   768.5            4790   768.5          4888.5   768.5

4929.16  772.44            4940   772.6       0  4940.1   772.6     769

5060.5   772.6     769  5060.6   772.6       0    5133   772.6       0

5170   773.8       0    5250   776.5       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      58

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3679.435     8103710.515     8083722.675     8063732.685     8043741.445     802

3749.575     8003765.095     7983776.585     7963783.345     7943789.985     792

3798.815     7903842.385     7883892.135     7863899.755     7843903.725     782

3911.395     7803921.225     7783926.745     7763938.355     7743992.155     772

4093.655     7704143.205     7684237.505     766 4427.93  765.144626.685     766

4735.715     7664738.605     764 4759.34  762.23  4939.8   760.7  4949.7   759.2

4967.7   758.7  4996.7   759.8  5029.7   759.6  5060.2   762.75072.895     764

5076.705     7665082.625     7685090.785     7705112.845     7725137.695     774

5162.535     7765192.685     7785264.195     7805306.605     7825341.135     784

5501.665     7865630.855     7885832.175     7905916.965     7925993.105     794

6046.095     7966090.105     7986133.735     8006165.215     8026184.235     804

6202.775     8066230.525     8086256.865     810

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3679.435     .054738.605     .035072.895     .06

Bank Sta: Left   Right    Coeff Contr.   Expan.

4738.6055072.895             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3679.435    4735   768.5 5079.746256.865  764.03

Downstream  Deck/Roadway Coordinates

num=      12

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4705   768.5            4750   768.5            4790   768.5

4888.5   768.5         4906.59  772.44            4940   772.6       0

4940.1   772.6     769  5060.5   772.6     769  5060.6   772.6       0

5133   772.6       0    5170   773.8       0    5250   776.5       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      69

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3833.88     810 3844.19     808 3863.59     806 3879.27     804 3894.81     804

3895.51     804  3916.2     802 3950.19     800 3964.04     798 3985.69     796

4011.23     794 4019.41     792 4056.01     790  4114.1     788 4143.51     786

4261.63     786 4271.35     784 4282.08     782 4299.69     780 4433.07     778

4622.8     776 4654.06     774 4674.45     772 4699.07     770 4713.27     768

4817.06     768 4838.45     768 4873.89     768 4906.56  763.78  4939.8   760.7

4949.7   759.2  4967.7   758.7  4996.7   759.8  5029.7   759.6  5060.2   762.7

5096.77     764 5103.11     766 5108.46     768  5117.1     770 5161.01     772

5168.87     772 5178.81     772 5191.63     774 5214.71     776 5240.16     778

5249.16     780 5252.78     782 5264.33     784 5270.48     786 5278.76     788

5284.58     790 5291.35     792 5296.54     794 5303.82     796 5309.91     798

5317     800 5320.91     802 5324.17     804 5329.95     806 5336.65     808

5342.18     810 5346.84     812 5352.84     814 5358.02     816 5366.24     818

5375.29     820 5384.58     822 5392.54     824 5397.45     826

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3833.88     .06 4906.56     .03 5096.77     .06

Bank Sta: Left   Right    Coeff Contr.   Expan.

4906.56 5096.77             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3833.88 4905.47     768    5071 5397.45     769

Left Levee      Station= 4906.01      Elevation=   768.5

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   768.5

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Piers =  1

Pier Data

Pier Station     Upstream=  5000.3    Downstream=  5000.3

Upstream     num=       2

Width   Elev    Width   Elev

4     758       4     769

Downstream     num=       2

Width   Elev    Width   Elev

4     758       4     769

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Yarnell                KVal =    1.25

Selected Low Flow Methods = Yarnell

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =      .8

Max Low Cord                =   760.5

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.249

INPUT

Description: Old Powers Bridge Road XS2

Station Elevation Data    num=      69

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3833.88     810 3844.19     808 3863.59     806 3879.27     804 3894.81     804

3895.51     804  3916.2     802 3950.19     800 3964.04     798 3985.69     796

4011.23     794 4019.41     792 4056.01     790  4114.1     788 4143.51     786

4261.63     786 4271.35     784 4282.08     782 4299.69     780 4433.07     778

4622.8     776 4654.06     774 4674.45     772 4699.07     770 4713.27     768

4817.06     768 4838.45     768 4873.89     768 4906.56  763.78  4939.8   760.7

4949.7   759.2  4967.7   758.7  4996.7   759.8  5029.7   759.6  5060.2   762.7

5096.77     764 5103.11     766 5108.46     768  5117.1     770 5161.01     772

5168.87     772 5178.81     772 5191.63     774 5214.71     776 5240.16     778

5249.16     780 5252.78     782 5264.33     784 5270.48     786 5278.76     788

5284.58     790 5291.35     792 5296.54     794 5303.82     796 5309.91     798

5317     800 5320.91     802 5324.17     804 5329.95     806 5336.65     808

5342.18     810 5346.84     812 5352.84     814 5358.02     816 5366.24     818

5375.29     820 5384.58     822 5392.54     824 5397.45     826

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3833.88     .06 4906.56     .03 5096.77     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4906.56 5096.77             21.5    21.5    21.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3833.88 4905.47     768    5071 5397.45     769

Left Levee      Station= 4906.01      Elevation=   768.5

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.246

INPUT

Description: Old Powers Bridge Road XS1

Station Elevation Data    num=      67

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3878.885     8103909.885     8083922.905     8063939.405     8043959.445     802

3981.435     8003995.425     7984014.735     7964022.435     7944035.785     792

4070.395     7904133.825     7884275.625     7864284.825     7844292.005     782

4310.935     7804389.975     7804394.275     7804551.845     7824566.385     784

4650.835     7844666.045     7824680.735     7764690.205     7744703.485     772

4712.895     7704717.515     7684756.485     768  4885.6  768.17  4887.7   760.2

4947.5   760.2  4997.5   758.2  5047.5   758.1  5087.5   758.1 5107.21  762.79

5117.645     7645119.795     7665123.965     7685127.395     7705165.275     772

5197.315     7745215.975     7765233.195     7785243.475     7805249.185     782

5257.055     7845261.335     7865270.155     7885275.725     7905283.615     792

5289.075     7945294.045     7965301.405     7985309.555     8005313.485     802

5316.045     8045321.685     8065329.085     8085334.855     8105339.545     812

5345.685     8145351.185     8165359.335     8185368.785     8205378.205     822

5386.225     8245391.975     826

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3878.885     .06  4885.6     .035117.645     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4885.65117.645              220     225     230             .1       .3

Left Levee      Station=  4885.6      Elevation=   768.5

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.158

INPUT

Description: Noone Dam XS4

Station Elevation Data    num=      64

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3935.68     810 3944.43     808 3952.78     806 3959.97     804 3969.71     802

3980.38     800 3989.07     798  4003.6     796 4023.79     794 4032.55     792

4068.56     790 4230.19     788 4252.83     786 4271.23     784 4280.28     782

4304.24     780 4378.03     780 4383.16     780 4532.97     782 4544.11     784

4640.46     784 4647.36     782 4663.67     776 4675.34     774 4686.31     772

4699.53     770 4705.52     768 4745.95     768 4759.66     768 4911.74  769.08

4914.75     760 4968.25     760 5018.25     758 5078.25   755.6 5095.93     764

5100.17     766 5105.96     768 5111.17     770 5116.72     772 5122.36     774

5127.95     776 5133.52     778 5139.11     780 5144.98     782 5150.75     784

5156.07     786 5162.32     788 5168.18     790 5172.71     792 5177.34     794

5182.03     796 5186.67     798 5195.51     802 5201.66     804 5206.28     806

5210.98     808 5218.99     810 5228.59     812 5237.56     814 5251.07     816

5262.95     818 5268.96     820 5284.94     822 5301.86     824

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3935.68     .06 4911.74     .03 5095.93     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4911.74 5095.93               46     106      76             .3       .5

Left Levee      Station= 4911.74      Elevation=   768.5

Blocked Obstructions     num=       1

Sta L   Sta R    Elev

4811.71 4864.44  789.92

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.113

INPUT

Description: Noone Dam XS3

Station Elevation Data    num=      58

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3920.535     8103928.765     8083937.215     8063944.745     8043953.615     802

3964.435     8003973.085     7983987.705     7963999.015     7944012.685     792

4063.575     7904212.215     7844247.195     7824278.925     7804342.245     780

4349.375     7804472.065     7824505.425     7844593.335     7844597.925     782

4613.735     7764626.655     7744635.885     7724654.745     7704661.145     768

4704.685     7684714.905     7684866.835     766  4908.9   765.6  4909.1   755.5

5090.9     7555091.835     7645096.625     7665108.075     7705118.285     774

5123.175     7765127.995     7785132.615     7805138.015     7825143.375     784

5148.695     7865153.965     7885159.205     7905175.265     7965180.645     798

5186.045     8005191.825     8025198.305     8045205.645     8065214.075     808

5224.295     8105234.945     8125244.805     8145252.595     8165263.035     818

5272.515     8205284.565     8225302.785     824

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3920.535     .08  4908.9     .035091.835     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4908.95091.835               20      20      20             .3       .5

Blocked Obstructions     num=       1

Sta L   Sta R    Elev

4731.66 4806.77  785.02

INLINE WEIR            RIVER: Contoocook River

REACH: 001                RS: 10.112

INPUT

Description:

Distance from Upstream XS =       9

Deck/Roadway Width        =       2

Weir Coefficient          =       3

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =       13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4847.6   766.1  4867.5   766.1  4868.5   768.2  4899.5   768.2  4899.6   765.6

4908.5   765.6  4908.6   763.8  5021.5   763.8  5021.6   765.3  5039.5   765.3

5039.6   763.8  5091.5   763.8  5105.5   768.5

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   763.8

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.111

INPUT

Description: Noone Dam XS2

Station Elevation Data    num=      67

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3924.145     8103938.955     8083948.055     8063956.365     8043962.265     802

3974.325     8003982.315     7983996.225     7964009.365     7944028.625     792

4064.525     7904159.035     7884179.575     7864207.075     7844226.745     782

4266.705     7804334.175     7804343.915     7804474.465     7824498.715     784

4572.685     7844576.355     7824582.275     7784593.905     7764607.125     774

4618.055     7724636.325     7704647.915     7684876.685     7624897.785     760

4904.695     756    4907   754.2    4924   749.8    5078   749.8    5093   754.2

5096.275     7565099.235     7585102.885     7605105.695     7625111.125     766

5115.325     7685122.835     7725126.475     7745130.065     7765133.595     778

5137.295     7805145.245     7845149.385     7865153.525     7885157.645     790

5161.895     7925168.795     7945174.325     7965179.765     7985185.285     800

5194.015     8025204.305     8045215.295     8065224.585     8085232.045     810

5241.425     8125250.115     8145257.265     8165267.605     8185277.535     820

5288.675     8225305.565     824

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3924.145      .1    4907     .05    5093     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4907    5093               53      53      53             .3       .5

Blocked Obstructions     num=       1

Sta L   Sta R    Elev

4757.96 4857.36  785.05

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 10.110

INPUT

Description: Noone Dam XS1

Station Elevation Data    num=      75

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4065.76     808 4072.44     806 4075.51     804 4081.73     802 4085.63     800

4092.24     798 4099.18     796 4106.86     794 4118.09     792 4131.21     790

4161.6     788 4186.04     786 4308.67     784  4410.2     782 4470.03     780

4499.14     778 4513.49     776 4524.42     774 4557.13     772 4578.69     770

4606.38     768 4670.92     766 4844.36  764.04 4849.82  755.92 4874.78     754

4878.93     752 4885.15     750 4904.82     748 4918.19   747.3 4932.71  748.09

4943.21  749.96 4953.59  751.04 4979.17  751.97 4996.66  753.82 5013.63  755.58

5032.29  755.41 5054.42  754.62  5064.1  753.98  5072.5     750  5080.7  750.03

5088.31  751.25 5095.97     754 5099.09     756 5102.79     758 5106.46     762

5107.97     764  5110.1     766 5112.69     768 5114.62     770 5119.05     772

5123.43     774 5127.77     776 5132.04     778  5136.3     780 5146.22     784

5150.97     786 5155.77     788 5161.57     790 5168.33     792 5180.96     794

5189.54     796 5198.98     798 5211.89     800 5218.62     802 5224.78     804

5230.58     806 5236.35     808 5242.19     810    5251     812 5259.77     814

5267.52     816 5277.63     818 5284.13     820 5296.19     822 5310.39     824

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4065.76     .07 4904.82     .05 5095.97     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4904.82 5095.97             1150    1075    1035             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.958

INPUT

Description:

Station Elevation Data    num=      49

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4791.105     7804793.725     7784796.695     7764800.345     7744804.405     772

4806.615     7704809.335     7684813.555     7664817.345     7644846.165     762

4851.725     7604854.175     7584856.595     7564859.075     7544860.785     752

4863.815     7504879.385     7484894.795     7464918.565     7444931.635     742

4943.965     7404949.535     7384959.705     736  4963.8  735.24    4972   732.9

4999   732.7    5027   732.9  5036.2  735.135037.475     7385039.475     740

5059.125     7425198.945     7445211.255     7465219.475     7485221.925     750

5226.815     7525230.855     7545245.335     7585251.875     7605270.915     762

5296.775     7645305.405     7665362.845     7685391.595     7705403.475     772

5417.475     7745429.705     7765458.655     7785489.015     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4791.105     .09  4963.8    .035  5036.2     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4963.8  5036.2              230     225     212             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.925

INPUT

Description:

Station Elevation Data    num=      46

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4732.41     780 4735.21     778 4737.62     776 4740.36     774 4743.16     772

4745.44     770 4753.66     768 4764.26     766 4789.24     764 4791.05     762

4794.61     760 4797.02     758 4799.43     756 4807.53     754 4819.02     752

4833.9     750  4862.4     748 4864.77     746 4872.41     744 4878.83     742

4891.72     740 4902.78     738 4921.18     736 4957.28     734    5000   730.6

5030.8   733.9 5033.19     734 5035.41     736 5045.84     738 5056.95     740

5083.3     742 5245.64     744 5257.25     746 5280.44     750 5288.57     754

5292.76     756 5301.03     760 5307.61     762 5317.15     764  5336.4     766

5349.56     768 5372.62     772 5386.47     774  5412.7     776 5443.99     778

5458.39     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4732.41     .07 4957.28    .035  5030.8     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4957.28  5030.8              620     560     500             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.847

INPUT

Description: FEMA M - Morrison Road Bridge XS4

Station Elevation Data    num=      52

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4570.485     7744588.205     7724599.775     7704614.055     7684637.515     766

4649.375     7644655.175     7624658.315     7604662.515     7584665.475     756

4669.885     7544716.245     7504721.865     7484726.135     7464729.305     744

4732.705     7424736.465     7404833.875     7384869.775     7364876.395     736

4895.085     7364917.895     7344961.845     732 4963.82  730.15    4968   730.1

4974   726.5    5002   726.3    5031   726.8    5036   730.1 5036.18  730.23

5054.025     7325084.965     7345144.005     7365187.545     7385240.095     740

5271.925     7445286.645     7465303.805     7485315.855     7505327.315     752

5334.825     7545348.925     7565354.235     7585364.565     7605376.845     762

5386.075     7645396.415     7665411.825     7685423.145     7705445.655     774

5460.655     7785468.875     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4570.485     .07 4963.82    .035 5036.18     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4963.82 5036.18             39.5    39.5    39.5             .3       .5

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.840

INPUT

Description: Morrison Road Bridge XS3

Station Elevation Data    num=      50

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4557.455     7744575.075     7724586.875     7704601.395     7684625.125     766

4636.915     7644642.705     7624645.875     7604650.045     7584653.015     756

4657.405     7544703.795     7504709.605     7484713.925     7464717.145     744

4720.565     7424724.215     7404902.975     7384922.105     7364946.895     734

4952.995     732  4954.5   726.1    4973   726.7    5000   726.1    5028   726.8

5034.5   728.2    5035   730.2  5045.5  730.235051.465     7385063.055     740

5220.355     7425355.445     7445441.405     7465499.465     7485552.885     750

5563.155     7525572.635     7545583.625     7565590.845     7585599.095     760

5613.765     7625629.805     7645673.875     7665684.545     7685692.535     770

5697.725     7725703.095     7745709.505     7765714.815     7785722.085     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4557.455     .074952.995    .035  5045.5     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4952.995  5045.5               42      42      42             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4557.455    4952  740.05    50485722.085     740

BRIDGE                 RIVER: Contoocook River

REACH: 001                RS: 9.838

INPUT

Description:

Distance from Upstream XS =    10.5

Deck/Roadway Width        =      21

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=       6

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4724.215     740          4962.4  740.05       0  4962.5  740.05   736.4

5037.5     740   736.4  5037.6     740       05063.055     740

Upstream Bridge Cross Section Data

Station Elevation Data    num=      50

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4557.455     7744575.075     7724586.875     7704601.395     7684625.125     766

4636.915     7644642.705     7624645.875     7604650.045     7584653.015     756

4657.405     7544703.795     7504709.605     7484713.925     7464717.145     744

4720.565     7424724.215     7404902.975     7384922.105     7364946.895     734

4952.995     732  4954.5   726.1    4973   726.7    5000   726.1    5028   726.8

5034.5   728.2    5035   730.2  5045.5  730.235051.465     7385063.055     740

5220.355     7425355.445     7445441.405     7465499.465     7485552.885     750

5563.155     7525572.635     7545583.625     7565590.845     7585599.095     760

5613.765     7625629.805     7645673.875     7665684.545     7685692.535     770

5697.725     7725703.095     7745709.505     7765714.815     7785722.085     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4557.455     .074952.995    .035  5045.5     .09

Bank Sta: Left   Right    Coeff Contr.   Expan.

4952.995  5045.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4557.455    4952  740.05    50485722.085     740

Downstream  Deck/Roadway Coordinates

num=       7

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4637.445     740            4950  740.05       0  4962.4  740.05       0

4962.5  740.05   736.4  5037.5     740   736.4  5037.6     740       0

5045.625     740

Downstream Bridge Cross Section Data

Station Elevation Data    num=      33

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4494.355     7524537.915     7504547.625     7484571.445     7464594.875     744

4619.945     7424637.445     740 4664.76  738.44 4714.33  738.424737.135     738

4781.075     7364904.385     7364933.685     736 4959.49  730.15    4967     728

4973   726.5    5000   725.9    5028   726.6  5034.5     728    5035     730

5037.5   730.2 5040.51  730.235045.625     7405182.115     7425198.315     744

5205.325     7465224.965     7485252.185     7505299.315     7505416.695     750

5450.365     7525469.875     7545492.805     756

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4494.355     .08 4959.49    .035 5040.51     .06

Bank Sta: Left   Right    Coeff Contr.   Expan.

4959.49 5040.51             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4494.355    4951     738    50485492.805     738

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =     740

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =    1.14

Selected Low Flow Methods = Highest Energy Answer

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =      .8

Max Low Cord                =   736.4

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.836

INPUT

Description: Morrison Road Bridge XS2

Station Elevation Data    num=      33

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4494.355     7524537.915     7504547.625     7484571.445     7464594.875     744

4619.945     7424637.445     740 4664.76  738.44 4714.33  738.424737.135     738

4781.075     7364904.385     7364933.685     736 4959.49  730.15    4967     728

4973   726.5    5000   725.9    5028   726.6  5034.5     728    5035     730

5037.5   730.2 5040.51  730.235045.625     7405182.115     7425198.315     744

5205.325     7465224.965     7485252.185     7505299.315     7505416.695     750

5450.365     7525469.875     7545492.805     756

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4494.355     .08 4959.49    .035 5040.51     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4959.49 5040.51             39.5    39.5    39.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4494.355    4951     738    50485492.805     738

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.827

INPUT

Description: Morrison Road Bridge XS1

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4473.79     752 4499.92     750 4524.72     748 4541.65     746 4560.63     744

4581.53     742 4616.19     740 4623.93  738.41 4672.13  738.41 4686.67     738

4701.97     736 4732.87     734 4798.18  732.12 4840.09     732 4847.94     734

4864.7     734 4955.84  730.15    4963   725.9    4990   725.6    5020     726

5044.16   729.6 5045.27     730 5049.47     732 5053.52     734 5059.26     736

5076.68     738 5096.77     740 5144.46     742  5166.5     744 5176.01     746

5185.77     748 5315.06     750 5376.71     752 5383.58     754 5394.28     756

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4473.79     .08 4955.84    .035 5044.16    .035

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4955.84 5044.16              350     720     670             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.685

INPUT

Description:

Station Elevation Data    num=      36

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4612.475     7584656.675     7564716.045     7544740.355     7524761.325     750

4795.405     7484818.555     7464843.435     7444864.445     7424890.455     740

4906.23  739.65 4909.71  737.37 4914.67  736.92    4935     7374949.475     736

4956.275     7344960.125     7324962.415     7304965.525     7284969.035     726

4971.61  726.01    4975     723    5000   722.5    5020     723 5028.39  725.96

5034.225     7265052.245     7285066.945     7305182.175     7345213.595     736

5241.325     7385268.275     7405293.345     7425306.515     7445333.115     746

5449.745     748

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4612.475    .055 4971.61    .033 5028.39     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4971.61 5028.39              990     950    1000             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.495

INPUT

Description:

Station Elevation Data    num=      72

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3862.4     7963865.965     7943869.405     7923878.965     7863882.045     784

3887.915     7803890.825     7783893.595     7763896.505     7743899.335     772

3902.275     7703907.595     7683912.975     7663918.175     7643923.425     762

3928.675     7603930.635     7583932.575     7563934.565     7543936.425     752

3938.305     7503942.995     7483947.575     7463952.195     7443956.875     742

3961.465     7404121.945     7384187.685     7364228.245     7364272.395     736

4290.835     7364296.335     7384315.315     7384322.785     7364324.305     734

4327.675     7324332.345     730 4395.71  727.994426.845     7284596.735     726

4644.705     7244955.255     722 4960.57  720.95    4967   718.8    5000   719.3

5034   719.6 5039.43  721.235042.685     722 5093.74  722.44 5240.97  722.64

5426.365     7225780.845     7205810.955     720 6154.99  720.916325.955     724

6351.505     7276404.335     7326419.385     7346435.505     7366447.855     738

6473.695     7426483.595     7446493.795     7466505.545     7486512.845     750

6531.675     7546539.385     7566555.815     7606575.225     7626590.025     764

6597.695     7666610.095     768

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3862.4     .06 4960.57    .033 5039.43     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4960.57 5039.43             1635    1760    1950             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.132

INPUT

Description: FEMA L - Route 101 Bridge XS4

Station Elevation Data    num=      41

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4539.545     7404548.525     7384568.835     7364593.905     7344601.615     732

4611.385     7304617.475     7284623.265     7264945.895     7244954.065     722

4959.485     7204962.585     718 4966.75   716.8    4969   715.3    4974  713.55

5000  713.55    5029  713.55    5031   715.3 5033.25   716.85033.445     718

5041.075     7205048.715     7225054.405     7245059.895     7265062.945     728

5071.875     7305089.825     7325116.115     7345136.605     7365155.795     738

5170.555     7405198.945     7425239.425     7445294.775     7465346.345     748

5393.925     7505428.835     7525460.405     7545505.705     7565532.175     758

5558.815     760

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4539.545     .06 4966.75    .033 5033.25     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4966.75 5033.25             17.5    17.5    17.5             .3       .5

Blocked Obstructions     num=       1

Sta L   Sta R    Elev

4651.53 4750.69  739.82

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.126

INPUT

Description: Route 101 Bridge XS3

Station Elevation Data    num=      73

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3252.415     7963267.225     7943325.225     7923328.875     7903333.885     788

3339.735     7863347.165     7843351.275     7823358.905     7803378.855     778

3404.795     7763430.425     7743445.555     7723461.795     7703468.075     768

3473.485     7663489.525     7643509.605     7623549.635     7583573.285     756

3700.875     7503744.205     7483791.225     7463838.995     7443853.155     742

3977.505     7384019.395     7364053.495     7344083.295     7324125.535     730

4196.005     7284261.165     7264270.745     7264318.745     7264642.345     726

4701.665     7284714.875     7284847.785     7284891.345     7304908.605     730

4914.455     7284920.245     7264925.765     7244932.365     7224943.055     720

4948.465     718 4955.03   716.8    4963  715.26    4998   713.5    5040  714.06

5044.97   716.85048.815     7185061.375     7205070.235     7225074.655     724

5079.545     7265083.725     7285087.445     7305092.755     7325096.215     734

5102.495     7365118.745     7385152.255     7405211.645     7425277.595     744

5332.945     7465384.525     7485432.105     7505467.005     7525498.575     754

5543.885     7565570.355     7585596.985     760

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3252.415     .04 4955.03    .033 5044.97     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4955.03 5044.97             87.5    87.5    87.5             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3252.415    4905     731    50955596.985     739

BRIDGE                 RIVER: Contoocook River

REACH: 001                RS: 9.122

INPUT

Description:

Distance from Upstream XS =      22

Deck/Roadway Width        =    43.5

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=       6

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4700     731       0  4904.9   734.5       0    4905   734.5   730.5

5095     739     735  5095.1     739       05152.255     740

Upstream Bridge Cross Section Data

Station Elevation Data    num=      73

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3252.415     7963267.225     7943325.225     7923328.875     7903333.885     788

3339.735     7863347.165     7843351.275     7823358.905     7803378.855     778

3404.795     7763430.425     7743445.555     7723461.795     7703468.075     768

3473.485     7663489.525     7643509.605     7623549.635     7583573.285     756

3700.875     7503744.205     7483791.225     7463838.995     7443853.155     742

3977.505     7384019.395     7364053.495     7344083.295     7324125.535     730

4196.005     7284261.165     7264270.745     7264318.745     7264642.345     726

4701.665     7284714.875     7284847.785     7284891.345     7304908.605     730

4914.455     7284920.245     7264925.765     7244932.365     7224943.055     720

4948.465     718 4955.03   716.8    4963  715.26    4998   713.5    5040  714.06

5044.97   716.85048.815     7185061.375     7205070.235     7225074.655     724

5079.545     7265083.725     7285087.445     7305092.755     7325096.215     734

5102.495     7365118.745     7385152.255     7405211.645     7425277.595     744

5332.945     7465384.525     7485432.105     7505467.005     7525498.575     754

5543.885     7565570.355     7585596.985     760

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3252.415     .04 4955.03    .033 5044.97     .04

Bank Sta: Left   Right    Coeff Contr.   Expan.

4955.03 5044.97             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3252.415    4905     731    50955596.985     739

Downstream  Deck/Roadway Coordinates

num=       6

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4700     731       0  4904.9   734.5       0    4905   734.5   730.5

5095     739     735  5095.1     739       0 5220.97     740

Downstream Bridge Cross Section Data

Station Elevation Data    num=      84

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3871.91     776 3882.86     774 3885.54     772 3894.87     770 3899.07     768

3903.4     766 3907.35     764  3911.2     762 3914.87     760 3917.74     758

3920.78     756 3923.94     754 3926.97     752 3930.15     750 3932.72     748

3935.68     746 3938.83     744 3942.09     742 3962.27     738 3990.13     736

4001.57     734 4026.85     732 4062.21     730 4121.16  728.96 4159.72  728.96

4252.13     728 4510.75     726 4618.46  727.68 4645.12     728 4754.55     730

4768.29     730 4778.39     728 4863.96     728 4901.51     730 4918.19     730

4923.39     728 4927.28     726 4933.45     724 4942.17     722 4945.95     720

4952.68     718 4954.16  716.34    4966   715.2    5001  713.44    5043     714

5045.84   716.8 5049.77     718 5058.18     720 5078.07     722 5107.51     724

5149.85     726 5177.95     728 5187.56     730 5195.98     732 5201.21     734

5206.33     736 5212.78     738 5220.97     740 5267.53     742 5275.51     742

5373.5     742 5416.92     744 5423.86     746 5427.12     748 5432.59     750

5438.88     752 5450.03     754 5465.18     758 5470.18     760 5481.35     762

5494.67     764 5501.89     766 5507.24     768 5514.13     770 5521.48     772

5526.57     774 5538.03     776 5548.44     778 5552.88     780  5564.6     782

5576.08     784 5579.91     786 5584.75     788 5590.01     790

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3871.91     .08 4954.16    .033 5045.84    .055

Bank Sta: Left   Right    Coeff Contr.   Expan.

4954.16 5045.84             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3871.91    4905     731    5095 5590.01     735

Blocked Obstructions     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4509.74 4539.93  740.05 4595.81 4618.46  740.05

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Piers =  1

Pier Data

Pier Station     Upstream=    4996    Downstream=    4996

Upstream     num=       2

Width   Elev    Width   Elev

4   713.5       4     735

Downstream     num=       2

Width   Elev    Width   Elev

4  713.44       4     735

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Yarnell                KVal =    1.25

Selected Low Flow Methods = Yarnell

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =      .8

Max Low Cord                =     735

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.117

INPUT

Description: Route 101 Bridge XS2

Station Elevation Data    num=      84

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3871.91     776 3882.86     774 3885.54     772 3894.87     770 3899.07     768

3903.4     766 3907.35     764  3911.2     762 3914.87     760 3917.74     758

3920.78     756 3923.94     754 3926.97     752 3930.15     750 3932.72     748

3935.68     746 3938.83     744 3942.09     742 3962.27     738 3990.13     736

4001.57     734 4026.85     732 4062.21     730 4121.16  728.96 4159.72  728.96

4252.13     728 4510.75     726 4618.46  727.68 4645.12     728 4754.55     730

4768.29     730 4778.39     728 4863.96     728 4901.51     730 4918.19     730

4923.39     728 4927.28     726 4933.45     724 4942.17     722 4945.95     720

4952.68     718 4954.16  716.34    4966   715.2    5001  713.44    5043     714

5045.84   716.8 5049.77     718 5058.18     720 5078.07     722 5107.51     724

5149.85     726 5177.95     728 5187.56     730 5195.98     732 5201.21     734

5206.33     736 5212.78     738 5220.97     740 5267.53     742 5275.51     742

5373.5     742 5416.92     744 5423.86     746 5427.12     748 5432.59     750

5438.88     752 5450.03     754 5465.18     758 5470.18     760 5481.35     762

5494.67     764 5501.89     766 5507.24     768 5514.13     770 5521.48     772

5526.57     774 5538.03     776 5548.44     778 5552.88     780  5564.6     782

5576.08     784 5579.91     786 5584.75     788 5590.01     790

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3871.91     .08 4954.16    .033 5045.84    .055

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4954.16 5045.84               10      10      10             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3871.91    4905     731    5095 5590.01     735

Blocked Obstructions     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4509.74 4539.93  740.05 4595.81 4618.46  740.05

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 9.112

INPUT

Description: Route 101 Bridge XS1

Station Elevation Data    num=      77

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3878.79     776 3889.74     774 3892.42     772 3901.75     770 3905.95     768

3910.28     766 3914.23     764 3918.08     762 3921.75     760 3924.62     758

3927.65     756 3930.82     754 3933.85     752 3937.03     750 3939.59     748

3942.56     746 3945.71     744 3948.97     742 3969.15     738 3997.06     736

4008.27     734 4032.83     732 4067.04     730 4149.76  729.04 4190.59  729.04

4259.67     728 4523.79  726.79 4712.26     728 4735.96  728.81 4764.16     728

4776.58     726 4784.04     724 4797.31     722 4920.22     720 4949.93     718

4952.73  716.34    4954   715.1  4957.5   713.4  4997.5   713.4  5037.5   713.4

5041.5   715.1 5047.27   716.8 5049.97     718 5052.12     720 5070.52     722

5114.96     724  5130.9     726 5139.46     728 5156.21     730 5174.01     732

5186.23     734 5196.55     736 5207.51     738 5220.35     740 5229.87  740.16

5300.16  740.16 5345.76     742 5373.91     744 5385.88     746 5441.09     752

5447.84     754 5457.79     756 5468.85     758 5473.42     760 5484.88     762

5498.5     764 5527.55     770 5546.54     772 5551.35     774 5558.82     776

5565.29     778 5572.52     780 5582.63     782 5590.48     784 5597.36     786

5601.76     788 5606.52     790

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3878.79     .08 4952.73    .033 5047.27     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4952.73 5047.27             1375    1485    1540             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.807

INPUT

Description: FEMA K - Confluence with Nubanusit Brook

Station Elevation Data    num=      84

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4554.3     802 4579.81     796 4589.25     794 4596.29     792 4602.85     790

4605.16     788 4609.72     784 4611.98     782 4614.19     780 4618.93     778

4623.37     776  4627.9     774 4637.66     770  4645.5     768  4653.9     766

4663.82     764 4675.24     762 4682.08     760 4687.47     758 4693.49     756

4700.58     754 4705.36     752 4710.22     750 4721.57     748  4724.7     746

4734.09     740 4738.07     738 4750.11  736.89  4789.7  736.89 4829.95  735.91

4833.98  726.55 4868.31     726 4873.98     724    4880     722 4887.62     720

4954.82     718 4960.12     716 4962.31   715.5  4963.5   711.8  4966.5   709.8

5001.5   706.3  5036.5   708.8  5037.5   711.9 5037.69  715.47 5040.19     716

5047.97     718 5071.47     720 5090.06     722  5115.2     724 5146.69     726

5174.2     728 5184.52     730 5192.78     732 5195.79     734 5198.85     736

5202.15     738 5206.02     740 5208.51     742 5212.64     744 5215.82     746

5217.25     748 5234.36     750 5236.48     750 5273.54     750 5275.89     752

5278.95     754 5301.57     756 5325.48     758 5356.56     760 5379.84     762

5385.2     764 5391.63     766 5401.69     768 5410.83     770 5421.91     772

5424.15     774 5428.74     776 5435.62     778 5439.36     780 5447.27     782

5456.4     784 5468.96     786 5476.38     788 5483.37     790

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4554.3     .08 4962.31     .03 5037.69     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4962.31 5037.69             1430    1500    1495             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.513

INPUT

Description: FEMA J -  Transcript Dam XS4

Station Elevation Data    num=      42

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3943.575     7483958.205     7403961.225     7384077.045     7364111.115     734

4143.115     732 4261.51  722.79 4332.39  721.04 4373.05  721.05 4509.25  721.13

4637.72  720.84 4684.99  720.84 4919.52  719.96 4931.79  715.24  4934.5     713

4966.5   710.6  4996.5   709.7  5026.5   710.8  5067.5   711.6 5068.21  715.24

5078.715     7205084.525     7225089.035     7245106.805     7385141.935     740

5145.295     7425149.115     7445161.105     7465209.575     7525212.125     754

5215.885     7565219.575     7585229.805     7585241.075     7585286.205     768

5287.435     7705290.695     7725293.935     7745297.185     7765300.435     778

5303.695     7805308.435     782

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3943.575    .035 4931.79     .03 5068.21     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4931.79 5068.21               14      14      14             .3       .5

Blocked Obstructions     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4404.62 4469.55  733.96 4865.28 4918.41  731.98

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.500

INPUT

Description:  Transcript Dam XS3

Station Elevation Data    num=      43

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3949.4     746 3953.28     744 3956.65     742    3961     740 3963.92     738

4079.5     736 4113.94     734  4145.9     732 4275.46  731.08 4362.48  730.76

4400.11   730.6 4431.64     728 4433.77     726 4464.35     724 4670.46  721.92

4940.06  721.25  4946.1   713.4    4970   710.4    5000   709.5    5030   710.6

5054.82   711.4 5059.94  715.24 5064.42     716 5070.31     718 5073.29     720

5082.38     722 5091.24     734 5096.58     734 5098.24     734 5131.79     736

5135.18     738 5137.68     740 5145.68     742  5153.5     744 5197.52     750

5221.5     752 5229.04     754 5244.91     756 5287.54     764 5288.99     766

5291.81     768 5294.64     770 5325.09     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3949.4    .035 4940.06     .03 5059.94     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4940.06 5059.94               14      14      14             .3       .5

Blocked Obstructions     num=       4

Sta L   Sta R    Elev   Sta L   Sta R    Elev   Sta L   Sta R    Elev

4391.61 4476.68  744.97 4687.76 4830.83  735.04  4869.5 4921.71  735.04

5160.16 5223.85  765.08

INLINE WEIR            RIVER: Contoocook River

REACH: 001                RS: 8.499

INPUT

Description:

Distance from Upstream XS =       6

Deck/Roadway Width        =       2

Weir Coefficient          =     3.3

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =       12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4871.6   722.4    4924   722.3  4939.3   722.3  4939.4   719.4    4944   719.4

4944.1  715.26    5052  715.26  5052.1   717.7    5068   717.7  5068.1   719.5

5077.8   720.6    5096   722.4

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =  715.26

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.498

INPUT

Description:  Transcript Dam XS2

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3952.02     748 3955.41     746 3959.33     744 3962.73     742 3967.07     740

3969.98     738 4085.62     736 4120.31     734 4152.25     732 4229.13  730.01

4248.92  730.01 4270.34  730.02 4325.53   728.4 4579.25     722 4943.02  721.25

4944.2     708    5053     708    5072     718 5073.79     720 5093.41  720.12

5094.41     732 5128.81     734 5132.49     736 5133.96     738 5135.17     740

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3952.02    .035 4943.02     .03 5073.79     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4943.02 5073.79               14      14      14             .3       .5

Blocked Obstructions     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4295.04 4532.33  744.07 4591.04 4828.63  734.98

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.494

INPUT

Description: Main Street Bridge XS4 -  Transcript Dam XS1

Station Elevation Data    num=      43

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3968.68     748 3972.13     746 3976.12     744 3979.61     742 3983.93     740

3986.8     738 4102.85     736 4139.18     734  4170.2     732 4227.11     730

4379.58     730 4384.39     730 4419.73     730 4670.32  721.45  4691.2  721.45

4946.44  721.25  4952.1   708.9    5000   706.5    5048   708.7 5053.56  721.25

5065.68  722.02 5067.88  727.58  5090.1   727.6 5093.42     730 5123.35     732

5137.88     734 5151.92     736 5154.07     738 5157.27     740 5168.27     742

5218.55     750 5235.34     752 5312.15     760 5320.48     762 5323.79     764

5327.12     766 5329.33     768 5331.83     770  5335.3     772 5341.01     774

5351.22     778 5356.49     780 5358.72     782

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3968.68     .04 4946.44    .032 5053.56     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4946.44 5053.56               20      20      20             .3       .5

Blocked Obstructions     num=       3

Sta L   Sta R    Elev   Sta L   Sta R    Elev   Sta L   Sta R    Elev

4431.21 4667.67  744.61 4707.16 4860.68     732 5175.54 5250.67  772.32

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.486

INPUT

Description: Main Street Bridge XS3

Station Elevation Data    num=      67

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3993.86     748 3997.42     746 4001.64     744 4005.06     742  4009.3     740

4012.11     738 4128.53     736 4166.41     734 4196.26     732 4258.99     730

4334.37  729.01  4374.8  729.01  4610.8  722.01 4958.16  721.25  4962.1   707.7

4962.2   707.6    4963   707.6    4964   707.6    4965   707.5    4966   707.4

4967   707.3    4968   707.3    4969  707.25    4970  707.25    4975   706.9

4980   706.5    4990  706.35    5000  706.35    5010  706.35    5020  706.35

5025   707.2    5030   708.1    5031   708.4    5032   708.6    5033   708.8

5034   708.9    5035   709.1    5036   709.4    5037     710  5037.8   710.1

5037.9   710.1 5041.84  727.34 5087.08     728 5129.24     730 5135.93     732

5145.28     734 5178.37     740 5197.39     742 5211.27     744 5222.38     746

5238.1     748 5256.31     750 5274.88     752 5341.22     758 5346.52     760

5350.01     762 5353.94     764  5355.6     766 5358.41     768 5360.48     770

5364.58     772 5372.87     774 5378.33     776  5384.5     778 5388.58     780

5389.63     782 5392.19     784

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3993.86     .04 4958.16    .032 5041.84     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4958.16 5041.84               83      83      83             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3993.86  4942.2   723.5  5057.8 5392.19   731.7

BRIDGE                 RIVER: Contoocook River

REACH: 001                RS: 8.482

INPUT

Description:

Distance from Upstream XS =      20

Deck/Roadway Width        =      43

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      36

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4800     715       0    4875   723.5       0    4928   727.8       0

4944   728.4       0  4956.7     729       0  4956.8   729.1       0

4962.1   729.1       0  4962.2   729.1     714    4963   729.1   716.5

4964   729.2     718    4965   729.2   719.4    4966   729.3   720.1

4967   729.3   720.6    4968   729.3   721.2    4969   729.4   721.8

4970   729.4     722    4975   729.7   723.1    4980     730     724

4990   730.4   725.1    5000   730.7   725.8    5010     731   725.5

5020   731.2     725    5030   731.4   723.7    5031   731.4   723.2

5032   731.5     723    5033   731.5   722.5    5034   731.6   721.9

5035   731.6     721    5036   731.7   719.9    5037   731.7     716

5037.7   731.7     714  5037.8   731.7       0    5044   732.2       0

5044.1     730       0    5078     730       0 5129.24     730

Upstream Bridge Cross Section Data

Station Elevation Data    num=      67

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3993.86     748 3997.42     746 4001.64     744 4005.06     742  4009.3     740

4012.11     738 4128.53     736 4166.41     734 4196.26     732 4258.99     730

4334.37  729.01  4374.8  729.01  4610.8  722.01 4958.16  721.25  4962.1   707.7

4962.2   707.6    4963   707.6    4964   707.6    4965   707.5    4966   707.4

4967   707.3    4968   707.3    4969  707.25    4970  707.25    4975   706.9

4980   706.5    4990  706.35    5000  706.35    5010  706.35    5020  706.35

5025   707.2    5030   708.1    5031   708.4    5032   708.6    5033   708.8

5034   708.9    5035   709.1    5036   709.4    5037     710  5037.8   710.1

5037.9   710.1 5041.84  727.34 5087.08     728 5129.24     730 5135.93     732

5145.28     734 5178.37     740 5197.39     742 5211.27     744 5222.38     746

5238.1     748 5256.31     750 5274.88     752 5341.22     758 5346.52     760

5350.01     762 5353.94     764  5355.6     766 5358.41     768 5360.48     770

5364.58     772 5372.87     774 5378.33     776  5384.5     778 5388.58     780

5389.63     782 5392.19     784

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3993.86     .04 4958.16    .032 5041.84     .05

Bank Sta: Left   Right    Coeff Contr.   Expan.

4958.16 5041.84             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

3993.86  4942.2   723.5  5057.8 5392.19   731.7

Downstream  Deck/Roadway Coordinates

num=      36

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

4800     715       0    4875   723.5       0    4928   727.8       0

4944   728.4       0  4956.7     729       0  4956.8   729.1       0

4962.1   729.1       0  4962.2   729.1     714    4963   729.1   716.5

4964   729.2     718    4965   729.2   719.4    4966   729.3   720.1

4967   729.3   720.6    4968   729.3   721.2    4969   729.4   721.8

4970   729.4     722    4975   729.7   723.1    4980     730     724

4990   730.4   725.1    5000   730.7   725.8    5010     731   725.5

5020   731.2     725    5030   731.4   723.7    5031   731.4   723.2

5032   731.5     723    5033   731.5   722.5    5034   731.6   721.9

5035   731.6     721    5036   731.7   719.9    5037   731.7     716

5037.7   731.7     714  5037.8   731.7       0    5044   732.2       0

5044.1     730       0    5078     730       0 5179.01     730

Downstream Bridge Cross Section Data

Station Elevation Data    num=      83

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4164.21     810 4167.96     808 4171.52     806 4175.12     804 4178.77     802

4182.27     800 4186.56     798    4191     796 4196.23     794 4200.99     792

4206     790  4209.7     788 4213.48     786 4217.29     784 4221.08     782

4224.99     780  4228.3     778 4230.96     776 4235.06     774 4238.52     772

4241.95     770 4247.25     768 4250.62     766 4258.02     764 4269.74     750

4335.86     748 4420.74     746 4540.83     734 4597.06     732 4632.49     730

4656.46  728.64 4659.51  723.37 4746.11     722 4769.68  720.96 4800.56  720.97

4931.36     720  4933.4     718  4935.8     716 4939.89     714 4947.62     712

4960.27     710  4962.1   707.6  4962.2   707.5    4963   707.5    4964   707.5

4965   707.4    4966   707.3    4967   707.2    4968   707.2    4969  707.15

4970  707.15    4975   706.8    4980   706.4    4990  706.25    5000  706.25

5010  706.25    5020  706.25    5025   707.1    5030     708    5031   708.3

5032   708.5    5033   708.7    5034   708.8    5035     709    5036   709.3

5037.51  709.66 5160.34     728 5179.01     730    5184     732 5190.86     734

5307.6     748 5313.55     750 5317.99     752 5321.56     754 5341.69     762

5360.52     764 5373.53     766 5389.19     768 5403.76     770 5407.96     772

5414.17     776 5422.19     778 5429.35     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4164.21     .04  4962.1    .032 5037.51     .04

Bank Sta: Left   Right    Coeff Contr.   Expan.

4962.1 5037.51             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4164.21  4942.2   723.4  5057.8 5429.35   725.8

Blocked Obstructions     num=       1

Sta L   Sta R    Elev

4393.47 4642.03  760.06

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   723.5

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =   1.154

Selected Low Flow Methods = Highest Energy Answer

High Flow Method

Pressure and Weir flow

Submerged Inlet Cd          =

Submerged Inlet + Outlet Cd =      .8

Max Low Cord                =   725.8

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.478

INPUT

Description: Main Street Bridge XS2

Station Elevation Data    num=      83

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4164.21     810 4167.96     808 4171.52     806 4175.12     804 4178.77     802

4182.27     800 4186.56     798    4191     796 4196.23     794 4200.99     792

4206     790  4209.7     788 4213.48     786 4217.29     784 4221.08     782

4224.99     780  4228.3     778 4230.96     776 4235.06     774 4238.52     772

4241.95     770 4247.25     768 4250.62     766 4258.02     764 4269.74     750

4335.86     748 4420.74     746 4540.83     734 4597.06     732 4632.49     730

4656.46  728.64 4659.51  723.37 4746.11     722 4769.68  720.96 4800.56  720.97

4931.36     720  4933.4     718  4935.8     716 4939.89     714 4947.62     712

4960.27     710  4962.1   707.6  4962.2   707.5    4963   707.5    4964   707.5

4965   707.4    4966   707.3    4967   707.2    4968   707.2    4969  707.15

4970  707.15    4975   706.8    4980   706.4    4990  706.25    5000  706.25

5010  706.25    5020  706.25    5025   707.1    5030     708    5031   708.3

5032   708.5    5033   708.7    5034   708.8    5035     709    5036   709.3

5037.51  709.66 5160.34     728 5179.01     730    5184     732 5190.86     734

5307.6     748 5313.55     750 5317.99     752 5321.56     754 5341.69     762

5360.52     764 5373.53     766 5389.19     768 5403.76     770 5407.96     772

5414.17     776 5422.19     778 5429.35     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4164.21     .04  4962.1    .032 5037.51     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4962.1 5037.51               10      10      10             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

4164.21  4942.2   723.4  5057.8 5429.35   725.8

Blocked Obstructions     num=       1

Sta L   Sta R    Elev

4393.47 4642.03  760.06

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.472

INPUT

Description: Main Street Bridge XS1

Station Elevation Data    num=      63

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4248.52     802 4252.75     800 4257.14     798 4261.85     796 4266.66     794

4271.12     792 4275.88     790 4279.22     788 4282.66     786 4286.27     784

4289.94     782 4293.86     780 4296.57     778  4299.7     776 4302.83     774

4305.93     772 4309.03     770 4313.75     768 4317.29     766 4320.87     764

4328.92     762  4359.5     748 4680.46  729.99 4683.85  722.95 4764.16  721.98

4780.29  719.97 4820.18  719.97 4844.72  719.83 4909.15  720.52 4940.47     720

4945.58     718 4949.66     716 4952.39     714 4955.87     712 4960.66     710

4964.56  709.22 4966.56  708.52    5000   706.1 5032.44  707.67 5035.44  709.37

5051.16  711.31 5052.09  718.86 5085.01  726.88 5140.03  728.27 5174.94  728.27

5181.96     728 5200.35     730 5205.04     732 5209.86     734 5294.99     736

5325.18     746 5330.36     748  5340.2     750 5342.46     752 5385.99     762

5394.39     764 5401.37     766 5407.83     768    5415     770  5433.2     774

5437.91     776 5444.66     778 5452.49     780

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4248.52     .04 4964.56    .032 5035.44     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4964.56 5035.44             1880    1898    1840             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 8.136

INPUT

Description: FEMA I

Station Elevation Data    num=      55

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4259.21     760 4299.87     758 4307.66     756 4340.67     754 4398.34     752

4409.04     750 4418.95     746 4423.24     744 4431.24     740 4434.44     738

4437.65     736 4444.21     732 4447.39     730 4458.12     728 4464.71     726

4471.4     724 4472.61     722 4476.06     720 4483.79     718 4491.49     716

4509.28     714 4750.52     712 4953.02     710  4957.4     708 4960.77     706

4962.27  705.65  5002.5   703.9 5037.73  705.36 5041.67     706 5043.76     708

5046.14     710  5049.9     712 5052.53     714 5053.96     716 5057.04     718

5061.75     720 5075.84  720.76 5108.06  720.76 5111.08     722 5118.24     724

5128.73     724 5144.83     724 5194.79     726 5266.81     728 5324.37     730

5347.22     732 5376.15     734 5387.36     736 5399.04     738  5408.3     740

5416.55     742 5422.77     744 5431.63     746 5435.74     748    5443     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4259.21      .1 4962.27    .032 5037.73      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4962.27 5037.73             2050    2277    2050             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 7.733

INPUT

Description: FEMA H

Station Elevation Data    num=      65

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4281.9     760 4291.99     758 4301.99     756  4311.4     754 4319.73     752

4327.11     750 4331.19     748 4335.34     746 4339.49     744 4343.68     742

4347.85     740 4356.14     738 4364.47     736 4372.82     734    4381     732

4389.25     730 4395.37     728  4398.4     726 4404.85     724  4412.4     722

4416.04     720 4420.65     718 4427.69     716 4432.51     714 4597.39     712

4828.86     710 4956.75     708 4959.22     706 4960.75     704  4961.5   703.7

4963.5   702.2  4999.5   700.2  5034.5   700.9  5037.5   703.7 5038.12     704

5040.48     706 5044.69     708 5048.78     710 5052.99     712 5055.35     714

5057.74     716 5060.66     718 5080.66  718.79 5129.75  718.79 5134.23     720

5138.09     722 5141.79     724 5145.65     726 5149.38     728 5153.21     730

5161.43     732 5169.76     732 5182.85     730 5241.51     730 5300.29     732

5370.32     734 5445.73     736 5490.01     738 5512.21     740 5523.56     742

5531.01     744 5540.33     746 5554.87     748 5564.63     750 5600.02     754

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4281.9     .08 4960.75    .032 5038.12     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4960.75 5038.12             1125    1135    1125             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 7.533

INPUT

Description:

Station Elevation Data    num=      65

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4694.05     760 4698.82     758 4703.71     756 4708.52     754 4713.49     752

4718.28     750 4723.29     748 4728.25     746 4733.31     744 4738.23     742

4743.21     740 4746.76     738 4750.33     736 4757.38     732 4761.01     730

4764.32     728 4767.65     726 4771.06     724 4777.66     720 4783.21     718

4806.56     714 4814.32     713 4834.06  712.92 4839.95     712 4847.34     710

4856.45     708 4952.94     706 4954.67     704  4955.5   699.5  4993.5   698.8

5036.5   699.5 5047.25     704 5049.64     706 5054.28     708 5062.25     708

5108.19     706 5139.86     706    5151     708  5161.4     708 5187.02     708

5337.51     710 5434.23     712 5463.93  712.75 5513.97   712.8 5517.75     714

5521.61     716 5528.12     718 5532.02     720 5536.13     722 5538.48     724

5543.79     726 5547.59     728 5551.24     730 5556.23     732 5563.14     734

5572.39     736 5578.48     738 5584.33     740 5606.11     746 5611.79     748

5619.18     750 5624.16     752 5626.05     754 5629.64     756 5636.76     760

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4694.05     .07 4954.67    .032 5047.25     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4954.67 5047.25             1555    1920    1500             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 7.186

INPUT

Description: FEMA G

Station Elevation Data    num=      55

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4016.57     748 4019.08     746  4021.6     744 4029.95     738 4033.91     736

4038.16     734 4042.71     732 4055.42     728 4062.91     726 4069.64     724

4075.77     722 4081.39     720 4085.49     718 4090.14     716 4093.96     714

4098.17     712 4102.96     710 4343.44     708 4353.66     706 4851.55     704

4884.69     704 4900.98     704 4962.33  703.67  4968.5   701.9  4971.5   700.4

4998.5   697.4  5025.5   700.9  5028.5   701.9 5037.67  703.67 5041.26     704

5060.92     706 5107.99     708 5118.18     710 5123.36     712 5129.05     714

5135.58     716 5218.73     716 5240.21     716 5252.42     718 5262.49     720

5274.96     722 5288.49     724 5301.18     726 5314.43     728 5327.88     730

5332.03     732 5336.42     734 5340.91     736 5345.23     738 5348.68     740

5354.16     742  5359.7     744 5365.41     746  5370.9     748 5376.64     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4016.57     .05 4962.33    .032 5037.67     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4962.33 5037.67             1580    1235    1175             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.975

INPUT

Description:

Station Elevation Data    num=      64

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4121.665     7604127.875     7584134.115     7564140.235     7544146.375     752

4152.425     7504160.485     7484168.645     7464176.905     7444185.255     742

4193.615     7404202.785     7384214.535     7364229.445     7344250.725     732

4262.905     7304280.455     7284310.585     7264335.105     7244362.415     722

4387.645     7204472.705     7184526.565     7164574.295     7144601.415     712

4621.39  711.974698.165     7104716.215     7084766.645     7064771.145     704

4781.22  703.72  4971.5   702.2  4974.5   700.8  4981.5     698  5001.5     697

5021.5     698  5029.5   701.2 5218.78  703.265224.535     7045232.775     706

5249.665     7085283.525     7105291.065     7125299.915     7145310.575     716

5320.315     7185331.995     7205386.195     7205412.955     7205416.455     722

5419.945     7245423.445     7265426.945     7285430.585     7305433.935     732

5439.345     7345444.395     7365458.125     7385461.265     7405468.545     742

5475.795     7445483.085     7465490.715     7485498.015     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4121.665     .04 4781.22    .032 5218.78     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4781.22 5218.78              530     465     300             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.889

INPUT

Description:

Station Elevation Data    num=      75

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4120.315     7604127.165     7584133.975     7564140.795     7544147.605     752

4154.385     7504158.655     7484172.055     7464182.375     7444193.385     742

4216.955     7404235.985     7384261.745     7364292.975     7344322.075     732

4346.215     7304373.015     7284404.145     7264425.255     7244470.305     722

4505.775     7204581.665     7184631.325     7164645.405     714 4677.22  713.39

4709.285     7144751.665     7164771.705     7184787.395     720 4795.68  721.54

4812.34  721.544819.595     7224825.945     7224829.335     7204833.785     718

4840.735     7164848.165     7144855.535     7124863.195     7104868.185     708

4873.255     7064879.935     704 4884.41  702.12    4985   702.1    4987   700.9

5000     698    5012     701    5015   702.4 5115.59  703.265120.655     704

5126.525     7065133.975     7085141.995     7105155.325     7125163.185     714

5175.745     716 5205.51  716.73  5253.8  716.735256.145     7185259.535     720

5263.285     7225267.015     7245270.745     7265274.465     7285278.385     730

5281.125     7325284.625     7345301.925     7365310.935     7385318.495     740

5326.285     7425334.195     7445342.275     7465350.575     7485358.685     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4120.315     .07 4884.41    .032 5115.59     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4884.41 5115.59              525     500     500             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.823

INPUT

Description:  North Village Dam XS4

Station Elevation Data    num=      65

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4232.6     760 4248.77     758 4265.31     756 4300.64     752 4316.71     750

4325.53     748 4344.49     746 4367.05     744 4484.09     742 4489.95     740

4503.21     738 4514.68     736 4522.14     734 4532.74     732 4541.84     730

4562.41     728 4618.86     726 4629.51     726 4642.76     726 4669.85     724

4687.97     722 4709.26     720 4730.11     718  4736.3     717 4776.05     717

4783.06     716 4791.11     714 4795.62     712 4801.71     710 4828.16     708

4835.89     706 4839.23  702.12    4854   701.3    4866   701.1    4870   697.2

4920     697    4969   697.2    4974   701.1    5000  703.26 5003.06     704

5004.79     706  5007.7     708 5012.05     710 5019.76     712 5043.93  712.65

5091.62  712.68  5094.5     714 5099.96     716 5104.13     718 5109.36     720

5113.29     722 5117.24     724 5121.21     726 5125.19     728 5129.37     730

5135.17     732 5139.54     734 5150.08     736 5153.46     738 5155.67     740

5161.52     742 5167.27     744 5173.23     746 5179.27     748 5185.16     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4232.6     .07 4839.23    .032    5000     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4839.23    5000               45      45      45             .3       .5

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.814

INPUT

Description:  North Village Dam XS3

Station Elevation Data    num=      60

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4341.225     7604359.015     7584376.965     7564393.855     7544410.205     752

4424.935     7504430.995     7484459.815     7464475.995     7444545.855     742

4557.255     7404574.685     7384585.975     7364601.445     7344622.355     732

4642.895     7304683.715     7284726.805     7264761.485     7244783.095     722

4799.535     7204814.015     7184824.515     7164835.595     714 4841.93  712.98

4862.23  712.984869.265     7124879.715     7104882.305     7084889.055     706

4906.91   697.5 5093.09   697.55098.805     7045102.095     7065104.415     708

5109.635     7105118.165     712 5132.11  712.39  5179.6  712.395185.595     714

5191.445     7165196.175     7185201.345     7205206.055     7225210.725     724

5215.335     7265219.875     7285224.555     7305232.095     7325237.245     734

5241.055     7345242.365     7345246.785     7365255.505     7385258.935     740

5263.665     7425269.615     7445275.765     7465282.015     7485288.185     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4341.225     .06 4906.91     .03 5093.09     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4906.91 5093.09               13      13      13             .3       .5

INLINE WEIR            RIVER: Contoocook River

REACH: 001                RS: 6.813

INPUT

Description:

Distance from Upstream XS =     5.5

Deck/Roadway Width        =       2

Weir Coefficient          =    3.32

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =       13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4850   708.2    4895   708.2  4897.8   705.6  4929.9   705.6    4930  702.69

5085.8  702.69  5085.9  705.79    5102  705.79    5117     710    5119   710.2

5140   710.5    5143   712.7    5147   712.8

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =  702.69

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.811

INPUT

Description:  North Village Dam XS2

Station Elevation Data    num=      75

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4383.62     758 4395.15     756 4417.78     752 4429.08     750 4438.45     748

4458.55     746  4475.3     744  4482.7     742 4501.75     740 4539.05     736

4566.87     734 4599.15     732 4627.72     730 4678.78     728 4721.52     726

4754.35     724 4777.47     722 4793.04     720  4808.7     718 4821.49     716

4826.17     714 4836.15     712 4838.99     712    4861     712 4875.65     710

4883.09     708 4894.15     706 4907.77     704 4921.35  696.02 4930.25     690

4945.25   691.8 4952.25     692 4963.25   691.5 4970.25   692.3 4990.25   692.7

4990.35   692.7 4990.45   692.7 4990.55   692.7 5040.25     693 5066.25   693.5

5068.05     694 5068.15     694    5082     696 5085.47     698 5088.14     700

5090.75     702 5092.59     704 5095.75     706 5099.88     708 5102.66     710

5107.91     712 5118.13     712 5118.53     712 5170.26  711.99  5175.2     714

5180.97     716 5186.77     718 5190.85     720 5196.83     722 5202.75     724

5208.14     726 5213.09     728 5219.55     730 5227.42     732 5233.52     732

5236.03     732 5240.97     734 5246.18     736  5256.6     738 5260.61     740

5265.24     742 5272.35     744 5279.55     746 5286.91     748 5294.11     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4383.62     .09 4921.35     .03    5082     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4921.35    5082              140     120     110             .3       .5

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.785

INPUT

Description: FEMA F - North Village Dam XS1

Station Elevation Data    num=      68

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4317.14     760 4327.11     758 4337.31     756 4347.53     754 4357.83     752

4368.1     750 4376.11     748 4390.43     746 4405.32     744 4411.62     742

4423.46     740 4435.75     738 4476.06     734 4504.13     732 4536.76     730

4606.18     728 4653.48     726 4686.61     724 4707.29     722 4723.23     720

4738.98     718 4756.16     716 4762.46     714 4772.09     712 4780.29     710

4780.5     710 4819.73     710  4871.3     708 4891.06     706 4894.35     704

4896.75     702 4898.84     700 4902.11     698 4906.18     696  4908.5     694

4928.5   693.7  4948.5   692.2  4988.5   692.7    5008   693.7 5008.55     694

5011.62     702 5022.73     704 5025.77     706 5029.81     708 5036.13     710

5042.23     712 5050.77     712 5059.73     712 5110.15  711.98 5117.54     714

5121.2     716 5125.92     718 5131.69     720  5145.7     722  5150.1     724

5158.1     726 5165.81     728 5178.17     730 5184.28     732  5195.9     734

5199.6     736  5216.5     738 5222.32     740  5229.4     742  5236.6     744

5243.7     746 5251.04     748 5258.11     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4317.14     .07  4908.5     .03 5008.55     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4908.5 5008.55              100      74      35             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.766

INPUT

Description:

Station Elevation Data    num=      72

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4187.68     760 4199.78     758 4211.06     756 4231.16     752 4240.12     750

4259.99     746 4268.32     744  4276.9     742 4289.36     740 4295.62     738

4314.84     734 4323.67     732    4339     730 4352.78     728 4366.94     726

4383.68     724 4409.52     722 4446.33     720 4526.23     718  4575.3     716

4580.46     714 4586.14     712 4609.98   710.1 4630.62   710.1 4653.77     710

4755.31     708 4759.92     706 4767.83     704 4771.84     702 4796.07     698

4818.75     696 4831.91     694    4859   691.9    4891   691.9    4902   691.9

4914   691.9    4918   691.9    4973   691.9    5000     694 5003.24     696

5009.02     698 5010.12     700 5011.11     700 5014.24     702 5017.74     704

5020.96     706 5027.25     708 5031.51     710 5037.34     712 5045.98     712

5053.74     712 5110.51     712 5113.22     712 5116.64     714 5120.79     716

5125.87     718  5130.8     720 5140.97     722 5147.92     724  5155.6     726

5161.69     728 5174.14     730 5178.35     732  5186.7     734 5198.29     736

5214.01     738 5219.43     740 5227.24     742 5234.93     744 5242.59     746

5250.45     748 5258.03     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4187.68    .035 4831.91     .03    5000     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4831.91    5000               83      83      83             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.765

INPUT

Description:

Station Elevation Data    num=      71

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4156.26     758 4170.32     756  4183.5     754 4206.75     750 4214.93     748

4228.56     746 4238.02     744 4246.01     742 4254.29     740 4263.57     738

4279.67     734 4286.87     732 4299.87     730 4312.02     728 4327.92     726

4342.08     724 4362.63     722 4389.98     720 4471.22     718 4476.16     718

4480.38     718 4536.34     716 4543.51     714 4548.97     712 4555.72  711.02

4593.61  711.02 4605.11  710.01 4743.92     708 4750.96     706 4757.24     704

4761.53     702 4809.64     702 4817.68     698 4821.68     696 4825.39  694.64

4879   691.9    4915   691.9    4927   691.9    4931   691.9    4986   691.9

5008.08  694.64 5009.74     698 5012.21     700 5015.51     702  5018.8     704

5022.11     706 5029.53     708  5033.6     710 5039.23     712 5047.64     712

5055.09     712 5089.87     712 5118.34     714 5122.72     716 5128.37     718

5134.31     720    5142     722 5150.68     724 5157.03     726 5162.11     728

5173.58     730 5181.34     732 5188.76     734 5200.69     736 5216.05     738

5221.11     740 5227.98     742 5235.01     744 5242.16     746 5249.82     748

5257.34     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4156.26    .035 4825.39     .03 5008.08     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4825.39 5008.08               83      83      83             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.749

INPUT

Description:

Station Elevation Data    num=      70

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4055.95     760 4070.73     758 4087.33     756 4103.23     754 4119.15     752

4135.97     750 4146.31     748 4169.84     746 4181.07     744  4189.8     742

4205.06     740 4220.06     738 4226.63     736 4241.14     734  4253.7     732

4269.96     730 4278.65     728 4287.27     726 4297.79     724 4310.74     722

4321.08     720 4334.41     718 4352.28     716 4389.96     714 4440.06     712

4450     710 4470.43     710 4481.41     710  4531.3     708 4546.47     706

4575.05     704  4594.5   703.3  4617.7     704 4725.06     706  4734.5     708

4743.01     710 4757.11     712 4768.49     712 4791.25     712 4841.51     712

4849.36  693.49  4874.5   691.6  4910.5   691.6  4922.5   691.6    4927   691.6

4982   691.6 5000.46  693.49 5001.32     696  5004.6     698 5007.66     700

5009.57     702 5013.02     704 5015.59     706  5020.8     708 5027.65     710

5044.92     712 5086.09     714 5105.55     716 5122.91     718    5132     720

5133.97     722 5137.86     724  5140.3     726  5142.7     728 5145.62     730

5150.41     732 5164.71     734 5239.61     742 5254.47     748  5285.3     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4055.95    .035 4849.36     .03 5000.46     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4849.36 5000.46               65      65      65             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.748

INPUT

Description:

Station Elevation Data    num=      73

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3964.65     760 3979.47     758 3993.93     756 4007.65     754 4021.25     752

4034.66     750 4051.42     748  4063.6     746  4075.6     744 4090.32     742

4154.5     738 4170.14     736  4181.7     734 4187.22     732 4197.64     730

4211.91     728 4220.76     726 4234.44     724 4248.65     722 4257.47     720

4272.53     718 4290.85     716 4338.29     714  4466.4     704 4578.85     704

4683.4     706 4693.69     708 4706.63     710 4753.25     712 4808.91     712

4816.96     710 4819.93     708  4825.7     706 4831.28     700 4843.55     698

4847.99     696 4850.26     694 4852.99  693.49  4876.5   691.6  4911.5   691.6

4924.2   691.6  4928.9   691.6  4983.4   691.6 5000.15  693.49 5001.93     696

5004.37     698 5005.92     700 5010.49     702 5014.28     704 5018.45     706

5022.26     708 5025.61     710 5041.17     712 5054.33  712.61 5081.45  712.77

5090.25     714 5099.02     716  5106.2     718  5115.2     720 5130.32     722

5146.54     724 5152.76     726 5154.49     728 5158.82     730 5162.11     732

5164.54     734 5175.61     736 5187.13     738 5206.44     740 5238.88     742

5251.09     746 5281.01     748  5311.3     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3964.65    .035 4852.99     .03 5000.15     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4852.99 5000.15               65      65      65             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.736

INPUT

Description:

Station Elevation Data    num=      87

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3986.69     760 4001.71     758 4023.24     756 4036.45     754 4046.85     752

4060.93     750 4078.85     748 4090.31     746 4102.85     744 4113.13     742

4120.06     740 4145.06     738 4152.37     736 4160.76     734 4163.94     734

4168.42     736 4181.17     736  4193.2     734 4203.99     732 4209.17     730

4223.73     728 4242.14     726 4255.97     724 4308.51     720  4314.9     718

4330.75     716 4362.02     714 4376.84     710 4390.41  708.88 4411.31   708.8

4425.52     708  4432.2     706 4483.61     704 4549.96  702.88 4600.65     704

4612.95     706 4628.02     708  4643.1     710 4645.27     710 4649.17     710

4769.1     712 4798.27     712 4817.73     710 4833.21     708 4844.99     706

4854.84     704 4869.29     702 4881.37     700 4935.84     698 4944.82     696

4947.9     694 4949.22  693.49    4950   691.3    5000   691.1    5048     691

5050.78  693.49 5054.13     694 5058.01     696 5064.68     698 5067.23     700

5070.16     702 5072.88     704 5075.94     706 5078.91     708  5081.9     710

5091.84  710.87 5111.54  710.99 5120.04     712 5123.42     714  5129.2     716

5131.72     718 5135.27     720 5146.74     722  5151.5     724 5160.71     726

5163.84     728 5169.08     730 5193.92     732 5220.71     734 5230.83     736

5244.08     738 5267.09     740 5288.43     742 5310.17     744 5332.92     746

5367.24     748 5400.95     750

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3986.69     .07 4949.22     .03 5050.78     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4949.22 5050.78             2930    3051    3320             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.258

INPUT

Description: FEMA E

Station Elevation Data    num=      41

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4421.25     728 4429.12     726 4524.43     724  4669.2     720 4749.92     718

4756.04     716 4760.86     714 4765.53     712 4770.35     710 4773.56     708

4776.96     706 4780.19     704 4783.54     702 4805.19     694 4847.28     692

4877.29     690    4903  689.75 4928.85     690    4949  689.43    4954   687.7

4959   686.1    4991   685.4    5025   686.4    5028   687.7    5051   688.8

5379.23     700 5397.56     702 5423.47     704 5620.34     706 5752.99     708

5803.85     710 5945.73     712 5969.14     714 5989.02  716.42 6011.74  716.42

6042.02     716 6092.61     718 6129.09     720 6161.46     724 6171.86     726

6189.2     728

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4421.25     .07    4949     .03    5051    .055

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4949    5051              980     980     900             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 6.110

INPUT

Description:

Station Elevation Data    num=      54

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4154.8     730 4191.73     728 4210.35     726 4222.73     724 4238.42     722

4250.53     720 4272.97     718 4293.76     716 4302.52     714 4308.73     712

4313.93     710 4321.88  709.59 4336.28     710 4360.83  710.68 4486.36  710.56

4524.66     710 4613.47     708 4643.87     706 4655.54     704 4683.87     702

4749.07     700 4941.75     698 4949.09     696 4951.87     694 4957.28     692

4961.98     690 4967.08     688 4969.29  687.55    4970   685.3    5000   684.6

5029.33   685.6 5035.92     688 5046.07     690 5055.25     692 5074.74     692

5116.03  691.28 5161.66     692 5250.85  694.11 5290.25   693.8 5359.64     692

5489.13     690 5520.48   689.3 5545.93     690 5553.26     692 5562.12     694

5578.47     696 5601.24     698 5632.18  698.91 5700.86     700 5732.82     702

5879.59     704 5944.33     706 6020.95     708 6069.74     710

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4154.8     .06 4969.29     .03 5035.92     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4969.29 5035.92             2350    2420    2190             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 5.748

INPUT

Description: FEMA D

Station Elevation Data    num=      58

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

2743.03     7302794.845     7282875.295     7262933.445     7222947.035     720

2964.525     7182998.475     7163026.565     7143067.765     7123086.205     710

3125.175     7083180.155     706 3318.49  702.973400.075     7043450.685     706

3558.94  706.223663.945     7063885.905     7043997.495     7004050.515     698

4121.89  697.384180.615     6984202.115     700 4223.02  700.774246.005     700

4277.455     6984289.355     6964861.085     6964873.845     698 4892.47  698.38

4902.535     6984909.035     6964914.265     6944918.575     6924949.635     690

4951.795     688 4956.88  685.88  4957.2   683.1    5041   683.1 5043.12   686.5

5080.325     6885132.635     6905233.135     6925281.495     6945301.805     696

5324.175     6985346.905     7005359.595     7025373.855     7045388.145     706

5399.345     7085411.135     7105419.175     7125427.975     7145436.495     716

5448.745     7185458.185     7205468.855     722

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

2743.03     .05 4956.88     .03 5043.12     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4956.88 5043.12             3120    3143    3300             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 5.256

INPUT

Description:

Station Elevation Data    num=      36

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3507.16     7043516.835     7023675.835     7003723.345     6963750.045     694

3794.185     6923923.645     6904087.395     688 4153.51  687.464224.975     688

4400.23  689.144509.215     688 4539.45  687.324588.845     6884845.645     690

4891.68  690.624899.305     6904905.235     688 4916.53  687.464938.445     688

4953.14  688.444961.195     688 4967.92  685.994969.191   680.8    5041   680.8

5042.025     6865210.415     6905215.795     6925221.515     6945227.455     696

5246.785     7025451.195     7045557.005     7065641.335     7085653.485     710

5679.445     712

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3507.16     .05 4967.92     .035042.025     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4967.925042.025              692    1936    1864             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 4.953

INPUT

Description: FEMA C

Station Elevation Data    num=      31

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4485.83     700 4548.59     698 4582.69     696  4633.9     694 4646.46     692

4676.9     690 4942.38     688 4948.13     686 4959.83  685.53    4960     683

4965     682    5000   679.5    5035   681.6    5040     683 5040.17  685.38

5042.65     686 5055.74     688 5135.74  689.11 5214.46     688 5255.08     688

5333.33  689.11 5419.18     688 5451.01  687.07 5472.39     688 5483.65     690

5490.26     692 5505.43     694 5512.67     696 5529.93     698 5543.35     700

5580.01     702

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4485.83     .06 4959.83     .03 5040.17     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4959.83 5040.17              956     870     787             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 4.817

INPUT

Description:

Station Elevation Data    num=      53

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4176.56     732  4253.8     730 4326.44     728 4346.97     726 4356.27     724

4373.27     722  4380.7     720 4400.16     718 4409.95     716 4418.57     714

4429.39     712 4433.54     710 4442.79     708 4449.05     706 4456.14     704

4463.48     702 4472.41     700 4481.42     700 4498.83     700 4502.79     698

4506.66     696 4510.31     694 4529.94     692 4687.59     690 4785.72  689.37

4857.73     690 4874.73  690.48  4890.9     690 4902.62     688 4923.03     686

4933.84  683.73  4950.5   682.4  4955.5   680.4  4990.5   678.9  5025.5     681

5066.16  684.48 5081.26     686 5101.64     688  5117.6  688.96 5137.28     688

5166.19     686 5197.14  684.61  5228.2     686 5235.58     688 5250.23     690

5254.23     692 5262.93     694 5272.89     696 5302.84     698 5360.46     700

5773.23     702 5989.98  702.38 6222.16     702

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4176.56     .05 4933.84     .03 5066.16     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4933.84 5066.16              729    1130    1200             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 4.640

INPUT

Description:

Station Elevation Data    num=      41

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3754.44  690.45 3942.94     690 3957.91     688 3986.86     686 4037.74  685.59

4095.12     686  4259.6     688 4333.46   688.5 4403.99     688 4412.71     686

4445.95  684.98 4474.98     686 4510.23  686.26 4543.61     686 4601.29  684.56

4657.62     686 4662.17     688 4703.07  688.22 4733.95     688 4778.06  687.54

4821.55     688 4882.52  688.39 4938.49     688 4959.02     686 4961.84  683.73

4965   679.9    5000   678.4    5035   680.5 5038.16  684.48 5048.87     686

5059.16     688 5066.56     690 5071.97     692 5075.03     694 5080.59     696

5093.28     698 5137.56  698.22 5215.97     698 5382.23   697.8 5516.76     698

6200.81   698.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3754.44     .08 4961.84     .03 5038.16     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4961.84 5038.16             1214    1814    1060             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 4.356

INPUT

Description: FEMA B

Station Elevation Data    num=      61

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4287.24     730 4303.86     728 4320.82     726 4330.46     724 4366.07     722

4405.82     720  4440.1     718 4483.77     716 4506.45     714 4512.93     712

4523.81     710 4532.62     708 4562.42     706 4578.33     704 4603.23     702

4612.02     700 4621.59     698 4661.13     696 4694.37  694.36 4720.62  694.25

4749.49  694.42 4767.08     696 4779.23   696.2 4792.12     696 4794.43     694

4796.94     692  4800.7     690 4808.83     688 4816.46  687.77 4824.71     688

4834.84  688.17 4846.05     688 4850.21     688 4851.93     690 4855.07     692

4888.29     692  4893.8     690 4897.58     688 4899.86     686 4906.32     684

4910.9  683.28 4913.29   677.8 4956.29   677.4 4999.29   677.7 5001.68  684.33

5011.73     686 5026.87     688 5052.34  688.51 5076.45     688 5100.75     686

5152.07  684.95 5193.99     686 5279.71     688 5604.58     690 5646.89     692

5761.7     694 5987.59     696 6390.89     698 6481.73  698.63 6560.13     698

7415.25     696

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4287.24     .04  4910.9     .03 5001.68     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4910.9 5001.68             1870    1815    1795             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 4.072

INPUT

Description:

Station Elevation Data    num=      72

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3782.21     718 3794.38     716 3805.13     714 3814.21     712 3818.26     710

3823.65     708 3828.97     706 3844.27     704 3882.42     702 4118.48     694

4160.12  693.45  4203.6     694 4231.86  694.12  4259.9     694 4283.85  693.94

4307.24     694 4313.11     696 4363.75     696 4367.64     694 4412.17  693.49

4460.3     694 4725.52  694.91 4841.97   695.5 4865.88   695.5 4906.93     694

4912.66     692 4917.62     690 4920.98     688    4926     686 4929.62     684

4934.37  682.67 4938.41   677.2 4958.41   676.8 4978.41   677.2 5001.03  681.61

5010.15     686 5160.95  686.29 5218.62     686 5257.99  685.14 5287.14     686

5400.04  686.94 5470.45     686 5518.57  684.43  5561.6     686 5585.35     688

5601.75  688.21 5617.94     688 5639.69     686 5659.19   685.4 5679.55     686

5762.41  687.43 5840.16  687.58 5973.72     686 6014.77  684.58 6039.76     686

6114.58  687.21 6153.46  687.25 6252.51     686 6274.74  685.46 6299.27     686

6348.6     688 6427.97     690  6635.4  691.95 6786.32     694 6818.22     694

6989.1     696 7205.47     698 7334.66  698.22 7446.29     698 7592.88  697.86

7708.66     698 8079.05     696

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3782.21     .08 4934.37     .03 5001.03     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4934.37 5001.03             1600    2191    1450             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 3.729

INPUT

Description:

Station Elevation Data    num=      52

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3401.59     730 3410.77     728 3416.51     726 3420.47     724 3424.63     722

3431.87     720 3438.47     718  3443.1     716 3450.18     714 3457.86     712

3462.65     710 3470.61     708  3477.9     706 3484.69     704 3506.66     702

3533.76     700 3564.59     696 3586.82     694 3640.72     690 3803.46     688

3853.56     686 3932.81  685.39  4139.5  685.45 4291.74     686 4369.12   686.3

4437.26     686 4518.18  684.61 4829.01  684.27 4891.65     684 4957.62     682

4965.99  681.01    4969     679    4974   677.8    5000     676    5026   677.5

5031     679 5034.01  681.61 5042.38     682 5052.05     684 5064.26     686

5085.76     686 5174.04     684 5213.65     684 5240.96     684 5248.59     682

5277.71     682 5416.73     686 5752.61     688 6126.29     690  6198.9     692

6375.46     694 6616.94     696

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3401.59     .05 4965.99     .03 5034.01     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4965.99 5034.01             3115    3654    3511             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 3.157

INPUT

Description:

Station Elevation Data    num=      68

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

3107.04     730 3110.34     728 3116.91     726 3124.06     724 3128.64     722

3133.93     720 3141.25     718 3144.09     716 3151.33     714 3155.18     712

3161.26     710 3170.45     708 3176.38     706 3188.83     704 3208.23     702

3223.72     700 3231.05     698 3245.17     696 3264.26     694 3384.65     688

3562.87     686 3591.33     684 3671.32  682.98 3753.94     684 3798.73     686

3879.13  686.69  3952.5     686 4073.56  685.38 4172.65     686 4331.17  686.58

4465.36     686 4524.54     684 4555.87  683.67 4576.39     684 4620.64  684.42

4658.81     684 4675.85     682 4710.28   679.8 4744.67     682    4753   683.8

4761.4     682 4824.54  680.59 4941.94     682 4973.93     682 4998.89  680.59

5012.361   678.3 5017.36   676.3 5050.36   673.5 5085.36   676.7 5090.36   678.3

5115.17  681.49  5123.2     680 5200.63  680.24 5250.56     682 5266.21     686

5285.75     688 5587.72     690 5658.97     692 5702.26     694 5815.53     698

5852.87     702 5861.08     704  5874.6     706 5909.63     708 5948.97     712

5966.01     714 5998.27     716  6052.5     720

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

3107.04     .07 4998.89     .03 5115.17     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4998.89 5115.17             1848    1910    2000             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 2.858

INPUT

Description: FEMA A

Station Elevation Data    num=      53

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4658.37     730 4665.07     728 4682.87     726 4689.11     724 4692.61     722

4704.45     720 4732.41     718 4766.13     716 4800.58     714  4821.1     712

4836.11     710  4840.8     708 4849.98     706 4855.68     704 4860.52     702

4864.71     700 4869.17     698 4876.05     696 4882.33     694 4888.18     692

4903.15     690 4910.82     688 4916.82     686 4921.47     684 4927.52     682

4931.7     680 4937.46  679.85    4948     678    4953     676    5000   673.2

5047   676.4    5052     678 5062.54  678.65 5068.69     680 5075.43     682

5090.22     682 5139.92     680 5157.54     682 5216.32     684 5273.15     686

5302.16     688 5336.25     692 5392.98     696 5420.16     698 5430.27     700

5446.53     702 5475.38     704  5494.1     706 5514.51     710 5528.22     712

5553.35     716 5561.48     718 5573.66     720

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4658.37     .08 4937.46     .03 5062.54     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4937.46 5062.54             1431    1463    1405             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 2.629

INPUT

Description:

Station Elevation Data    num=      44

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4236.325     7204291.945     7184329.175     7164398.335     7144472.575     712

4514.915     7104559.015     7084575.225     7064589.005     7044605.275     702

4627.925     7004640.305     6984648.705     6964662.285     6944674.985     692

4698.205     6904710.165     6884724.285     6864736.075     6844907.545     682

4915.825     680 4932.81  679.19    4948   677.1    4953   675.1    5000   673.1

5047   676.3    5052   677.9 5067.19  679.195080.065     6805136.595     682

5153.955     6845179.875     6865188.945     6885198.745     6905221.295     694

5227.925     6965242.745     7005254.865     7025265.895     7045278.915     706

5298.435     7105317.855     7145331.525     7165341.925     718

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4236.325     .08 4932.81     .03 5067.19     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

4932.81 5067.19             1105    1130    1225             .1       .3

CROSS SECTION          RIVER: Contoocook River

REACH: 001                RS: 2.452

INPUT

Description: North Townline

Station Elevation Data    num=      46

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

4110.7     720 4172.29     718 4238.28     716 4272.72     714 4286.47     712

4308.81     710 4327.57     708 4362.31     706 4376.61     704 4396.89     702

4522.14     698 4627.84     692 4638.98     690 4676.26     688 4746.68     684

4790     680    4815     679 4840.03     680 4876.24  680.81 4909.96     680

4921  679.19    4946   677.9    4956   674.9    5000   674.5    5044   673.4

5079  679.19 5116.56     680 5130.79     682 5166.97  682.32 5199.87     682

5230.81   681.4 5249.97  681.37 5289.47     682 5522.88     684 5663.69     686

5671.21     688 5680.32     690 5686.85     692 5694.11     694 5701.16     696

5707.91     698  5714.8     700 5723.44     702 5733.56     704 5785.82     712

5796.36     714

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

4110.7      .1    4921     .06    5079      .1

Bank Sta: Left   Right    Coeff Contr.   Expan.

4921    5079             .1       .3

SUMMARY OF MANNING'S N VALUES

River:Contoocook River

Reach          River Sta.       n1        n2        n3

001                  12.704             .06      .037       .09

001                  12.271             .07      .037       .09

001                  11.809             .06      .037      .055

001                  11.430             .09      .037       .07

001                  11.422             .09      .037       .07

001                  11.420       Bridge

001                  11.418             .09      .037       .07

001                  11.412             .09      .037       .07

001                  11.223             .09      .037       .09

001                  11.040             .08      .035       .09

001                  10.970             .08      .035       .09

001                  10.866             .08      .035       .09

001                  10.752             .07      .035       .07

001                  10.681             .07      .033       .07

001                  10.677             .07      .033       .09

001                  10.675       Bridge

001                  10.673             .07      .033       .09

001                  10.667             .07      .033       .09

001                  10.567             .07       .03       .08

001                  10.456             .06       .03       .07

001                  10.366             .06       .03       .07

001                  10.260             .05       .03       .07

001                  10.253             .05       .03       .06

001                  10.251       Bridge

001                  10.249             .06       .03       .06

001                  10.246             .06       .03       .06

001                  10.158             .06       .03       .06

001                  10.113             .08       .03       .07

001                  10.112       Inline Weir

001                  10.111              .1       .05       .09

001                  10.110             .07       .05       .09

001                  9.958              .09      .035       .09

001                  9.925              .07      .035       .09

001                  9.847              .07      .035       .09

001                  9.840              .07      .035       .09

001                  9.838        Bridge

001                  9.836              .08      .035       .06

001                  9.827              .08      .035      .035

001                  9.685             .055      .033       .09

001                  9.495              .06      .033       .07

001                  9.132              .06      .033       .08

001                  9.126              .04      .033       .04

001                  9.122        Bridge

001                  9.117              .08      .033      .055

001                  9.112              .08      .033       .07

001                  8.807              .08       .03       .07

001                  8.513             .035       .03       .05

001                  8.500             .035       .03       .05

001                  8.499        Inline Weir

001                  8.498             .035       .03       .05

001                  8.494              .04      .032       .05

001                  8.486              .04      .032       .05

001                  8.482        Bridge

001                  8.478              .04      .032       .04

001                  8.472              .04      .032       .04

001                  8.136               .1      .032        .1

001                  7.733              .08      .032       .05

001                  7.533              .07      .032       .06

001                  7.186              .05      .032       .06

001                  6.975              .04      .032       .06

001                  6.889              .07      .032       .06

001                  6.823              .07      .032       .06

001                  6.814              .06       .03       .04

001                  6.813        Inline Weir

001                  6.811              .09       .03       .04

001                  6.785              .07       .03       .04

001                  6.766             .035       .03       .04

001                  6.765             .035       .03       .04

001                  6.749             .035       .03       .04

001                  6.748             .035       .03       .04

001                  6.736              .07       .03       .07

001                  6.258              .07       .03      .055

001                  6.110              .06       .03       .06

001                  5.748              .05       .03       .07

001                  5.256              .05       .03       .08

001                  4.953              .06       .03       .07

001                  4.817              .05       .03       .07

001                  4.640              .08       .03       .09

001                  4.356              .04       .03       .07

001                  4.072              .08       .03       .07

001                  3.729              .05       .03       .06

001                  3.157              .07       .03       .07

001                  2.858              .08       .03       .08

001                  2.629              .08       .03       .08

001                  2.452               .1       .06        .1

SUMMARY OF REACH LENGTHS

River: Contoocook River

Reach          River Sta.      Left     Channel    Right

001                  12.704            2350      2445      2400

001                  12.271            2450      2555      2500

001                  11.809            1795      2200      2270

001                  11.430            28.5      28.5      28.5

001                  11.422            45.5      45.5      45.5

001                  11.420       Bridge

001                  11.418            18.5      18.5      18.5

001                  11.412            1000       955       900

001                  11.223             880       930       970

001                  11.040             750       880       855

001                  10.970             500       540       480

001                  10.866             570       565       470

001                  10.752             460       340       225

001                  10.681              33        33        33

001                  10.677              38        38        38

001                  10.675       Bridge

001                  10.673              48        48        48

001                  10.667             360       830       450

001                  10.567             510       915       825

001                  10.456             565       625       690

001                  10.366            1100      1120      1025

001                  10.260            29.5      29.5      29.5

001                  10.253              41        41        41

001                  10.251       Bridge

001                  10.249            21.5      21.5      21.5

001                  10.246             220       225       230

001                  10.158              46       106        76

001                  10.113              20        20        20

001                  10.112       Inline Weir

001                  10.111              53        53        53

001                  10.110            1150      1075      1035

001                  9.958              230       225       212

001                  9.925              620       560       500

001                  9.847             39.5      39.5      39.5

001                  9.840               42        42        42

001                  9.838        Bridge

001                  9.836             39.5      39.5      39.5

001                  9.827              350       720       670

001                  9.685              990       950      1000

001                  9.495             1635      1760      1950

001                  9.132             17.5      17.5      17.5

001                  9.126             87.5      87.5      87.5

001                  9.122        Bridge

001                  9.117               10        10        10

001                  9.112             1375      1485      1540

001                  8.807             1430      1500      1495

001                  8.513               14        14        14

001                  8.500               14        14        14

001                  8.499        Inline Weir

001                  8.498               14        14        14

001                  8.494               20        20        20

001                  8.486               83        83        83

001                  8.482        Bridge

001                  8.478               10        10        10

001                  8.472             1880      1898      1840

001                  8.136             2050      2277      2050

001                  7.733             1125      1135      1125

001                  7.533             1555      1920      1500

001                  7.186             1580      1235      1175

001                  6.975              530       465       300

001                  6.889              525       500       500

001                  6.823               45        45        45

001                  6.814               13        13        13

001                  6.813        Inline Weir

001                  6.811              140       120       110

001                  6.785              100        74        35

001                  6.766               83        83        83

001                  6.765               83        83        83

001                  6.749               65        65        65

001                  6.748               65        65        65

001                  6.736             2930      3051      3320

001                  6.258              980       980       900

001                  6.110             2350      2420      2190

001                  5.748             3120      3143      3300

001                  5.256              692      1936      1864

001                  4.953              956       870       787

001                  4.817              729      1130      1200

001                  4.640             1214      1814      1060

001                  4.356             1870      1815      1795

001                  4.072             1600      2191      1450

001                  3.729             3115      3654      3511

001                  3.157             1848      1910      2000

001                  2.858             1431      1463      1405

001                  2.629             1105      1130      1225

001                  2.452

SUMMARY OF CONTRACTION AND EXPANSION COEFFICIENTS

River: Contoocook River

Reach          River Sta.     Contr.    Expan.

001                  12.704          .1        .3

001                  12.271          .1        .3

001                  11.809          .1        .3

001                  11.430          .3        .5

001                  11.422          .3        .5

001                  11.420   Bridge

001                  11.418          .3        .5

001                  11.412          .1        .3

001                  11.223          .1        .3

001                  11.040          .1        .3

001                  10.970          .1        .3

001                  10.866          .1        .3

001                  10.752          .1        .3

001                  10.681          .3        .5

001                  10.677          .3        .5

001                  10.675   Bridge

001                  10.673          .3        .5

001                  10.667          .1        .3

001                  10.567          .1        .3

001                  10.456          .1        .3

001                  10.366          .1        .3

001                  10.260          .3        .5

001                  10.253          .3        .5

001                  10.251   Bridge

001                  10.249          .3        .5

001                  10.246          .1        .3

001                  10.158          .3        .5

001                  10.113          .3        .5

001                  10.112   Inline Weir

001                  10.111          .3        .5

001                  10.110          .1        .3

001                  9.958           .1        .3

001                  9.925           .1        .3

001                  9.847           .3        .5

001                  9.840           .3        .5

001                  9.838    Bridge

001                  9.836           .3        .5

001                  9.827           .1        .3

001                  9.685           .1        .3

001                  9.495           .1        .3

001                  9.132           .3        .5

001                  9.126           .3        .5

001                  9.122    Bridge

001                  9.117           .3        .5

001                  9.112           .1        .3

001                  8.807           .1        .3

001                  8.513           .3        .5

001                  8.500           .3        .5

001                  8.499    Inline Weir

001                  8.498           .3        .5

001                  8.494           .3        .5

001                  8.486           .3        .5

001                  8.482    Bridge

001                  8.478           .3        .5

001                  8.472           .1        .3

001                  8.136           .1        .3

001                  7.733           .1        .3

001                  7.533           .1        .3

001                  7.186           .1        .3

001                  6.975           .1        .3

001                  6.889           .1        .3

001                  6.823           .3        .5

001                  6.814           .3        .5

001                  6.813    Inline Weir

001                  6.811           .3        .5

001                  6.785           .1        .3

001                  6.766           .1        .3

001                  6.765           .1        .3

001                  6.749           .1        .3

001                  6.748           .1        .3

001                  6.736           .1        .3

001                  6.258           .1        .3

001                  6.110           .1        .3

001                  5.748           .1        .3

001                  5.256           .1        .3

001                  4.953           .1        .3

001                  4.817           .1        .3

001                  4.640           .1        .3

001                  4.356           .1        .3

001                  4.072           .1        .3

001                  3.729           .1        .3

001                  3.157           .1        .3

001                  2.858           .1        .3

001                  2.629           .1        .3

001                  2.452           .1        .3