HEC-RAS September 1998 Version 2.2

U.S. Army Corp of Engineers

Hydrologic Engineering Center

609 Second Street, Suite D

Davis, California 95616-4687

(916) 756-1104

X     X  XXXXXX    XXXX        XXXX       XX      XXXX

X     X  X        X    X       X   X     X  X    X

X     X  X        X            X   X    X    X   X

XXXXXXX  XXXX     X       XXX  XXXX     XXXXXX    XXXX

X     X  X        X            X  X     X    X        X

X     X  X        X    X       X   X    X    X        X

X     X  XXXXXX    XXXX        X    X   X    X   XXXXX

PROJECT DATA

Project Title: Peterborough 1979 FIS Import - NubMulti

Project File : 79NubM.prj

Run Date and Time: 12/13/00 2:21:28 PM

Project in English units

Project Description:

PETERBOROUGH, NH                     FLOOD INSURANCE STUDY

ANDERSON-NICHOLS  1979 FIS  2860-11  SFC ENGINEERING PARTNERSHIP

NUBANUSIT BROOK MULTIPLE RUN

1979 PETERBOROUGH NH FIS (HEC2 IMPORT)

Nubanusit Brook

Direct 1979 RAS Import 01:

-Converted dams from HEC2 bridges to Inline Weirs

-Adjusted bridge modeling parameters to match Duplicate HEC2

PLAN DATA

Plan Title: Imported Plan 01

Plan File : d:\My Documents\H&H\Pboro\NubRAS\79NubM.p01

Geometry Title: Imported Geom 01

Geometry File : d:\My Documents\H&H\Pboro\NubRAS\79NubM.g01

Flow Title    : Imported Flow 01

Flow File     : d:\My Documents\H&H\Pboro\NubRAS\79NubM.f01

Plan Summary Information:

Number of:  Cross Sections =   65    Mulitple Openings =    0

Culverts       =    0    Inline Weirs      =    5

Bridges        =    5

Computational Information

Water surface calculation tolerance =  0.01

Critical depth calculaton tolerance =  0.01

Maximum number of interations       =  20

Maximum difference tolerance        =  0.3

Flow tolerance factor               =  0.001

Computation Options

Critical depth computed only where necessary

Conveyance Calculation Method: At breaks in n values only

Friction Slope Method:         Average Conveyance

Computational Flow Regime:     Subcritical Flow

Encroachment Data

Equal Conveyance = True

Left Offset      =        0

Right Offset     =        0

River = RIVER-1          Reach = Reach-1

RS      Profile           Method  Value1  Value2

1       PF 6                   1   964.2  1025.3

2       PF 6                   1   964.2  1025.3

3       PF 6                   1   965.2  1025.1

4       PF 6                   1     965  1024.4

5       PF 6                   1     974    1020

6       PF 6                   1   976.7  1024.1

6.5     PF 6                   0

7       PF 6                   1   976.7  1024.1

8       PF 6                   1   976.7  1027.1

9       PF 6                   1   969.9 1030.02

10      PF 6                   1   969.9  1030.1

10.5    PF 6                   0

11      PF 6                   1   969.9  1030.1

12      PF 6                   1   969.9  1030.1

13      PF 6                   1   961.9  1029.6

14      PF 6                   1     959  1041.2

15      PF 6                   1     978    1022

16      PF 6                   1     971    1029

17      PF 6                   1     941    1013

18      PF 6                   1   948.4  1051.6

18.5    PF 6                   0

19      PF 6                   1   948.4  1051.6

20      PF 6                   1   948.4  1051.6

21      PF 6                   1     938    1058

22      PF 6                   1     955    1040

23      PF 6                   1     962    1028

24      PF 6                   1     980    1007

25      PF 6                   1     965    1025

26      PF 6                   1   959.5  1052.7

26.5    PF 6                   0

27      PF 6                   1   959.5  1052.7

28      PF 6                   1     935    1065

29      PF 6                   1     935    1065

30      PF 6                   1     947    1065

31      PF 6                   1     988  1012.1

32      PF 6                   1   982.2  1017.8

33      PF 6                   1   982.2  1017.8

34      PF 6                   1   982.2  1017.8

34.5    PF 6                   0

35      PF 6                   1   982.2  1017.8

36      PF 6                   1     981  1027.1

37      PF 6                   1   981.1    1024

38      PF 6                   1  916.48    1009

39      PF 6                   1  1933.5  2096.3

40      PF 6                   1     970    1030

41      PF 6                   1    1955 2019.58

42      PF 6                   1     973    1012

43      PF 6                   1   969.9  1030.1

43.5    PF 6                   0

44      PF 6                   1   969.9  1030.1

45      PF 6                   1     988    1012

46      PF 6                   1     987    1016

47      PF 6                   1     976    1026

48      PF 6                   1     966    1034

49      PF 6                   1     990    1005

50      PF 6                   1     974    1028

51      PF 6                   1   966.9  1032.1

51.5    PF 6                   0

52      PF 6                   1   966.9  1032.1

53      PF 6                   1   964.9  1034.1

54      PF 6                   1   964.9  1035.1

54.5    PF 6                   0

55      PF 6                   1   964.9  1035.1

56      PF 6                   1     932  1068.2

57      PF 6                   1     932  1068.2

58      PF 6                   1     984    1018

59      PF 6                   1     940  1035.1

59.5    PF 6                   0

60      PF 6                   1     940  1035.1

61      PF 6                   1     940    1028

62      PF 6                   1     984    1045

62.5    PF 6                   0

63      PF 6                   1     984    1045

64      PF 6                   1     900    1020

65      PF 6                   1     985    1050

FLOW DATA

Flow Title: Imported Flow 01

Flow File : d:\My Documents\H&H\Pboro\NubRAS\79NubM.f01

Flow Data (cfs)

River           Reach           RS                   PF 1            PF 2            PF 3            PF 4            PF 5            PF 6

RIVER-1         Reach-1         65                    650             700             800             900             800             800

RIVER-1         Reach-1         56                    300             350             450             550             450             450

RIVER-1         Reach-1         53                    650             700             800             900             800             800

Boundary Conditions

River           Reach           Profile                       Upstream                 Downstream

RIVER-1         Reach-1         PF 1                                               Known WS = 715.31

RIVER-1         Reach-1         PF 2                                               Known WS = 715.46

RIVER-1         Reach-1         PF 3                                               Known WS = 715.78

RIVER-1         Reach-1         PF 4                                               Known WS = 716.12

RIVER-1         Reach-1         PF 5                                               Known WS = 715.78

RIVER-1         Reach-1         PF 6                                               Known WS = 716.78

GEOMETRY DATA

Geometry Title: Imported Geom 01

Geometry File : d:\My Documents\H&H\Pboro\NubRAS\79NubM.g01

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 65

INPUT

Description: 3.409

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

798.8   926.6   824.4   917.1     846   913.5   868.4   912.9   905.6   899.2

942   894.9   942.1   889.1     943   887.6     980     885    1000   883.8

1020   884.6    1055   886.3    1058   889.1  1102.2   900.5  1102.3   900.5

1120   909.9  1143.6   916.5  1170.8     926    1182   936.7  1215.6   936.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

798.8      .1     980     .05    1020      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

980    1020              730     915     980             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 64

INPUT

Description: 3.235

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

822   877.5   849.6   876.9   849.7   876.9   849.8   876.9   849.9   876.9

900   862.4     980   860.6     982   859.6    1000     858    1017   858.6

1020   860.6    1044   875.1    1053   874.9  1053.1   874.9  1053.2   874.9

1079     879  1152.6   880.2  1203.4   882.3  1231.8   884.7  1231.9   884.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

822     .08     900     .04    1020      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

900    1020               37      42      47             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 63

INPUT

Description: 3.225

This is a REPEATED section.

Station Elevation Data    num=      19

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

800   880.6     852   878.9     947   866.2   947.1   866.2   955.3   865.4

955.4   865.4     975   863.4     984     862   985.7   861.9  1008.2   860.9

1017.6   860.9    1029   857.7  1034.7   857.7  1042.5   861.2    1045   861.9

1045.1   861.9    1064   868.6  1064.1   868.6    1090   875.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

800     .08     984     .04  1045.1     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

984  1045.1             21.5    21.5    21.5             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

800     984   877.1  1045.1    1090   875.7

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 62.5

INPUT

Description: Bridge #10

Distance from Upstream XS =       0

Deck/Roadway Width        =    21.5

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      11

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

800   880.6       0     852   878.9       0     947   877.1       0

947.1   878.1       0   955.3     878       0   955.4     879   875.8

1045   878.5   875.2  1045.1   878.5       0    1064   878.4       0

1064.1   877.3       0    1090   875.7       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      19

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

800   880.6     852   878.9     947   866.2   947.1   866.2   955.3   865.4

955.4   865.4     975   863.4     984     862   985.7   861.9  1008.2   860.9

1017.6   860.9    1029   857.7  1034.7   857.7  1042.5   861.2    1045   861.9

1045.1   861.9    1064   868.6  1064.1   868.6    1090   875.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

800     .08     984     .04  1045.1     .08

Bank Sta: Left   Right    Coeff Contr.   Expan.

984  1045.1             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

800     984   877.1  1045.1    1090   875.7

Downstream  Deck/Roadway Coordinates

num=      11

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

800   880.6       0     852   878.9       0     947   877.1       0

947.1   878.1       0   955.3     878       0   955.4     879   875.8

1045   878.5   875.2  1045.1   878.5       0    1064   878.4       0

1064.1   877.3       0    1090   875.7       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      19

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

800   880.2     852   878.5     947   865.8   947.1   865.8   955.3     865

955.4     865     975     863     984   861.6   985.7   861.5  1008.2   860.5

1017.6   860.5    1029   857.3  1034.7   857.3  1042.5   860.8    1045   861.5

1045.1   861.5    1064   868.2  1064.1   868.2    1090   875.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

800     .08     984     .04  1045.1     .08

Bank Sta: Left   Right    Coeff Contr.   Expan.

984  1045.1             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

800     984   875.8  1045.1    1090   875.2

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   875.7

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Piers =  1

Pier Data

Pier Station     Upstream= 1014.55    Downstream= 1014.55

Upstream     num=       2

Width   Elev    Width   Elev

15   857.7      15   875.8

Downstream     num=       2

Width   Elev    Width   Elev

15   857.3      15   875.8

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Yarnell                KVal =    1.25

Selected Low Flow Methods = Yarnell

High Flow Method

Energy Only

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 62

INPUT

Description: 3.221

Station Elevation Data    num=      19

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

800   880.2     852   878.5     947   865.8   947.1   865.8   955.3     865

955.4     865     975     863     984   861.6   985.7   861.5  1008.2   860.5

1017.6   860.5    1029   857.3  1034.7   857.3  1042.5   860.8    1045   861.5

1045.1   861.5    1064   868.2  1064.1   868.2    1090   875.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

800     .08     984     .04  1045.1     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

984  1045.1               10      10      10             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

800     984   875.8  1045.1    1090   875.2

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 61

INPUT

Description: 3.219

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

614.4   899.2   638.4   891.5   693.6   884.4   739.6   878.4     866   876.9

880   876.6     916   876.2     940   861.2     974   859.8     977   858.5

1000   862.8    1020   857.2    1026   859.8    1050   875.7    1080   875.2

1104.4     876    1148   878.1  1210.4   877.8  1274.4   879.9    1340   884.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

614.4     .08     940     .04    1026     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

940    1026               15      20      30             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 60

INPUT

Description: 3.215

This is a REPEATED section.

Station Elevation Data    num=       9

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

870   876.6     904   876.2     915   870.6     924   865.5   924.1   865.5

940   857.5    1000     857    1035   857.5  1035.1   873.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

870     .08     940     .04  1035.1     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

940  1035.1                9       9       9             .2       .4

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

870     940   870.4  1035.1  1035.1   867.4

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 59.5

INPUT

Description: Bridge #9

Distance from Upstream XS =       0

Deck/Roadway Width        =       9

Weir Coefficient          =       3

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=       8

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

870   876.6       0     904   876.2       0     915   870.6       0

924   870.5       0   924.1   870.5   865.5    1000   868.9   863.9

1035   867.4   862.4  1035.1   873.2       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=       9

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

870   876.6     904   876.2     915   870.6     924   865.5   924.1   865.5

940   857.5    1000     857    1035   857.5  1035.1   873.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

870     .08     940     .04  1035.1     .08

Bank Sta: Left   Right    Coeff Contr.   Expan.

940  1035.1             .2       .4

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

870     940   870.4  1035.1  1035.1   867.4

Downstream  Deck/Roadway Coordinates

num=       8

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

870   876.6       0     904   876.2       0     915   870.6       0

924   870.5       0   924.1   870.5   865.5    1000   868.9   863.9

1035   867.4   862.4  1035.1   873.2       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=       9

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

870   876.6     904   876.2     915   870.6     924   865.5   924.1   865.5

940   857.5    1000     857    1035   857.5  1035.1   873.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

870     .09     940     .04  1035.1     .08

Bank Sta: Left   Right    Coeff Contr.   Expan.

940  1035.1             .2       .4

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

870     940   865.4  1035.1  1035.1   862.4

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   867.4

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Piers =  1

Pier Data

Pier Station     Upstream=  987.55    Downstream=  987.55

Upstream     num=       2

Width   Elev    Width   Elev

18     857      18   865.4

Downstream     num=       2

Width   Elev    Width   Elev

18     857      18   865.4

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Yarnell                KVal =    1.25

Selected Low Flow Methods = Yarnell

High Flow Method

Energy Only

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 59

INPUT

Description: 3.213

Station Elevation Data    num=       9

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

870   876.6     904   876.2     915   870.6     924   865.5   924.1   865.5

940   857.5    1000     857    1035   857.5  1035.1   873.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

870     .09     940     .04  1035.1     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

940  1035.1              460     375     300             .2       .4

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

870     940   865.4  1035.1  1035.1   862.4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 58

INPUT

Description: 3.142

Station Elevation Data    num=      17

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

911     875     922     870     941     865     957     860     965     855

980     854     983     851     987     848    1000     847  1017.5     848

1020     851  1022.5     854    1050     855    1150     860    1200     865

1269     870    1338     875

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

911     .06     987    .035  1017.5     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

987  1017.5              440     440     440             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 57

INPUT

Description: 3.059

This is a REPEATED section.

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

765.2   869.4   803.2   868.6   839.6   861.1   869.6   852.6   869.7   852.6

900   852.6     932   852.9   932.1   850.5     935   847.9     970   841.5

1000     842    1030   841.5    1068   849.7  1068.1   850.5  1068.2   852.7

1138   855.2  1138.1   855.2  1138.2   855.2  1138.3   855.2  1138.4   855.2

1169.2   852.5  1206.4   857.6  1251.6   859.3  1293.6   867.1    1346   875.1

1385.6   879.6  1415.2   880.7  1415.3   880.7  1415.4   880.7  1415.5   880.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

765.2     .06     932     .03  1068.2     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

932  1068.2               45      45      45             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 56

INPUT

Description: 3.051

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

765.2   869.2   803.2   868.4   839.6   860.9   869.6   852.4   869.7   852.4

900   852.4     932   852.7   932.1   850.3     935   847.7     970   841.3

1000   841.8    1030   841.3    1068   849.5  1068.1   850.3  1068.2   852.5

1138     855  1138.1     855  1138.2     855  1138.3     855  1138.4     855

1169.2   852.3  1206.4   857.4  1251.6   859.1  1293.6   866.9    1346   874.9

1385.6   879.4  1415.2   880.5  1415.3   880.5  1415.4   880.5  1415.5   880.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

765.2     .07     932     .03  1068.2     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

932  1068.2                2       2       2             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 55

INPUT

Description: 3.051

This is a REPEATED section.

Station Elevation Data    num=       8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

915   859.5     942   852.5   964.9   852.4     965   849.2    1035   849.2

1035.1   852.7    1080   853.4    1150   857.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

915     .07   964.9    .035  1035.1     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

964.9  1035.1              1.5     1.5     1.5             .1       .3

INLINE WEIR            RIVER: RIVER-1

REACH: Reach-1            RS: 54.5

INPUT

Description:

Distance from Upstream XS =       0

Deck/Roadway Width        =     1.5

Weir Coefficient          =       3

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =        8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

915   859.5     942   852.5   964.9   852.4     965   849.2    1035   849.2

1035.1   852.7    1080   853.4    1150   857.5

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   849.2

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 54

INPUT

Description: 3.05

Station Elevation Data    num=       8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

915   859.5     942   852.5   964.9   852.4     965   849.2    1035   849.2

1035.1   852.7    1080   853.4    1150   857.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

915     .07   964.9    .035  1035.1     .03

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

964.9  1035.1                1       1       1             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 53

INPUT

Description: 3.05

Station Elevation Data    num=       8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

915   859.5     942   852.5   964.9   852.4     965   838.7    1035   838.7

1035.1   852.7    1080   853.4    1150   857.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

915     .07   964.9    .035  1035.1     .03

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

964.9  1035.1                7       7       7             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 52

INPUT

Description: 3.049

This is a REPEATED section.

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

900   850.8   966.9   851.6     967   838.5     972   838.5     982   838.5

992   838.5     997   838.5    1006   838.5    1011   838.5    1018   838.5

1025   838.5    1032   838.5  1032.1   853.6    1152   856.7    1222     863

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

900     .02   966.9    .035  1032.1     .02

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

966.9  1032.1             47.2    47.2    47.2             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

900   966.9   849.8  1032.1    1222   852.6

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 51.5

INPUT

Description: Bridge #7

Distance from Upstream XS =       0

Deck/Roadway Width        =    47.2

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      15

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

900   850.8       0   966.9   851.6       0     967   854.1   846.1

972   854.2   846.9     982   854.5   848.2     992   854.8   849.2

997     855   849.5    1006   855.3   849.5    1011   855.5   849.3

1018   855.7     849    1025   855.9   848.5    1032   856.1   847.8

1032.1   853.6       0    1152   856.7       0    1222     863       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

900   850.8   966.9   851.6     967   838.5     972   838.5     982   838.5

992   838.5     997   838.5    1006   838.5    1011   838.5    1018   838.5

1025   838.5    1032   838.5  1032.1   853.6    1152   856.7    1222     863

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

900     .02   966.9    .035  1032.1     .02

Bank Sta: Left   Right    Coeff Contr.   Expan.

966.9  1032.1             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

900   966.9   849.8  1032.1    1222   852.6

Downstream  Deck/Roadway Coordinates

num=      15

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

900   850.8       0   966.9   851.6       0     967   854.1   846.1

972   854.2   846.9     982   854.5   848.2     992   854.8   849.2

997     855   849.5    1006   855.3   849.5    1011   855.5   849.3

1018   855.7     849    1025   855.9   848.5    1032   856.1   847.8

1032.1   853.6       0    1152   856.7       0    1222     863       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

900   849.8   966.9   850.6     967   837.5     972   837.5     982   837.5

992   837.5     997   837.5    1006   837.5    1011   837.5    1018   837.5

1025   837.5    1032   837.5  1032.1   852.6    1152   855.7    1222     862

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

900     .09   966.9     .05  1032.1     .07

Bank Sta: Left   Right    Coeff Contr.   Expan.

966.9  1032.1             .2       .4

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

900   966.9   849.5  1032.1    1222   849.5

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   849.8

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =    1.16

Selected Low Flow Methods = Energy

High Flow Method

Energy Only

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 51

INPUT

Description: 3.04

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

900   849.8   966.9   850.6     967   837.5     972   837.5     982   837.5

992   837.5     997   837.5    1006   837.5    1011   837.5    1018   837.5

1025   837.5    1032   837.5  1032.1   852.6    1152   855.7    1222     862

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

900     .09   966.9     .05  1032.1     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

966.9  1032.1               32      32      32             .2       .4

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

900   966.9   849.5  1032.1    1222   849.5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 50

INPUT

Description: 3.034

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

628.4   866.8   657.2   869.7   694.4   869.4   729.6   851.6     800   843.3

836   843.3   865.2   843.6   892.8   843.8   897.6   843.8   897.7   843.8

906   843.5     956   843.5     974   836.9     978   834.9    1000   836.6

1021   832.8    1026   836.9    1028   837.8  1028.1   837.8  1028.2   837.8

1062.4   846.5  1105.6   848.3  1142.8   844.5    1174   846.5    1210   854.6

1248.4   858.1  1276.4   863.2  1297.6   871.2  1328.4   875.7  1360.4   878.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

628.4      .1     974     .05    1028      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

974    1028              450     495     540             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 49

INPUT

Description: 2.94

Station Elevation Data    num=      13

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

950     835     955     830     960     825     980     820     990     816

993.5   814.6    1000   814.5    1004   814.6    1005     816    1028     820

1045     825    1060     830    1097     835

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

950     .08     990     .04    1005      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

990    1005              480     480     480             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 48

INPUT

Description: 2.849

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

446     829   475.2   829.6     538   826.9   590.4   824.8     652     821

681.6   820.4   708.8   820.4   764.4   817.4   830.4   817.7     878   816.2

916   807.8     956   808.8     966   805.8     968   805.2    1000   804.3

1022   803.3    1034   805.8    1046   817.8  1046.1   817.8  1046.2   817.8

1093.6   825.4  1169.2   850.4  1169.3   850.4  1169.4   850.4  1169.5   850.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

446     .08     966    .033    1034      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

966    1034             1895    2342    1820             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 47

INPUT

Description: 2.406

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

687.2   833.5     706   827.5   726.4   821.3   767.6   817.7   803.6   815.3

842.4   811.5   886.4   812.4   915.6   811.5   916.1   811.5   916.2   811.5

933   811.6     959   808.9     974   801.6     978   798.6    1000   795.5

1026   799.8    1028   801.6    1082   804.7  1082.1   804.7  1082.2   804.7

1126.6   804.8  1153.8   804.9  1215.8   804.6    1303     804  1388.2   804.9

1518.2   807.3  1578.6   807.6  1662.2   805.8  1757.4   806.7  1836.6   808.5

1911   812.1  1984.2   814.4  2065.4   821.9  2149.8   828.4  2225.4   836.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

687.2     .08     978    .033    1026     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

978    1026             1620    2390    2060             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 46

INPUT

Description: 1.961

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

855     810     868     805     920     800     965     795     987   791.5

989   788.6    1000   788.4    1011   788.5    1016   791.5    1038     795

1075     800    1230     805

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

855     .09     987     .03    1016     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

987    1016              520     530     525             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 45

INPUT

Description: 1.862

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

753.6   804.9   786.4   808.2     824   807.3   871.6   805.8   898.4   798.7

928   798.8     988   789.5     990   787.5    1000   783.3    1008   787.5

1012   789.5    1056   803.7  1056.1   803.7  1056.2   803.7  1056.3   803.7

1095.2   810.9  1132.8   814.7  1180.8     815  1258.8   815.9  1318.8   815.9

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

753.6     .09     988    .035    1012     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

988    1012               45      45      45             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 44

INPUT

Description: 1.856

This is a REPEATED section.

Station Elevation Data    num=      32

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

884.5   802.2     901   797.5     916   797.8     942     799   952.3   795.2

962.9   789.7     965   788.8   969.9   787.7     970   787.6     974   787.4

980   787.6     983   787.6     987   787.3     991   786.3    1000     783

1006   785.7    1009   786.2    1012   787.7    1019   788.1    1026     788

1030   788.1  1030.1   788.1    1034   788.2    1038   788.7    1042   789.7

1046   791.7  1050.8   795.2    1054   797.8  1058.8   800.2  1061.5   801.2

1115.8   802.5    1121   805.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

884.5     .07   969.9    .035  1030.1     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

969.9  1030.1            16.33   16.33   16.33             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

884.5   969.9   797.3  1030.1    1121   800.2

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 43.5

INPUT

Description: Bridge #6

Distance from Upstream XS =       0

Deck/Roadway Width        =   16.33

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      11

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

884.7     802       0     901   797.5       0     916   797.8       0

942     799       0   969.9     800       0     970   800.6   796.3

1030   800.7   796.5  1030.1   800.2       0  1061.5   801.2       0

1115.8   802.5       0    1121   805.2       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      32

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

884.5   802.2     901   797.5     916   797.8     942     799   952.3   795.2

962.9   789.7     965   788.8   969.9   787.7     970   787.6     974   787.4

980   787.6     983   787.6     987   787.3     991   786.3    1000     783

1006   785.7    1009   786.2    1012   787.7    1019   788.1    1026     788

1030   788.1  1030.1   788.1    1034   788.2    1038   788.7    1042   789.7

1046   791.7  1050.8   795.2    1054   797.8  1058.8   800.2  1061.5   801.2

1115.8   802.5    1121   805.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

884.5     .07   969.9    .035  1030.1     .07

Bank Sta: Left   Right    Coeff Contr.   Expan.

969.9  1030.1             .1       .3

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

884.5   969.9   797.3  1030.1    1121   800.2

Downstream  Deck/Roadway Coordinates

num=      11

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

884.7     802       0     901   797.5       0     916   797.8       0

942     799       0   969.9     800       0     970   800.6   796.3

1030   800.7   796.5  1030.1   800.2       0  1061.5   801.2       0

1115.8   802.5       0    1121   805.2       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      32

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

884.5     802     901   797.3     916   797.6     942   798.8   952.3     795

962.9   789.5     965   788.6   969.9   787.5     970   787.4     974   787.2

980   787.4     983   787.4     987   787.1     991   786.1    1000   782.8

1006   785.5    1009     786    1012   787.5    1019   787.9    1026   787.8

1030   787.9  1030.1   787.9    1034     788    1038   788.5    1042   789.5

1046   791.5  1050.8     795    1054   797.6  1058.8     800  1061.5     801

1115.8   802.3    1121     805

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

884.5     .09   969.9    .035  1030.1     .08

Bank Sta: Left   Right    Coeff Contr.   Expan.

969.9  1030.1             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

884.5   969.9   796.3  1030.1    1121   796.5

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   797.3

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =    1.15

Selected Low Flow Methods = Energy

High Flow Method

Energy Only

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 43

INPUT

Description: 1.853

Station Elevation Data    num=      32

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

884.5     802     901   797.3     916   797.6     942   798.8   952.3     795

962.9   789.5     965   788.6   969.9   787.5     970   787.4     974   787.2

980   787.4     983   787.4     987   787.1     991   786.1    1000   782.8

1006   785.5    1009     786    1012   787.5    1019   787.9    1026   787.8

1030   787.9  1030.1   787.9    1034     788    1038   788.5    1042   789.5

1046   791.5  1050.8     795    1054   797.6  1058.8     800  1061.5     801

1115.8   802.3    1121     805

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

884.5     .09   969.9    .035  1030.1     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

969.9  1030.1               58      58      58             .3       .5

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

884.5   969.9   796.3  1030.1    1121   796.5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 42

INPUT

Description: 1.842

Station Elevation Data    num=       9

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

925     800     945     795     965     790     978   788.3    1000   782.2

1012   788.3    1025     790    1038     795    1062     800

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

925     .09     978    .035    1012     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

978    1012              405     390     390             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 41

INPUT

Description: 1.776

Station Elevation Data    num=      18

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1775     800    1810     795    1955     790    1973     787    1985     783

2000     782    2012     783    2025     787    2055     790    2075   790.4

2118   789.5    2140     790    2340     792    2620   789.1    2923   788.6

3200     790    3260     795    3300     800

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1775     .09    1985     .03    2012     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1985    2012             1110    1165    1010             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 40

INPUT

Description: 1.559

Station Elevation Data    num=      40

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

510.4   792.4   598.4   791.8     668   790.9   763.2   790.3   809.2   789.5

848     788   888.8   784.4     900   783.8   902.2   783.8   906.1   783.8

908   782.6     968   783.1     970   782.5     975   780.5    1000   775.5

1025   780.3    1030     782    1080     782  1080.1     782  1080.2     782

1115.5     782    1225     782  1329.1     782  1446.7     782  1602.7     782

1705.9     782  1729.9     782  1817.1     782  1905.5     782  2033.9     782

2086.7     782  2157.9   782.6  2262.7   784.4  2307.1     785  2457.9   785.3

2513.5     790  2574.3   796.9  2622.3   806.7  2674.3   811.5  2713.9   816.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

510.4      .1     970     .03    1030      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

970    1030             3180    3530    2500             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 39

INPUT

Description: 0.898

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

1215.2   790.9  1246.8   787.4    1404   786.8  1634.8   784.7  1772.4   783.5

1790.4   779.9    1868   779.9  1868.1   779.9  1868.2   779.9  1868.3   779.9

1900   779.1    1980   778.9    1984   776.4    2000   772.9    2016   775.9

2020   778.9    2060     779  2060.1     779  2060.2     779  2060.3     779

2090.7     779  2173.1     779  2225.5   779.6  2265.1   789.7  2305.1   792.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

1215.2     .07    1980     .03    2020     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

1980    2020             1700    1950    1540             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 38

INPUT

Description: 0.531

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

412     800     460     795     540     790     640     785     720     780

990   778.5     993   775.8    1000   774.2    1006   775.9    1009   778.5

1040     779    1068     785    1150     790    1205     795    1250     800

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

412     .09     990     .03    1009     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

990    1009              750     700     630             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 37

INPUT

Description: 0.402

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

975     795   975.1   781.5     981     781   981.1   777.1    1000   774.7

1017   776.7    1019   777.1    1027   778.8  1027.1   783.8    1043   791.6

1063   791.5    1094   793.9    1124   794.5    1140   799.6    1163   798.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

975     .08   981.1     .03    1019      .1

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

981.1    1019               45      45      45             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 36

INPUT

Description: 0.393

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

968.5     795   968.6     781     981     781   981.1     776    1000     773

1017   776.7    1027     778  1027.1     783    1043   791.6    1063   791.5

1095     794    1124   794.5    1140   799.6    1163   798.4    1204   803.7

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

968.5     .08     981     .03  1027.1     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

981  1027.1                1       1       1             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 35

INPUT

Description: 0.393

This is a REPEATED section.

Station Elevation Data    num=       4

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

982.2   784.6  982.25   774.8 1017.75   774.8  1017.8   787.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

982.2     .06   982.2     .03  1017.8     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

982.2  1017.8               .5      .5      .5             .1       .3

INLINE WEIR            RIVER: RIVER-1

REACH: Reach-1            RS: 34.5

INPUT

Description:

Distance from Upstream XS =       0

Deck/Roadway Width        =      .5

Weir Coefficient          =       3

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =        4

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

982.2     782  982.25   774.8 1017.75   774.8  1017.8   784.5

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   774.8

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 34

INPUT

Description: 0.393

This is a REPEATED section.

Station Elevation Data    num=       4

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

982.2   784.6  982.25   774.8 1017.75   774.8  1017.8   787.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

982.2     .06   982.2     .02  1017.8     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

982.2  1017.8                1       1       1             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 33

INPUT

Description: 0.393

This is a REPEATED section.

Station Elevation Data    num=       4

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

982.2     783  982.25   773.2 1017.75   773.2  1017.8   785.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

982.2     .06   982.2     .02  1017.8     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

982.2  1017.8               33      33      33             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 32

INPUT

Description: 0.386

Station Elevation Data    num=       4

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

982.2     782  982.25   772.2 1017.75   772.2  1017.8   784.5

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

982.2     .07   982.2     .02  1017.8     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

982.2  1017.8               45      45      45             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 31

INPUT

Description: 0.378

Station Elevation Data    num=       5

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

988     800   988.1   770.3    1000     770    1012   770.3  1012.1     800

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

988     .07     988     .03  1012.1     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

988  1012.1              130     110     100             .5       .7

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 30

INPUT

Description: 0.358

Station Elevation Data    num=       8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

947     790   947.5   770.1    1000     769  1047.5   770.5    1065     775

1095     780    1110     785    1130     790

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

947     .07     947     .03    1065     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

947    1065              190     148      95             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 29

INPUT

Description: 0.329

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

769.6   801.3   799.2   798.1     820   784.4   859.2   781.7   874.8   779.6

900   776.8     935   776.9   935.1     774   935.2   768.6     975   767.2

1000     772    1030   772.1    1055     770    1065     774    1085   781.8

1103.2   783.5  1147.2   788.9    1208     790  1265.6   790.6    1322     796

1338.4   801.1  1396.4     807    1432   808.2    1468   808.8  1468.1   808.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

769.6     .07     935     .03    1065     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

935    1065               53      53      53             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 28

INPUT

Description: 0.319

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

769.6   801.3   799.2   798.1     820   784.4   859.2   781.7   874.8   779.6

900   776.8     935   776.9   935.2   767.6     975   766.2    1000     771

1030   771.1    1054     769    1065     773    1085   781.8    1103   783.5

1147   788.9    1208     790    1266   790.6    1332     796    1338   801.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

769.6     .06     935     .03    1065     .06

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

935    1065                5       5       5             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 27

INPUT

Description: 0.318

This is a REPEATED section.

Station Elevation Data    num=       8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

899.5     810   899.6   776.3   959.5   776.3   959.7   773.2  1040.6   773.2

1040.7   774.6  1052.7   774.6    1068     782

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

899.5     .06   959.5     .02  1052.7     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

959.5  1052.7                2       2       2             .3       .5

INLINE WEIR            RIVER: RIVER-1

REACH: Reach-1            RS: 26.5

INPUT

Description:

Distance from Upstream XS =       0

Deck/Roadway Width        =       2

Weir Coefficient          =    3.35

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =        8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

899.5     810   899.6   776.3   959.5   776.3   959.7   773.2  1040.6   773.2

1040.7   774.6  1052.7   774.6    1068     782

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   773.2

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 26

INPUT

Description: 0.318

Station Elevation Data    num=       8

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

899.5     810   899.6   776.3   959.5   776.3   959.7   773.2  1040.6   773.2

1040.7   774.6  1052.7   774.6    1068     782

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

899.5     .06   959.5     .06  1052.7     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

959.5  1052.7               25      25      25             .3       .5

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 25

INPUT

Description: 0.313

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

899.5     810   899.6   776.3   959.5   776.3   959.7   762.5     970   761.8

980   761.2     990   760.2    1000   758.7    1010   759.1    1020     761

1030     763    1040     767    1050   773.3    1060   778.5    1068     782

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

899.5      .1     970     .06    1020     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

970    1020               30      15       5             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 24

INPUT

Description: 0.31

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

802.4   802.5     848   802.8     874   797.5   903.2   785.6     922   784.1

955   775.2     975   775.9     980   746.7    1000   746.2    1002   746.8

1020   755.7    1030   756.1    1040     758    1059   759.9    1125   760.6

1126   760.6  1179.6   764.8  1236.4   769.2  1325.2   770.4  1372.8   775.5

1419.6   781.4  1449.6   786.8    1492   793.3  1558.4   796.6  1607.6   798.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

802.4      .1     980    .035    1002     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

980    1002              165     155     150             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 23

INPUT

Description: 0.28

This is a REPEATED section.

Station Elevation Data    num=       7

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

945     755     955     750     962   747.5    1000     744    1026   747.5

1040     750    1045     755

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

945     .09     962     .04    1026     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

962    1026              125     125     125             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 22

INPUT

Description: 0.257

Station Elevation Data    num=       7

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

945   751.8     955   746.8     962   744.3    1000   740.8    1026   744.3

1040   746.8    1045   751.8

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

945     .09     962     .04    1026     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

962    1026              110     110     110             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 21

INPUT

Description: 0.236

Station Elevation Data    num=      30

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

496.4   801.6     526   792.1   537.2   787.1   611.6   780.5     620   771.6

664.8   773.7   690.4   773.1     738   770.1   766.8   759.7   833.6   749.6

890   750.3     938   749.4     942   747.3     947   741.8    1000   741.5

1043   737.1    1058   747.3    1086   753.8  1086.1   753.8  1086.2   753.8

1103.6   764.5    1146   775.2  1211.6   783.8  1268.8   794.8  1313.6   800.5

1368.8   816.5  1396.4   824.8  1422.8   826.9  1432.6   831.4  1432.7   831.4

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

496.4     .09     938    .035    1058     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

938    1058               36      36      36             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 20

INPUT

Description: 0.229

Station Elevation Data    num=       9

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

791.6   753.5   800.6   749.5   936.4   749.2   948.3   749.1   948.4     736

1031.6     736    1040     740  1051.6   746.3  1061.6     751

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

791.6     .08   948.3     .02  1051.6     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

948.3  1051.6                7       7       7             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 19

INPUT

Description: 0.228

This is a REPEATED section.

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

791.6   753.5   800.6   749.5   936.4   749.2   936.5   750.3   938.4   750.3

938.5   749.1   948.3   749.1   948.4   746.3  1051.6   746.3  1061.6     751

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

791.6     .07   948.4     .02  1051.6     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

948.4  1051.6                2       2       2             .1       .3

INLINE WEIR            RIVER: RIVER-1

REACH: Reach-1            RS: 18.5

INPUT

Description:

Distance from Upstream XS =       0

Deck/Roadway Width        =       2

Weir Coefficient          =    2.84

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =       10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

791.6   753.5   800.6   749.5   936.4   749.2   936.5   750.3   938.4   750.3

938.5   749.1   948.3   749.1   948.4   746.3  1051.6   746.3  1061.6     751

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   746.3

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 18

INPUT

Description: 0.227

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

791.6   753.5   800.6   749.5   936.4   749.2   936.5   750.3   938.4   750.3

938.5   749.1   948.3   749.1   948.4   746.3  1051.6   746.3  1061.6     751

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

791.6     .07   948.4     .03  1051.6     .08

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

948.4  1051.6                3       3       3             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 17

INPUT

Description: 0.227

Station Elevation Data    num=      17

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

791.6   753.5   800.6   749.5   936.4   749.2   936.5   750.3   938.4   750.3

938.5   749.1     941   749.1   941.1     730     950   729.5     980   729.3

1010   729.5    1013   729.5    1020   731.1    1030   735.6    1040     740

1051.6   746.3  1061.6     751

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

791.6     .07     950     .03    1013     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

950    1013               45      45      45             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 16

INPUT

Description: 0.218

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

474   800.2     508   780.2   517.6   773.1   563.2   767.7   584.8   766.9

628.4   766.6   654.8   761.2   682.8   752.6     738   750.8   807.2   752.9

897.6   751.4     920     746   920.1     746   920.2     746   920.3     746

941   743.1     961   741.6     971   729.6    1000   727.6    1029   729.6

1043   739.6  1043.1   739.6  1043.2   739.6  1043.3   739.6  1043.4   739.6

1074.7   757.6  1105.1   763.9  1150.3   766.6  1199.9   769.8  1235.5   773.7

1274.3   783.2  1311.1   790.6  1343.5   799.6  1375.5   805.8  1408.3     810

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

474     .03     971     .03    1029     .09

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

971    1029              175     175     175             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 15

INPUT

Description: 0.185

Station Elevation Data    num=      10

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

900     740     905     735     917     733     978     732     979   726.5

1000   725.2    1021   726.5    1022     732    1035     735    1058     740

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

900     .08     978     .04    1022    .055

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

978    1022              280     280     280             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 14

INPUT

Description: 0.132

Station Elevation Data    num=      35

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

140.4   775.5     174     771   238.4     763     316   750.8   415.2   744.8

456.8   741.9   494.8   742.5   508.4   740.4   519.2   729.4   569.6   729.1

674.4   730.3   788.8   730.6   823.6   730.6   851.6   730.6   902.8   730.9

949   731.6     959   732.6   959.1   727.1   959.2   724.7    1000   722.3

1041   725.1  1041.1   727.1  1041.2   732.3    1080   729.6  1080.1   729.6

1122.4   732.4  1182.4   735.9  1211.6   737.4  1265.6   739.2  1308.8   742.8

1327.2   755.6    1342     763  1368.4   763.6    1398     768  1420.4   771.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

140.4     .08     959     .03  1041.2    .055

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

959  1041.2               35      35      35             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 13

INPUT

Description: 0.125

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

928     745   928.1     730   945.8     730   945.9   731.7   961.9   731.7

962   719.1  1029.5   719.1  1029.6   731.3  1031.1   731.3  1031.2     730

1143   730.6    1159   734.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

928     .07   961.9     .03  1029.6     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

961.9  1029.6                5       5       5             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 12

INPUT

Description: 0.124

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

928     745   928.1     730   945.8     730   945.9   731.7   969.9   731.7

970     719    1030     719  1030.1   731.3  1031.6   731.3  1031.7     730

1143   730.6    1159   734.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

928     .07   969.9    .014  1030.1     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

969.9  1030.1                5       5       5             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 11

INPUT

Description: 0.123

This is a REPEATED section.

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

928     745   928.1   728.3   945.8   728.3   945.9   731.7   969.9   731.7

970   725.9    1030   725.9  1030.1   731.3  1031.6   731.3  1031.7   728.9

1143   730.6    1159   734.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

928     .07   969.9    .014  1030.1     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

969.9  1030.1                1       1       1             .1       .3

INLINE WEIR            RIVER: RIVER-1

REACH: Reach-1            RS: 10.5

INPUT

Description:

Distance from Upstream XS =       0

Deck/Roadway Width        =       1

Weir Coefficient          =    3.97

Bridge Deck/Roadway Skew  =

Weir Embankment Coordinates    num =       12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

928     745   928.1   728.3   945.8   728.3   945.9   731.7   969.9   731.7

970   725.9    1030   725.9  1030.1   731.3  1031.6   731.3  1031.7   728.9

1143   730.6    1159   734.1

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   725.9

Weir crest shape                            = Broad Crested

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 10

INPUT

Description: 0.123

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

928     745   928.1   728.3   945.8   728.3   945.9   731.7   969.9   731.7

970   725.9    1030   725.9  1030.1   731.3  1031.6   731.3  1031.7   728.9

1143   730.6    1159   734.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

928     .07   969.9    .014  1030.1     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

969.9  1030.1             11.5    11.5    11.5             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 9

INPUT

Description: 0.121

Station Elevation Data    num=      12

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

928     745   928.1   728.3   945.8   728.3   945.9   731.7   969.9   731.7

970   717.6    1030   717.6  1030.1   731.3  1031.6   731.3  1031.7   728.9

1143   730.6    1159   734.1

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

928     .07   969.9    .014  1030.1     .04

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

969.9  1030.1               10      10      10             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 8

INPUT

Description: 0.119

Station Elevation Data    num=      25

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

263   747.8     418   738.1     454   738.1     484   732.6     568   729.2

688     732     734     732     761   729.2     818   729.2     859   730.1

925   730.5     926   729.6     950   731.2   975.2   731.2   975.3   732.8

976.7   732.8   976.8   717.6    1027   717.5  1027.1   732.4  1028.6   732.4

1028.7     730    1050     730    1130     736    1160     740    1244   748.3

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

263     .03   976.7    .014  1027.1     .03

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

976.7  1027.1               30      30      30             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 7

INPUT

Description: 0.113

This is a REPEATED section.

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

923   724.2   975.2   730.1   975.3     730   976.7     730   976.8   717.2

982   717.2     987   717.2     992   717.2     997   717.2    1002   717.2

1006   717.2    1011   717.3    1017   717.3    1021   717.4    1024   717.4

1024.1   730.8    1025   730.8  1025.1   730.8    1050   732.5    1084   735.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

923     .03   976.7    .014  1024.1     .03

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

976.7  1024.1               25      25      25             .2       .4

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

923   976.7   728.2  1024.1    1084   729.8

BRIDGE                 RIVER: RIVER-1

REACH: Reach-1            RS: 6.5

INPUT

Description: Bridge #1

Distance from Upstream XS =       0

Deck/Roadway Width        =      25

Weir Coefficient          =     2.5

Bridge Deck/Roadway Skew  =

Upstream  Deck/Roadway Coordinates

num=      19

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

923   728.2       0   975.2   729.1       0   975.3     732       0

976.7   732.1       0   976.8   732.1     725     982  732.15   725.4

987   732.2   725.8     992   732.3     726     997   732.4   726.2

1006   732.5   726.4    1011   732.6   726.3    1017   732.7  726.15

1021   732.8     726    1024   732.8   725.9  1024.1   732.8       0

1025   732.8       0  1025.1   729.8       0    1050     731       0

1084   734.2       0

Upstream Bridge Cross Section Data

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

923   724.2   975.2   730.1   975.3     730   976.7     730   976.8   717.2

982   717.2     987   717.2     992   717.2     997   717.2    1002   717.2

1006   717.2    1011   717.3    1017   717.3    1021   717.4    1024   717.4

1024.1   730.8    1025   730.8  1025.1   730.8    1050   732.5    1084   735.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

923     .03   976.7    .014  1024.1     .03

Bank Sta: Left   Right    Coeff Contr.   Expan.

976.7  1024.1             .2       .4

Ineffective Flow     num=       2

Sta L   Sta R    Elev   Sta L   Sta R    Elev

923   976.7   728.2  1024.1    1084   729.8

Downstream  Deck/Roadway Coordinates

num=      19

Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord     Sta Hi Cord Lo Cord

923   728.2       0   975.2   729.1       0   975.3     732       0

976.7   732.1       0   976.8   732.1     725     982  732.15   725.4

987   732.2   725.8     992   732.3     726     997   732.4   726.2

1006   732.5   726.4    1011   732.6   726.3    1017   732.7  726.15

1021   732.8     726    1024   732.8   725.9  1024.1   732.8       0

1025   732.8       0  1025.1   729.8       0    1050     731       0

1084   734.2       0

Downstream Bridge Cross Section Data

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

923   723.2   975.2   729.1   975.3     729   976.7     729   976.8   716.2

982   716.2     987   716.2     992   716.2     997   716.2    1002   716.2

1006   716.2    1011   716.3    1017   716.3    1021   716.4    1024   716.4

1024.1   729.8    1025   729.8  1025.1   729.8    1050   731.5    1084   734.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

923      .1   976.7    .033  1024.1     .07

Bank Sta: Left   Right    Coeff Contr.   Expan.

976.7  1024.1             .1       .3

Upstream Embankment side slope              =       0 horiz. to 1.0 vertical

Downstream Embankment side slope            =       0 horiz. to 1.0 vertical

Maximum allowable submergence for weir flow =     .95

Elevation at which weir flow begins         =   728.2

Energy head used in spillway design         =

Spillway height used in design              =

Weir crest shape                            = Broad Crested

Number of Bridge Coefficient Sets =  1

Low Flow Methods and Data

Energy

Momentum               Cd   =    1.15

Selected Low Flow Methods = Energy

High Flow Method

Energy Only

Additional Bridge Parameters

Add Friction component to Momentum

Do not add Weight component to Momentum

Class B flow critical depth computations use critical depth

inside the bridge at the upstream end

Criteria to check for pressure flow = Upstream energy grade line

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 6

INPUT

Description: 0.109

Station Elevation Data    num=      20

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

923   723.2   975.2   729.1   975.3     729   976.7     729   976.8   716.2

982   716.2     987   716.2     992   716.2     997   716.2    1002   716.2

1006   716.2    1011   716.3    1017   716.3    1021   716.4    1024   716.4

1024.1   729.8    1025   729.8  1025.1   729.8    1050   731.5    1084   734.2

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

923      .1   976.7    .033  1024.1     .07

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

976.7  1024.1               50      50      50             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 5

INPUT

Description: 0.099

Station Elevation Data    num=       6

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

940     730     974     727     975     716    1019     716    1020   726.5

1030     730

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

940      .1     974    .033    1020    .065

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

974    1020              385     385     385             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 4

INPUT

Description: 0.026

Station Elevation Data    num=       7

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

550     725     960     721     968     713    1000     712    1021     713

1030     721    1535     725

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

550     .08     960    .033    1030     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

960    1030                1       1       1             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 3

INPUT

Description: 0.026

This is a REPEATED section.

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

650     726     960     721     968     713     980     712     981     716

985     716     986   712.3    1000     712    1003   712.1  1003.1     716

1007     716    1008   712.5    1021     713    1030     721    1535     726

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

650     .08     960    .033    1030     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

960    1030               42      42      42             .1       .3

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 2

INPUT

Description: 0.018

Station Elevation Data    num=      15

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

650     725     960     720     968     712     980     711     981     715

985     715     986   711.3    1000     711    1003   711.1  1003.1     715

1007     715    1008   711.5    1021     712    1030     720    1535     725

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

650     .08     960    .033    1030     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

960    1030                1       1       1             .2       .4

CROSS SECTION          RIVER: RIVER-1

REACH: Reach-1            RS: 1

INPUT

Description: 0.018

Station Elevation Data    num=       7

Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev     Sta    Elev

550     725     960     720     968     712    1000     711    1021     712

1030     720    1535     725

Manning's n Values        num=       3

Sta   n Val     Sta   n Val     Sta   n Val

550     .08     960    .033    1030     .05

Bank Sta: Left   Right    Lengths: Left Channel   Right     Coeff Contr.   Expan.

960    1030                0       0       0             .1       .3

SUMMARY OF MANNING'S N VALUES

River:RIVER-1

Reach          River Sta.       n1        n2        n3

Reach-1              65                  .1       .05        .1

Reach-1              64                 .08       .04        .1

Reach-1              63                 .08       .04       .08

Reach-1              62.5         Bridge

Reach-1              62                 .08       .04       .08

Reach-1              61                 .08       .04       .08

Reach-1              60                 .08       .04       .08

Reach-1              59.5         Bridge

Reach-1              59                 .09       .04       .08

Reach-1              58                 .06      .035       .09

Reach-1              57                 .06       .03       .07

Reach-1              56                 .07       .03       .04

Reach-1              55                 .07      .035       .04

Reach-1              54.5         Inline Weir

Reach-1              54                 .07      .035       .03

Reach-1              53                 .07      .035       .03

Reach-1              52                 .02      .035       .02

Reach-1              51.5         Bridge

Reach-1              51                 .09       .05       .07

Reach-1              50                  .1       .05        .1

Reach-1              49                 .08       .04        .1

Reach-1              48                 .08      .033        .1

Reach-1              47                 .08      .033       .09

Reach-1              46                 .09       .03       .09

Reach-1              45                 .09      .035       .09

Reach-1              44                 .07      .035       .07

Reach-1              43.5         Bridge

Reach-1              43                 .09      .035       .08

Reach-1              42                 .09      .035       .07

Reach-1              41                 .09       .03       .08

Reach-1              40                  .1       .03        .1

Reach-1              39                 .07       .03       .08

Reach-1              38                 .09       .03       .07

Reach-1              37                 .08       .03        .1

Reach-1              36                 .08       .03       .08

Reach-1              35                 .06       .03       .06

Reach-1              34.5         Inline Weir

Reach-1              34                 .06       .02       .06

Reach-1              33                 .06       .02       .06

Reach-1              32                 .07       .02       .06

Reach-1              31                 .07       .03       .07

Reach-1              30                 .07       .03       .06

Reach-1              29                 .07       .03       .06

Reach-1              28                 .06       .03       .06

Reach-1              27                 .06       .02       .08

Reach-1              26.5         Inline Weir

Reach-1              26                 .06       .06       .08

Reach-1              25                  .1       .06       .08

Reach-1              24                  .1      .035       .08

Reach-1              23                 .09       .04       .08

Reach-1              22                 .09       .04       .08

Reach-1              21                 .09      .035       .08

Reach-1              20                 .08       .02       .08

Reach-1              19                 .07       .02       .08

Reach-1              18.5         Inline Weir

Reach-1              18                 .07       .03       .08

Reach-1              17                 .07       .03       .09

Reach-1              16                 .03       .03       .09

Reach-1              15                 .08       .04      .055

Reach-1              14                 .08       .03      .055

Reach-1              13                 .07       .03       .04

Reach-1              12                 .07      .014       .04

Reach-1              11                 .07      .014       .04

Reach-1              10.5         Inline Weir

Reach-1              10                 .07      .014       .04

Reach-1              9                  .07      .014       .04

Reach-1              8                  .03      .014       .03

Reach-1              7                  .03      .014       .03

Reach-1              6.5          Bridge

Reach-1              6                   .1      .033       .07

Reach-1              5                   .1      .033      .065

Reach-1              4                  .08      .033       .05

Reach-1              3                  .08      .033       .05

Reach-1              2                  .08      .033       .05

Reach-1              1                  .08      .033       .05

SUMMARY OF REACH LENGTHS

River: RIVER-1

Reach          River Sta.      Left     Channel    Right

Reach-1              65                 730       915       980

Reach-1              64                  37        42        47

Reach-1              63                21.5      21.5      21.5

Reach-1              62.5         Bridge

Reach-1              62                  10        10        10

Reach-1              61                  15        20        30

Reach-1              60                   9         9         9

Reach-1              59.5         Bridge

Reach-1              59                 460       375       300

Reach-1              58                 440       440       440

Reach-1              57                  45        45        45

Reach-1              56                   2         2         2

Reach-1              55                 1.5       1.5       1.5

Reach-1              54.5         Inline Weir

Reach-1              54                   1         1         1

Reach-1              53                   7         7         7

Reach-1              52                47.2      47.2      47.2

Reach-1              51.5         Bridge

Reach-1              51                  32        32        32

Reach-1              50                 450       495       540

Reach-1              49                 480       480       480

Reach-1              48                1895      2342      1820

Reach-1              47                1620      2390      2060

Reach-1              46                 520       530       525

Reach-1              45                  45        45        45

Reach-1              44               16.33     16.33     16.33

Reach-1              43.5         Bridge

Reach-1              43                  58        58        58

Reach-1              42                 405       390       390

Reach-1              41                1110      1165      1010

Reach-1              40                3180      3530      2500

Reach-1              39                1700      1950      1540

Reach-1              38                 750       700       630

Reach-1              37                  45        45        45

Reach-1              36                   1         1         1

Reach-1              35                  .5        .5        .5

Reach-1              34.5         Inline Weir

Reach-1              34                   1         1         1

Reach-1              33                  33        33        33

Reach-1              32                  45        45        45

Reach-1              31                 130       110       100

Reach-1              30                 190       148        95

Reach-1              29                  53        53        53

Reach-1              28                   5         5         5

Reach-1              27                   2         2         2

Reach-1              26.5         Inline Weir

Reach-1              26                  25        25        25

Reach-1              25                  30        15         5

Reach-1              24                 165       155       150

Reach-1              23                 125       125       125

Reach-1              22                 110       110       110

Reach-1              21                  36        36        36

Reach-1              20                   7         7         7

Reach-1              19                   2         2         2

Reach-1              18.5         Inline Weir

Reach-1              18                   3         3         3

Reach-1              17                  45        45        45

Reach-1              16                 175       175       175

Reach-1              15                 280       280       280

Reach-1              14                  35        35        35

Reach-1              13                   5         5         5

Reach-1              12                   5         5         5

Reach-1              11                   1         1         1

Reach-1              10.5         Inline Weir

Reach-1              10                11.5      11.5      11.5

Reach-1              9                   10        10        10

Reach-1              8                   30        30        30

Reach-1              7                   25        25        25

Reach-1              6.5          Bridge

Reach-1              6                   50        50        50

Reach-1              5                  385       385       385

Reach-1              4                    1         1         1

Reach-1              3                   42        42        42

Reach-1              2                    1         1         1

Reach-1              1                    0         0         0

SUMMARY OF CONTRACTION AND EXPANSION COEFFICIENTS

River: RIVER-1

Reach          River Sta.     Contr.    Expan.

Reach-1              65              .1        .3

Reach-1              64              .1        .3

Reach-1              63              .1        .3

Reach-1              62.5     Bridge

Reach-1              62              .3        .5

Reach-1              61              .2        .4

Reach-1              60              .2        .4

Reach-1              59.5     Bridge

Reach-1              59              .2        .4

Reach-1              58              .2        .4

Reach-1              57              .1        .3

Reach-1              56              .2        .4

Reach-1              55              .1        .3

Reach-1              54.5     Inline Weir

Reach-1              54              .1        .3

Reach-1              53              .1        .3

Reach-1              52              .1        .3

Reach-1              51.5     Bridge

Reach-1              51              .2        .4

Reach-1              50              .1        .3

Reach-1              49              .2        .4

Reach-1              48              .1        .3

Reach-1              47              .1        .3

Reach-1              46              .1        .3

Reach-1              45              .3        .5

Reach-1              44              .1        .3

Reach-1              43.5     Bridge

Reach-1              43              .3        .5

Reach-1              42              .2        .4

Reach-1              41              .2        .4

Reach-1              40              .1        .3

Reach-1              39              .1        .3

Reach-1              38              .1        .3

Reach-1              37              .1        .3

Reach-1              36              .1        .3

Reach-1              35              .1        .3

Reach-1              34.5     Inline Weir

Reach-1              34              .1        .3

Reach-1              33              .1        .3

Reach-1              32              .1        .3

Reach-1              31              .5        .7

Reach-1              30              .1        .3

Reach-1              29              .3        .5

Reach-1              28              .3        .5

Reach-1              27              .3        .5

Reach-1              26.5     Inline Weir

Reach-1              26              .3        .5

Reach-1              25              .2        .4

Reach-1              24              .2        .4

Reach-1              23              .1        .3

Reach-1              22              .1        .3

Reach-1              21              .1        .3

Reach-1              20              .1        .3

Reach-1              19              .1        .3

Reach-1              18.5     Inline Weir

Reach-1              18              .1        .3

Reach-1              17              .1        .3

Reach-1              16              .1        .3

Reach-1              15              .1        .3

Reach-1              14              .1        .3

Reach-1              13              .2        .4

Reach-1              12              .1        .3

Reach-1              11              .1        .3

Reach-1              10.5     Inline Weir

Reach-1              10              .1        .3

Reach-1              9               .1        .3

Reach-1              8               .1        .3

Reach-1              7               .2        .4

Reach-1              6.5      Bridge

Reach-1              6               .1        .3

Reach-1              5               .1        .3

Reach-1              4               .2        .4

Reach-1              3               .1        .3

Reach-1              2               .2        .4

Reach-1              1               .1        .3