CTAP Land Cover/Land Use Update Procedure

August, 2007

Recommended Procedure:

Establish a starting location for your QC process, typically the NW or SW corner of your coverage area.  Using a standard viewing scale of 1:5000, review each screen of data to ensure that all features visible in the imagery are captured and coded appropriately.  Once you have completed a screen review, proceed at the established viewing scale to the next screen (Note: you can add buttons to move exactly one screen, north/south/east/west using the Tools/customize/Commands/Pan/Zoom and add  the appropriate tool , Page Left, Page right, etc., to your toolbar. Using these tools ensures that movement across the study area is conducted in a consistent and comprehensive manner).

As you review the data, two types of errors will be encountered – miscoded polygons, and polygons requiring updated geometry (either re-delineations of existing polygons or new delineations).

- Polygon Recodes

- Submit all recodes for your region in a single document, preferably an .xls file, with 3 columns – GRANITID, Old Code, New Code

- Indicate the polygon to be recoded via the GRANITID number

- Record the old LC/LU code as well as the new LC/LU code

- Polygon Delineations/Re-delineations

- Create a graphic (including a world file such that the image can be used as a backdrop while updating the polygon geometry) that shows how the geometry should be changed

- Include updated polygon codes for the new geometry in the graphic

We will track changes by adding a version to the title of the land cover/land use geodatabase. The initial geodatabase will be CTAPLCLU2005V1_0. Subsequent version will increment the version in the geodatabase name (e.g. V1_1, V1_2, etc.). Updates to the geodatabase will be posted to the GRANIT ftp site on a bi-weekly basis, should any change be necessary. This maintenance will be continued through January, 2008.