Introduction

The NH Land Use Mapping Standard describes a classification scheme and mapping protocols for generating land use data from high resolution, remotely sensed data sources. The standard was developed by GRANIT staff at Complex Systems Research Center (CSRC), University of New Hampshire, in consultation with the Office of Energy and Planning and the nine Regional Planning Commissions in the state. It was informed by prior land use mapping projects conducted by Planning Commissions and GRANIT staff, as well as a series of discussions hosted by the NH Department of Environmental Services.  This broad input yielded a standard which is designed to meet the land use mapping needs of a diverse community of users.

The standard was developed under the auspices of the CTAP/I-93 Corridor Project in southern New Hampshire, and will govern the production of land use data for the 26 towns in that Corridor.   While developed for that project, it is recommended for all NH land use data sets derived from high resolution image sources that are to be archived in the GRANIT database.

It should be noted that while land use and land cover are at times simultaneous, the standard does not necessarily apply to land cover data sets.

Data Sources

The primary data source for land use data is high-resolution (1 ft.), color, leaf-off, digital orthophotography (Figure 1).  Additional data sources include:

- NH Department of Transportation road centerlines

- NH National Hydrography Dataset (NHHD)

- NH Department of Environmental Services water distribution areas, depicting water and sewer service zones

- US Fish & Wildlife Service National Wetlands Inventory (NWI)

- USGS town boundaries

Data on water distribution areas are available from the NH Department of Environmental Services.  All other sources listed above are available from the GRANIT GIS repository (www.granit.sr.unh.edu).

In addition to these existing data sources, project-specific field data collection will be required to meet the standard.

Figure 1. Image extract – 1-ft. resolution imagery, UNH campus, Durham, NH. collected April 2005.

Land Use Classification

The data will utilize a classification structure that represents an enhancement of the standard USGS Anderson Level II land use coding (USGS Professional Paper 964, 1976).  This hierarchical coding structure assigns a Level I (1-digit) code as follows:

1.	Urban and built-up land

2.	Agricultural land

3.	Brush or transitional between open and forest

4.	Forest

5.	Water

6.	Wetlands

7. 	Barren land

8.	Tundra

9.	Permanent snow and ice (no known examples in New Hampshire)

Within the Anderson classification, Level II (2-digit) codes expand to provide more detailed information.

Efforts by OEP in the mid 1990’s to coordinate a NH land use mapping standard resulted in the incorporation of Level III (3-digit) and IV (4-digit) codes to the USGS structure, thereby creating a comprehensive, detailed land use categorization (Appendix II).  The following illustrates the 4 classification levels for one type of land use:

Level		Code		Category Description

I		1		Urban and built-up land

II		14		Transportation, communication, and utilities

III		144		Road transportation

IV		1441		Limited & controlled highway right-of-way

The OEP standard was further modified to reflect current data sources and current mapping needs.  Appendix I reports the amended, comprehensive land use categorization.

Table 1 below presents the 58 land use categories, extracted from Appendix I, which will be used for the I-93 Corridor land use mapping effort.  To maintain consistency in assigning codes and to facilitate subsequent use of the data, all codes have been extended to 4 digits although they represent a combination of Levels I, II, III, and IV categories.    Mappers will benefit from using Table 1 as a quick reference, while relying on Appendix I to provide the full framework for the coding scheme and to offer explanatory notes on the intended contents of selected categories.

Because the project land use classes represent a combination of mapping levels, it is important for users of the 58-category classification to recognize the context for selected codes in order to apply the correct code to a land use feature.  Typically, at any level of mapping, there is a final code ending in the digit ‘9’ that collects all miscellaneous uses within that category.  However, that catchall category is only appropriately used when all preceding codes at the same level of specificity are used.

For example, within the Industrial category, a full mapping of all Level III categories would result in the use of code 139 (other industrial) to map miscellaneous industrial uses.  However, for the 58-category subset, only code 137 (mining) is being mapped at Level III.  All other industrial uses are mapped at a generalized level and should therefore be assigned a code of 1300.  Similarly, in the road transportation codes, note that 1440 is used to collect all codes that are not specifically identified in the subsequent detailed road classes.

Table 1.  Target land use categories.

Mapping Parameters

This section describes basic mapping parameters governing the development of data in all land use classes:

- Coordinate reference system:  New Hampshire State Plane Coordinate System, North American Datum of 1983, units - feet.

- Minimum mapping unit:  .25 acres.  Smaller features that result from automated processes to map surrounding land uses may also be included in the data.

- Map unit purity:  For areas with complex mixes of land use, a map unit purity of 85% or greater is required, indicating that up to 15% of a coded map feature may comprise a different land use type.

- Data format:  Preferred format - personal geodatabase (.mdb or .gdb).  If this is not an option, shapefiles will be accepted. The feature class must be polygons.

- Topological requirements:  All data must be “topologically clean”.  If using ArcGIS 9.x, apply appropriate topology rules to ensure that there are no overlapping polygons, no sliver polygons, and no gaps in the data.  If you do not have access to ArcGIS, use available tools to ensure that topology can be constructed from your data.

- Image display scale:  For land use digitizing purposes, imagery should be displayed at a minimum scale of 1:2,400 (1”=200’).  For quality control/verification purposes, a smaller display scale (e.g. 1:5,000) may be used.

- The Page Left/Right/Up/Down tools (under Customize>Commands>Zoom/Pan in ArcMap) may be used to systematically step across an image one screen at a time while preserving a viewing scale.

- If digitizing new roads, zoom into 1:1,200 (1”=100’) to delineate the centerline.  Return to the standard viewing scale for all land use polygon delineations.

- Naming conventions for the land use datafile:  LU_<RPC acronym>, e.g. LU_NRPC, with the following fields:

- LU – integer, width: 4 – based on Table 1 codes.  (Note that all codes should be carried out to the full 4 digits.)

- ID – integer, width: 4 – sequentially assigned ID used during data development/QC phases.  This field will likely be eliminated once the composite is finalized.

- Documentation:  CSRC staff will generate an FGDC-compliant metadata record that includes the general procedures and protocols contained in this document.  RPC staff should submit to CSRC documentation that describes any data sources or mapping techniques that deviate from and/or extend these general project standards.

Data Development Protocols

This section describes methodologies for generating and/or delineating individual land use features.

- Town Bounds:  Start with the GRANIT town boundary layer (PBNH) and select all towns in your study area.  Eliminate any internal town bounds so that you have only the outer boundary as a starting point.

- Roads: Clip out roads for your study area from the December, 2006 NH DOT road centerline file.  For the purposes of this project, the only required field is the pavement width.   Display the roads on top of the imagery, and review to ensure that spatial alignments are satisfactory, that all roads are captured, and that all pavement width fields are populated.  Screen-digitize/enter any new data as necessary (Figure 2).  Populate pavement width fields, if necessary, based on visual estimation.

Select out the limited & controlled highways, and buffer based on the pavement width field.  (Local knowledge may be required to select out the appropriate road segments.)  Generate a second roads buffer data set based on the remaining roadways and their pavement widths.  Combine the two buffered data sets, ensuring that the limited & controlled highways take precedence over the local roads where there is overlap.

- Railroads:  Digitize all railroads from the imagery as linear features, then buffer by 12’ to generate the land use polygons.  (This buffer width is based on a visual assessment of the average railroad bed in the 1998 DOQ’s.)

- Composite:  Generate a composite of the town bounds, the buffered roads, and the buffered railroads.   Review and clean up the data at this point, ensuring that:

  - Where railroads cross road ways, the railroad feature supersedes in the data unless the road crosses over the rail bed on a bridge.

  - Any buffer polygons that extend beyond the study area are eliminated.

  - Any slivers resulting from the overlay process are removed.

Figure 2. Review of road centerline data.

The composite data set constitutes the starting point for the individual land use feature delineation.  All remaining land use features should be incorporated into the layer by screen-digitizing boundaries visible in the source photography and should be coded based on the visible feature characteristics and/or by field data collection.  The following protocols are provided to guide the on-screen delineation, with categories grouped where mapping protocols are the same:

Residential (1110, 1120, 1130, 1140, 1150, and 1190):  Digitize residential features to visible use boundaries when possible, using yard edges/natural features to guide the delineation (Figure 3, Example 1; Figure 4, Example 1). However, where boundaries (or partial boundaries) are indistinct, use one of several approaches:

1a)   For indistinct boundaries of houses within 250' of one another and within public water/sewer zones, a .5-acre circle centered on the structure edge furthest from the associated road is used as a guide for the polygon delineation (Figure 4, Example 4).

1b)   For indistinct boundaries of houses within 250' of one another and outside of public water/sewer zones,   the 1a) protocol is applied using a 1-acre circle (Figure 4, Example 3).

2a)  For indistinct boundaries of houses greater than 250' apart and within public water/sewer zones, a .5-acre box is generated, centered on the structure (Figure 5, Example 1) or centered in the approximate midpoint of multiple structures on what appears to be a single parcel.  If the structure(s) is within 700' of a road, the box is oriented parallel to the nearest road. In cases where the rotated box intersects the road edge, it is repositioned further away from the road to preserve as much of the box area as possible and the road edge becomes the polygon edge (Figure 5, Example 2). In these cases, the box becomes somewhat smaller than the original .5-acre (or 1-acre when outside the water/sewer zones). If the house is further than 700' from the road, or does not appear to be associated with a nearby road, the box is not rotated.

2b) For indistinct boundaries of houses greater than 250' apart and outside of public water/sewer zones,   the 2a) protocol is applied using a 1-acre box (Figure 3, Example 2).

Note that CSRC has developed a VBA tool to assist in applying the approaches described above.  Contact GRANIT staff for access to this tool.

Figure 3. Application of residential digitizing rules.

Figure 4. Additional application of residential digitizing rules.

Figure 5. Application of residential digitizing rules within water service areas.

Commercial, services, and institutional (1210, 1220, 1230, 1240, 1250, 1260, 1270, 1280, and 1290): Digitize features to visible use boundaries (Figure 6).

Figure 6.  Mapping features in the Commercial, services, and institutional category.

Industrial (1300, 1370): Digitize features to visible use boundaries.  Use 1370 to map mining activities (including only the portion where there is a structure/processing facility), and 1300 for all other industrial land uses.  (Note that other mining activities are mapped under code 7500.)

Air transportation (1410): Digitize features to visible use boundaries.  Note that this category includes airline terminals, hangers, and grassy areas between and around runways.

Rail transportation (1420): These features are developed by buffering the railroad arcs (12 ft/side, for a total width of 24 ft.).  The category may also include adjacent narrow strips that are <= 20 ft. in width and that are generated during the buffer process.

Water transportation (1430): Digitize features to visible use boundaries.

Road transportation (1440): Digitize features to visible use boundaries. This category includes all transportation features not explicitly mapped into individual categories, including truck terminals, bus terminals, and other road transportation features.

Limited & controlled highway right –of-way (1441): This category is developed by buffering the DOT road centerline based on pavement width.  It may also include adjacent narrow strips that are <= 20 ft. in width and that are generated during the buffer process.

Road right-of-way (1442): This category will be developed by buffering the DOT road centerline data based on the pavement width.  It may also include adjacent narrow strips that are <= 20 ft. in width and that are generated during the buffer process.

Park & ride lot (1445): Digitize features to visible use boundaries.  Only designated park and ride lots are mapped in this category.  Other parking lots are mapped in category 1446.

Parking structure/lot (1446): Digitize features to visible use boundaries. These include public areas in mixed use commercial areas, i.e. downtowns.  Parking lots should not be separately delineated for single-use activities, such as a shopping mall.

Auxiliary transportation (1447):  Digitize to visible extent of the feature. Margins along roadways in excess of 40-feet will be captured (Figure 7). This category also includes limited access highway medians and on/off ramps or cloverleafs.

Figure 7. Potential auxiliary transportation issues.

Communication (1450): Digitize to visible extent of the feature.

Electric/transmission lines (1460):  Digitize width of cleared area under the line.  Where these clearings traverse another land use, the other land uses take precedence (Figure 8).

Figure 8. Potential electric/transmission line issues.

Water and wastewater utilities (1470): Digitize to visible extent of the feature.

Solid waste utilities (1480): Digitize to visible extent of the feature.

Other transportation, communications, and utilities (1490): Digitize to visible extent of the feature.

Industrial park (1510): Digitize to visible extent of the feature, including associated parking lots.

Office park (1520): Digitize to visible extent of the feature, including associated parking lots.

Shopping mall (1530): Digitize to visible extent of the feature, including associated parking lots.

Other industrial complexes (1580): Digitize to visible extent of the feature. This includes industrial sites > 25 acres with multiple occupants, including associated parking lots.  Otherwise, map in Industrial category (13).

Other commercial complexes (1590): Digitize to visible extent of the feature. This includes multiple concerns with a shared parking lot.  Otherwise, map in Commercial category (12).

Mixed residential-commercial (1610): Digitize to visible extent of the feature.  This includes areas where level II uses are mixed.  A typical example might be a structure containing a business on the ground level with residences on the upper levels, with no single use predominating.

Other mixed use (1690): Digitize to visible extent of the feature.

Outdoor and other urban built-up land (1710, 1720, 1730, 1740, and 1790): Digitize to visible extent of the feature.  Include only the developed areas within park/recreation and other outdoor areas.

Vacant (1800): Digitize to visible extent of the feature.  Include all vacant, developed land (e.g. empty shopping center).

Agricultural land (2000): Digitize to visible extent of the feature. This category includes fields, pastures, row crops, orchards, etc. It does not include farm buildings (Figure 9).

Other agricultural land (2900): Digitize to visible extent of the feature. This category should be used to capture farm buildings. Where the visible extent is vague or undefined, use the residential digitizing approaches described above (Figure 9).

Figure 9. Examples of agricultural land and other agricultural land (farmsteads).

Transitional (3000): Digitize to visible extent of the feature (Figure 10).

Figure 10. Illustration of abandoned or idle land in the transitional class.

Forest (4000): Digitize to visible extent of the feature. Small forested areas (less than 5 acres) that are completely enclosed within a developed polygon are assumed to "belong" to the developed polygon, and are generally not distinguished.  There may be instances, however, where inclusions of forest less than 5 acres result from mapping multiple surrounding uses.  These may remain in the data.

Water (5000):  Delineate all surface water feature polygons from the imagery using NHNHD as a reference.  If a feature is presented as a polygon in NHNHD, it should be delineated as a land use polygon (Figure 11).  This approach provides a means of standardizing the set of surface water features mapped.  Also, capture water to visible extent in image, not high or low water mark (as seen in tidal regions).

Figure 11. Illustration of digitizing standard for defining double line streams.

Wetlands (6000): Digitize to visible extent of the feature. This category includes all wetlands visible in the image (recognizing that some forested wetlands will be indistinguishable). NWI datasets may be used to identify the presence/absence of wetlands (Figure 12).

Figure 12. Illustration of forested and open wetland classes.

Barren (7100, 7200, 7300, 7400, 7500, 7600, and 7900): Digitize to visible extent of the feature. With respect to mining, this category includes only developed areas within mining activities, and does not include mining buildings/machinery (which should be assigned a category of 1370, Figure 13).  Construction sites for new development provide an example of “disturbed” uses.

Figure 13. Illustration of the barren category.

Tundra (8000): Digitize to visible extent of the feature. This category is rare and probably only occurs at high elevations in Carroll, Coos, and Grafton counties.

It is expected that secondary data sources will be required to code some of the categories. In particular, many of the developed categories will require either field visits or access to digital parcel data in order to correctly classify the use or density of use.  Additionally, transitional categories can be difficult to identify from aerial photography, making field visits a necessary step. Typically, these sites can be determined via “windshield surveys” after the feature has been defined on-screen. Ultimately, it is left to the analyst’s discretion as to the most appropriate procedure used to code a given land use.

Quality Control

Review all feature data for topological integrity by using standard GIS tools to check for polygon closure, sliver polygons, etc.

Review attribute integrity by confirming that all polygons are coded, and by checking all codes against an attribute domain list.  In addition, a “dissolve” operation should be applied to confirm that there are no adjacent polygons with identical land use codes.

The quality of the feature interpretation and delineation should also be reviewed during the quality control phase.  The delineated land use polygons may be mapped, using transparent symbology, on the source imagery displayed at a minimum scale of 1:5,000.  Linework and attribute coding should be modified, as necessary.

Appendix I.  Comprehensive 4-digit land use classification scheme.  Yellow cells indicate the 58 categories extracted for the I93 Corridor land use mapping project.

1In the original land use standards (Appendix II), the 3-digit code of 111 was defined as residential units with 3 or more stories, while 112 was defined as residential units with 1-2 stories.  However, pilot testing using the classification indicated that modifying the thresholds to 4 or more stories (111) and 1-3 stories (112) was more appropriate when mapping established residential areas in larger cities (e.g. Manchester).

Appendix II.  NEW HAMPSHIRE LAND USE/LAND COVER CLASSIFICATION

The first two levels of land use and land cover classification employed in the statewide GRANIT system taken from the US Geological Survey (J.R.Anderson, E.E.Hardy, J.T.Roach, and R.E.Witmer) and detailed in USGS Professional Paper 964, 1976.  This classification system is hierarchical in design and has been expanded to a third and fourth level of detail by the State of Vermont.  Levels III and IV of the land use and land cover classification system for New Hampshire are the same as Vermont's (VGIS Part 2 - Standards Section C) with minor additions.

1 URBAN AND BUILT-UP LAND

11	RESIDENTIAL

111 Multi-family, medium to high rise apartments & condominiums 		    (3 or more stories)

1111	more than 50 units per acre

1112	36 to 50 units per acre

1113	21 to 35 units per acre

1114	10 to 21 units per acre

1115	1 to 10 units per acre

112 Multi-family, low rise apartments and town houses, but not 		    duplexes; (1 or 2 stories)

1121	more than 18 units per acre

1122	12 to 18 units per acre

1123	8 to 12 units per acre

1124	less than 8 units per acre

113 Single family/duplex

1131	more than 8 units per acre

1132	5 to 8 units per acre

1133	3 to 4 units per acre

1134	1 to 2 units per acre

1135	less than 1 unit per acre

114 Mobile home parks

1141	more than 9 units per acre

1142	6 to 9 units per acre

1143	2 to 5 units per acre

1144	less than 2 units per acre

115 Group and transient quarters

1151	Rooming and boarding houses

1153 	Residence halls and dormitories

1154	Retirement homes and orphanages

1155	Religious quarters

1156	Residential hotels

1157	Fraternities/sororities

1159	Other group & transient quarters

119 Other residential

12	COMMERCIAL, SERVICES AND INSTITUTIONAL

121 Commercial retail

1211	Building materials, hardware and farm equipment

1212	General merchandise/department store

1213	Food/groceries

1214	Automotive, marine craft, aircraft and accessories/dealers

1215	Furniture, home furnishings and equipment

1216	Eating and drinking (restaurants)

1217	Gasoline/petroleum

1218	Farm stand

1219	Other (Not elsewhere recorded)

122 Commercial wholesale

1221	Food/sundries/beverages

1222	Agricultural products/supplies

1223	Lumber/hardware/building supplies/paper

1224	Industrial product/chemical/petroleum

1225	Motor vehicles/parts/supplies

1229	Other

123 Services

1231	Banking

1232	Personal services

1233	Professional services

1234	Self-storage

1235	Day care

1236	Contract construction services

1237	Automotive services/car washes

1238	Agricultural sales/services

1239	Other services

124 Lodging

1241	Hotel/motel

1242	Bed and breakfast

1249	Other lodging

12	COMMERCIAL, SERVICES AND INSTITUTIONAL

125 Government

1251	Correctional

1252	Military

1253	Courthouse

1254	Postal service

1255	Administrative offices

1256	Emergency services

1257	Public works

1259	Other government

126 Institutional

1261	Religious

1262	Hospital

1263	Medical clinics

1264	Nursing

1265	Social organizations/associations

1269	Other institutional

127 Educational

1271	Preschool

1272	Elementary

1273	Middle

1274	High school

1275	College/university

1276	Vocational/trade

1279	Other educational

128 Indoor cultural/public assembly

1281	Museum

1282	Theatre

1283	Amusement

1284	Sport

1289	Other indoor cultural assembly

129 Other commercial, services and institutional

13	INDUSTRIAL

131 Primary metal production

132 Petrochemicals/chemicals

133 Primary wood processing and paper mills

134 Stone, clay, glass

135 Metal and non-metal fabrication

136 Food processing

137 Mining (active operations)

1371	Hard rock

1372	Quarry

1373	Sand/gravel

1379	Other mining

138 Electronics

139 Other industrial

14	TRANSPORTATION, COMMUNICATIONS & UTILITIES

141 Air transportation

1411	Commercial

1412	Non-commercial

1413	Heliports

1419	Other air transportation

142 Rail transportation

1421	Rail yard

1422	Station or terminal

1423	Active rail line

1424	Inactive rail line

1429	Other rail transportation

143 Water transportation

1431	Port facilities

1439	Other water transportation

144 Road transportation

1441	Limited & controlled highway right-of-way

1442	Road right-of-way

1443	Truck terminal

1444	Bus terminal

1445	Park/ride lot

1446	Parking structure/lot

1449	Other road transportation

145 Communication

1451	Radio station

1452	Telecommunications facilities

1453	Television station

1454	Transmitters/towers

1459	Other communication

146 Electric, gas and other utilities

1461	Electric transmission lines

1462	Electric power generation facilities

1463	Gas or oil pipeline (natural, propane or other)

1464	Gas or oil storage facilities

1469	Other utilities

14	TRANSPORTATION, COMMUNICATIONS & UTILITIES (continued)

147 Water and wastewater utilities

1471	Water treatment plant

1472	Aqueduct

1473	Water storage tanks

1474	Wastewater treatment

1475	Interceptors

1479	Other water/wastewater utilities

148 Solid waste utilities

1481	Active landfills

1482	Inactive dump sites

1483	Recycling/transfer stations

1484	Incinerator

1485	Composting facility

1486	Sludge processing facility

1487	Hazardous waste collection/processing facility

1489	Other solid waste facilities

149 Other communications, utilities

15	INDUSTRIAL AND COMMERCIAL COMPLEXES

151 Industrial park

152 Office park

153 Shopping center/mall

158 Other industrial complexes

159 Other commercial complexes

16	MIXED (areas where level 2 uses are mixed with no one use 					predominating)

161 Multiple stories, residential in upper stories only

1621	Commercial lower level

1622	Services lower level

1623	Mixed commercial/services lower level

1629	Other mixed uses in lower level

169 Other mixed level 2 uses

17	OUTDOOR AND OTHER URBAN AND BUILT-UP LAND

171 Outdoor cultural

1711	Botanical gardens and arboretums

1712	Zoos

1713	Other outdoor cultural

172 Outdoor public assembly

1721	Ampitheaters

1722	Drive-in movies

1723	Stadiums

1724	Racetracks

1725	Fairgrounds

1726	Amusement parks

1729	Other outdoor public assembly

173 Outdoor recreation

1731	Playground or play field

1732	Sports areas

1733	Water recreation/marina/launch

1734	Ski area

1735	Golf course

1736	Campground

1737	Parks and recreation

1739	Other outdoor recreation

174 Cemeteries

179 Other outdoor urban, built-up and developed

2 AGRICULTURAL LAND

21	CROPLAND AND PASTURE

211 Row crops (not including orchards and berries, code 22)

2111	Corn (land cover includes silage corn)

2112	Silage (corn and grasses)

2113	Potatoes

2114	Soybeans

2115	Alfalfa

2118	Other root crops

2119	Other non-root crops

212 Hay/rotation/permanent pasture

2121	Hay

2122	Rotation pasture

2123	Permanent pasture

2124	Idle agricultural land; use level 3 for land cover

2129	Other pasture

213 Grains (not including row crops)

2131	Wheat

2132	Oats

2133	Sorghum

21	CROPLAND AND PASTURE (continued)

213 Grains (not including row crops) (continued)

2134	Barley

2139	Other grains (not including row crops)

22	ORCHARDS, BUSH FRUITS, VINEYARDS AND ORNAMENTAL HORTICULTURE

221 Tree fruits, regularly spaced (planted)

2211	Apples

2212	Pears

2219	Other tree fruits

222 Bush and vine fruits (in rows)

2221	Strawberries

2222	Raspberries

2223	Blueberries

2224	Grapes

2229	Other bush and vine fruits

223 Ornamental horticulture & nurseries (floriculture, etc.)

224 Tree farms

2241	Christmas tree farms

2242	Other coniferous trees

2243	Deciduous trees

2249	Other tree farms

225 Sugarbush

229 Other orchards, etc.

23	CONFINED FEEDING OPERATIONS

231 Livestock

2311	Beef

2312	Dairy

2313	Swine

2314	Lamb

2319	Other livestock

232 Poultry

2321	Chicken

2322	Turkeys

2329	Other

233 Pisciculture

2331	Aquaculture

2332	Fish hatchery

239 Other confined feeding operations

24	OTHER AGRICULTURAL LAND

241 Farmsteads

242 Greenhouses and mushroom houses

243 Stables & racetracks (non-commercial training areas)

244 Sod

249 Other

3 BRUSH OR TRANSITIONAL BETWEEN OPEN AND FORESTED

31	HERBACEOUS, NON-WOODY VEGATION

32	SHRUB/BRUSH

33	MIXED HERBACEOUS AND SHRUB/BRUSH

4 FOREST ([nn] = Society of American Foresters type number)

41	BROADLEAF FOREST (generally deciduous)

411 Boreal hardwoods

4111	Aspen [16]

4112	Pin cherry [17]

4113	Paper birch [18]

4119	Other boreal hardwoods

412 Northern hardwoods

4121	Sugar maple [27]

4122	Sugar maple/Beech/Birch [25]

4123	Sugar maple/Basswood [26]

4124	Black cherry/Maple [28]

4125	Beech/Sugar maple [60]

4126	Red maple [28]

4129	Other northern hardwoods

413 Upland Oaks

4131	Chestnut oak [44]

4132	White oak/Black oak/Northern red oak [52]

4133	White oak [53]

4134	Black oak [110]

4135	Northern red oak [55]

4136	Northern pin oak [14]

4139	Other upland oaks

414 Other hardwoods

4141	Gray birch/Red maple [19]

4142	Black ash/Elm/Red maple [39]

4143	Hawthorn [104]

42 CONIFEROUS FOREST (generally evergreen)

421 Boreal conifers

4211	Jack pine [1]

4212	Balsam fir [5]

4213	Black spruce [12]

4214	Black spruce/Tamarack [13]

4215	White spruce [107]

4216	Tamarack [38]

4219	Other boreal conifers

422 Spruce-fir types

4221	Red spruce [32]

4222	Red spruce/Balsam fir [33]

4223	Red spruce/Fraser fir [34]

4224	Northern white cedar [37]

4229	Other spruce-fir types

423 Pine and hemlock

4231	Red pine [15]

4232	White pine [21]

4233	White pine/Hemlock [22]

4234	Eastern hemlock [23]

4235	Eastern red cedar [46]

4239	Other pine and hemlock

43	MIXED CONIFEROUS-BROADLEAF FOREST

431 Mixed spruce-fir types

4311	Red spruce/Yellow birch [30]

4312	Red spruce/Sugar maple/Beech [31]

4313	Paper birch/Red spruce/Balsam fir [35]

432 Mixed pine/hemlock types

4321	White pine/Red oak/Red maple [20]

4322	White pine/Chestnut oak [51]

4323	Hemlock/Yellow birch [24]

5 WATER (see 143 for transportation uses and 233 for agricultural uses)

51	RIVERS, CANALS AND OTHER WATERWAYS

511 Canal

512 River or Stream

519 Other waterways

52	LAKES AND PONDS

53	RESERVOIRS (and other artificial water surfaces)

54	BAYS/ESTUARIES

6 WETLANDS (not including open water)

61	FORESTED WETLAND

611	Broad-leaved deciduous

612	Needle-leaved deciduous

613	Broad-leaved evergreen

614	Needle-leaved evergreen

615	Dead

619	Mixed deciduous and coniferous forested wetland

62	NON-FORESTED WETLAND

621 Aquatic bed

6211	Algal

6212	Aquatic moss

6213	Rooted vascular

6214	Floating

622 Moss-lichen

6221	Moss dominant (bogs and fens)

6222	Lichens dominant

623 Emergent wetland

6231	Wet meadow

6232	Shallow marsh

6233	Deep marsh

624 Scrub-shrub wetland

6241	Broad-leaved deciduous

6242	Needle-leaved deciduous

6243	Broad-leaved evergreen

6244	Needle-leaved evergreen

6245	Dead

629 Other non-forested, non-tidal wetland

63 TIDAL WETLANDS

631	Saltmarsh

632	Tidal flat

639	Other tidal wetland

7 BARREN LAND

71	SALT FLATS

72	BEACHES AND RIVER BANKS

721	Sand beach

722	Gravel beach

723	River banks

729	Other beaches/riverbanks

73	SANDY AREAS (Non-Beaches)

731	Sand dunes

732	Sand pits

739	Other sandy areas

74	BARE/EXPOSED ROCK

741	Rock knobs

742	Escarpments/Cliffs

743	Shoreline rock outcrop

744	Riverbank rock outcrop

749	Other bare/exposed rock

75	STRIP MINE/QUARRY OR GRAVEL PIT

76	DISTURBED LAND

79	OTHER BARREN LANDS

8 TUNDRA

81	SHRUB AND BRUSH

82	HERBACEOUS

83	BARE GROUND

84	WET

85	MIXED

9 PERMANENT SNOW & ICE (no known examples in New Hampshire)

# Text boxes

NH Land Use Mapping Standard

CTAP Land Use Mapping Project

GRANIT/Complex Systems Research Center

March, 2007