Identification_Information:

Citation:

Citation_Information:

Originator: U.S. Department of Agriculture, Natural Resources

Conservation Service

Publication_Date: 20050525

Title: Soil Survey Geographic (SSURGO) database for Merrimack and

Belknap County Area, New Hampshire

Publication_Information:

Publication_Place: Fort Worth, Texas

Publisher: U.S. Department of Agriculture, Natural Resources

Conservation Service

Other_Citation_Details: nh609

Online_Linkage: URL:http://www.ftw.nrcs.usda.gov/ssur_data.html

Description:

Abstract:

This data set is a digital soil survey and generally is the most

detailed level of soil geographic data developed by the National

Cooperative Soil Survey. The information was prepared by digitizing

maps, by compiling information onto a planimetric correct base

and digitizing, or by revising digitized maps using remotely

sensed and other information.

This data set consists of georeferenced digital map data and

computerized attribute data. The map data are in a soil survey area

extent format and include a detailed, field verified inventory

of soils and miscellaneous areas that normally occur in a repeatable

pattern on the landscape and that can be cartographically shown at

the scale mapped. A special soil features layer (point and line

features) is optional. This layer displays the location of features

too small to delineate at the mapping scale, but they are large

enough and contrasting enough to significantly influence use and

management. The soil map units are linked to attributes in the

National Soil Information System relational database, which gives

the proportionate extent of the component soils and their properties.

Purpose:

SSURGO depicts information about the kinds and distribution of

soils on the landscape. The soil map and data used in the SSURGO

product were prepared by soil scientists as part of the National

Cooperative Soil Survey.

Supplemental_Information:

Digital versions of hydrography, cultural features, and other

associated layers that are not part of the SSURGO data set may be

available from the primary organization listed in the Point of

Contact.

Time_Period_of_Content:

Time_Period_Information:

Range_of_Dates/Times:

Beginning_Date: 0000

Ending_Date: 20050525

Currentness_Reference: publication date

Status:

Progress: Complete

Maintenance_and_Update_Frequency: As needed

Spatial_Domain:

Bounding_Coordinates:

West_Bounding_Coordinate: -72.113

East_Bounding_Coordinate: -71.144

North_Bounding_Coordinate: 43.768

South_Bounding_Coordinate: 42.993

Keywords:

Theme:

Theme_Keyword_Thesaurus: None

Theme_Keyword: soil survey

Theme_Keyword: soils

Theme_Keyword: Soil Survey Geographic

Theme_Keyword: SSURGO

Place:

Place_Keyword_Thesaurus: USGS Geographic Names Information System (GNIS)

Place_Keyword: New Hampshire

Place_Keyword: Merrimack and Belknap County Area

Place_Keyword: Squam Mountains Quadrangle

Place_Keyword: Melvin Village Quadrangle

Place_Keyword: Center Harbor Quadrangle

Place_Keyword: Holderness Quadrangle

Place_Keyword: Ashland Quadrangle

Place_Keyword: Grafton Quadrangle

Place_Keyword: Wolfeboro Quadrangle

Place_Keyword: West Alton Quadrangle

Place_Keyword: Laconia Quadrangle

Place_Keyword: Winnisquam Lake Quadrangle

Place_Keyword: Bristol Quadrangle

Place_Keyword: Danbury Quadrangle

Place_Keyword: Sunapee Lake North Quadrangle

Place_Keyword: New London Quadrangle

Place_Keyword: Alton Quadrangle

Place_Keyword: Gilmanton Ironworks Quadrangle

Place_Keyword: Belmont Quadrangle

Place_Keyword: Northfield Quadrangle

Place_Keyword: Franklin Quadrangle

Place_Keyword: Andover Quadrangle

Place_Keyword: Sunapee Lake South Quadrangle

Place_Keyword: Bradford Quadrangle

Place_Keyword: Parker Mountain Quadrangle

Place_Keyword: Pittsfield Quadrangle

Place_Keyword: Loudon Quadrangle

Place_Keyword: Penacook Quadrangle

Place_Keyword: Webster Quadrangle

Place_Keyword: Warner Quadrangle

Place_Keyword: Washington Quadrangle

Place_Keyword: Hillsboro Upper Village Quadrangle

Place_Keyword: Gossville Quadrangle

Place_Keyword: Suncook Quadrangle

Place_Keyword: Concord Quadrangle

Place_Keyword: Hopkinton Quadrangle

Place_Keyword: Henniker Quadrangle

Place_Keyword: Candia Quadrangle

Place_Keyword: Manchester North Quadrangle

Place_Keyword: Goffstown Quadrangle

Place_Keyword: Weare Quadrangle

Place_Keyword: Deering Quadrangle

Access_Constraints: None

Use_Constraints:

The U.S. Department of Agriculture, Natural Resources Conservation

Service, should be acknowledged as the data source in products

derived from these data.

This data set is not designed for use as a primary regulatory tool

in permitting or citing decisions, but may be used as a reference

source. This is public information and may be interpreted by

organizations, agencies, units of government, or others based on

needs; however, they are responsible for the appropriate

application. Federal, State, or local regulatory bodies are not to

reassign to the Natural Resources Conservation Service any

authority for the decisions that they make. The Natural Resources

Conservation Service will not perform any evaluations of these maps

for purposes related solely to State or local regulatory programs.

Photographic or digital enlargement of these maps to scales greater

than at which they were originally mapped can cause misinterpretation

of the data. If enlarged, maps do not show the small areas of

contrasting soils that could have been shown at a larger scale. The

depicted soil boundaries, interpretations, and analysis derived from

them do not eliminate the need for onsite sampling, testing, and

detailed study of specific sites for intensive uses. Thus, these data

and their interpretations are intended for planning purposes only.

Digital data files are periodically updated. Files are dated, and

users are responsible for obtaining the latest version of the data.

Point_of_Contact:

Contact_Information:

Contact_Organization_Primary:

Contact_Organization: U.S. Department of Agriculture, Natural

Resources Conservation Service

Contact_Position: State Soil Scientist

Contact_Address:

Address_Type: mailing address

Address: Federal Building

City: Durham

State_or_Province: New Hampshire

Postal_Code: 03824-2043

Contact_Voice_Telephone: 603 868 7581

Contact_TDD/TTY_Telephone: 202 720 2600

Contact_Facsimile_Telephone: 603 868 5301

Data_Quality_Information:

Attribute_Accuracy:

Attribute_Accuracy_Report: Attribute accuracy is tested by manual

comparison of the source with hard copy plots and/or symbolized

display of the map data on an interactive computer graphic system.

Selected attributes that cannot be visually verified on plots or

on screen are interactively queried and verified on screen. In

addition, the attributes are tested against a master set of valid

attributes. All attribute data conform to the attribute codes in

the signed classification and correlation document and amendment(s).

Logical_Consistency_Report:

Certain node/geometry and topology GT- polygon/chain relationships

are collected or generated to satisfy topological requirements

(the GT-polygon corresponds to the soil delineation). Some of these

requirements include: chains must begin and end at nodes, chains

must connect to each other at nodes, chains do not extend through

nodes, left and right GT-polygons are defined for each chain

element and are consistent throughout, and the chains representing

the limits of the file are free of gaps. The tests of logical

consistency are performed using vendor software. All internal

polygons are tested for closure with vendor software and are checked

on hard copy plots. All data are checked for common soil lines (i.e.,

adjacent polygons with the same label). Edge locations generally do

not deviate from centerline to centerline by more than 0.01 inch.

The Merrimack and Belknap County Area soil survey has not been edge matched

with SSURGO certified counties of Grafton, Cheshire, Hillsborough Western

Part, Hillsborough Eastern Part, Rockingham, Strafford and Sullivan, New

Hampshire.  The county borders are not exact match.

Completeness_Report:

A map unit is a collection of areas defined and named in terms of

their soil components or miscellaneous areas or both. Each map

unit differs in some respect from all others in a survey area and

each map unit has a symbol that uniquely identifies the map unit

on a soil map. Each individual area, point, or line so identified

on the map is a delineation.

Soil Scientists identify small areas of soils or miscellaneous areas

that have properties and behavior significantly different than the

named soils in the surrounding map unit. These minor components

may be indicated as special features. If they have a minimal effect

on use and management, or could not be precisely located, they may

not be indicated on the map.

A map unit has specified kinds of soils or miscellaneous areas

(map unit components), each with a designated range in

proportionate extent. Map units include one or more kinds of soil

or miscellaneous area. Miscellaneous areas are areas that have little

or no recognizable soil.

Specific National Cooperative Soil Survey standards and procedures

were used in the classification of soils, design and name of map

units, and location of special soil features. These standards are

outlined in Agricultural Handbook 18, Soil Survey Manual, 1993,

USDA, NRCS; Agricultural Handbook 436, Soil Taxonomy, 1995,

USDA, NRCS; and all Amendments; Keys to Soil Taxonomy,

(current issue) USDA, NRCS; National Soil Survey

Handbook, title 430-VI,(current issue) USDA, NRCS.

The actual composition and interpretive purity of the map unit

delineations were based on data collected by scientists during

the course of preparing the soil maps. Adherence to National

Cooperative Soil Survey standards and procedures is based on

peer review, quality control, and quality assurance. Quality

control is outlined in the memorandum of understanding for the

soil survey area and in documents that reside with the Natural

Resources Conservation Service state soil scientist. Four kinds

of map units are used in soil surveys: consociations, complexes,

associations, and undifferentiated groups.

Consociations - Consociations are named for the dominant soil.

In a consociation, delineated areas use a single name from the

dominant component in the map unit. Dissimilar components are

minor in extent. The soil component in a consociation may be

identified at any taxonomic level. Soil series is the lowest

taxonomic level. A consociation that is named as a miscellaneous

area is dominantly that kind of area and minor components do not

significantly affect the use of the map unit. The total amount of

dissimilar inclusions of other components in a map unit generally

does not exceed about 15 percent if limiting and 25 percent if

nonlimiting. A single component of a dissimilar limiting inclusion

generally does not exceed 10 percent if very contrasting.

Complexes and associations - Complexes and associations consist

of two or more  dissimilar components that occur in a regularly

repeating pattern. The total amount of other dissimilar components

is minor extent. The following arbitrary rule determines whether

complex or association is used in the name. The major components

of an association can be separated at the scale of mapping. In

either case, because the major components are sufficiently different

in morphology or behavior, the map unit cannot be called a

consociation. In each delineation of a complex or an association,

each major component is normally present though their proportions

may vary appreciably from one delineation to another. The total

amount of inclusions in a map unit that are dissimilar to any of

the major components does not exceed 15 percent if limiting and

25 percent if nonlimiting. A single kind of dissimilar limiting

inclusion usually does not exceed 10 percent.

Undifferentiated groups - Undifferentiated groups consist of two

or more components that are not consistently associated

geographically and, therefore, do not always occur together in

the same map delineation. These components are included in the

same named map unit because their use and management are the same

or very similar for common uses. Generally they are grouped together

because some common feature, such as steepness, stoniness, or

flooding, determines their use and management. If two or more

additional map units would serve no useful purpose, they may be

included in the same unit. Each delineation has at least one of the

major components, and some may have all of them. The same principles

regarding the proportion of minor components that apply to

consociations also apply to undifferentiated groups. The same

principles regarding proportion of inclusion apply to

undifferentiated groups as to consociations.

Minimum documentation consists of three complete soil profile

descriptions that are collected for each soil added to the legend,

one additional per 3,000 acres mapped; three 10 observation

transects for each map unit, one additional 10 point transect per

3,000 acres.

A defined standard or level of confidence in the interpretive

purity of the map unit delineations is attained by adjusting the

kind and intensity of field investigations. Field investigations

and data collection are carried out in sufficient detail to name

map units and to identify accurately and consistently areas of

about 3 to 5 acres for an Order 2 survey and about 35 to 50 acres

for an Order 3 survey.

Positional_Accuracy:

Horizontal_Positional_Accuracy:

Horizontal_Positional_Accuracy_Report:

The accuracy of these digital data is based upon their

compilation to base maps that meet National Map

Accuracy Standards at a scale of 1 inch equals 1,000

feet. The difference in positional accuracy between the

soil boundaries and special soil features locations in the

field and their digitized map locations is unknown. The

locational accuracy of soil delineations on the ground varies

with the transition between map units.

For example, on long gently sloping landscapes the transition

occurs gradually over many feet. Where landscapes change

abruptly from steep to level, the transition will be very

narrow. Soil delineation boundaries and special soil features

generally were digitized within 0.01 inch of their locations on

the digitizing source. The digital map elements are edge matched

between data sets. The data along each quadrangle edge are

matched against the data for the adjacent quadrangle. Edge

locations generally do not deviate from centerline to centerline

by more than 0.01 inch.

Lineage:

Source_Information:

Source_Citation:

Citation_Information:

Originator:

U.S. Department of Agriculture, Soil Conservation

Service

Publication_Date: 1965

Title: Soil Survey of Merrimack County, New Hampshire

Geospatial_Data_Presentation_Form: map

Publication_Information:

Publication_Place: Washington, D.C.

Publisher: U.S. Government Printing Office

Source_Scale_Denominator: 20,000

Type_of_Source_Media: paper

Source_Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Calendar_Date:19630304

Source_Currentness_Reference: publication date

Source_Citation_Abbreviation: SCS1

Source_Contribution: attribute data, and soil symbols

Source_Information:

Source_Citation:

Citation_Information:

Originator:

U.S. Department of Agriculture, Soil Conservation

Service

Publication_Date: 1968

Title: Soil Survey of Belknap County, New Hampshire

Geospatial_Data_Presentation_Form: map

Publication_Information:

Publication_Place: Washington, D.C.

Publisher: U.S. Government Printing Office

Source_Scale_Denominator: 15,840

Type_of_Source_Media: paper

Source_Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Calendar_Date:19650708

Source_Currentness_Reference: publication date

Source_Citation_Abbreviation: SCS2

Source_Contribution: attribute data, and soil symbols

Source_Information:

Source_Citation:

Citation_Information:

Originator:

U.S. Department of Agriculture, Soil Conservation

Service

Publication_Date: 1985 & 1986

Title: film positives

Geospatial_Data_Presentation_Form: map

Source_Scale_Denominator: 24,000

Type_of_Source_Media: stable-base material

Source_Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Calendar_Date:

Source_Currentness_Reference: publication date

Source_Citation_Abbreviation: SCS3

Source_Contribution: digitizing source

Source_Information:

Source_Citation:

Citation_Information:

Originator: U.S. Geological Survey

Publication_Date: 1969-1987

Title: topographical maps

Geospatial_Data_Presentation_Form: map

Publication_Information:

Publication_Place: Reston, Virginia

Publisher: U.S. Geological Survey

Source_Scale_Denominator: 24,000

Type_of_Source_Media: stable-base material

Source_Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Calendar_Date:

Source_Currentness_Reference: publication date

Source_Citation_Abbreviation: USGS1

Source_Contribution: compilation base

Source_Information:

Source_Citation:

Citation_Information:

Originator: U.S. Geological Survey

Publication_Date: 1989

Title: multiple analog orthophotographs

Geospatial_Data_Presentation_Form: map

Publication_Information:

Publication_Place: Reston, Virginia

Publisher: U.S. Geological Survey

Source_Scale_Denominator: 24,000

Type_of_Source_Media: stable-base material

Source_Time_Period_of_Content:

Time_Period_Information:

Range_of_Dates/Times:

Beginning_Date: 1974

Ending_Date: 1986

Source_Currentness_Reference: publication date

Source_Citation_Abbreviation: USGS2

Source_Contribution: compilation base

Source_Information:

Source_Citation:

Citation_Information:

Originator: U.S. Department of Agriculture,

Natural Resources Conservation Service

Publication_Date: 2004

Title: National Soil Information System (NASIS) data base

Geospatial_Data_Presentation_Form: unknown

Publication_Information:

Publication_Place: Fort Collins, Colorado

Publisher:

U.S. Department of Agriculture,

Natural Resources Conservation Service

Type_of_Source_Media: database

Source_Time_Period_of_Content:

Time_Period_Information:

Range_of_Dates/Times:

Beginning_Date: 2004

Ending_Date: 2004

Source_Currentness_Reference: publication date

Source_Citation_Abbreviation: NASIS

Source_Contribution: attribute (tabular) information

Process_Step:

Process_Description:

Field procedures for the second order soil survey

included plotting of soil boundaries determined by field observations

and by interpretation of remotely sensed data. References used were the

USGS topographical maps and old soil surveys of Merrimack Co.

(published 1965) and Belknap Co. (published 1968). Boundaries were

verified at closely spaced intervals, and the soils in each delineation

were identified by traversing and transecting the landscape. Soil

scientists described and sampled the soils, analyzed the samples in the

laboratory, and statistically analyzed the data.

Source_Used_Citation_Abbreviation: NRCS1, SCS1, SCS2

Process_Date: 2004

Process_Step:

Process_Description:

The field maps were manually compiled to 1:24,000

full quadrangle film positives in NAD27.

Source_Used_Citation_Abbreviation: NRCS1

Process_Date: 2004

Process_Step:

Process_Description: The data were sent to the U.S. Department of

Agriculture, Natural Resources Conservation Service, Wisconsin

Digitizing Unit, Madison, Wisconsin (WIDU). The annotated soil

delineation overlays were sent to Midwest Graphics, Kenosha, Wisconsin

for raster scanning at 250 dpi on an Intergraph Anatach scanner in

tiff uncompressed format.  The tiff files were geo-referenced to a

digital full quad index using ArcGIS 8.3 ArcMap.  The raster scanned

data were imported into LT2000 version 1.0 maps.  Once all the scanned

soil lines were added to the maps, a county border was added.  The

soils and special soil features were digitized on screen from the

annotated soil delineations tiff files in LT2000 at a resolution of 0.01

inch.  The raster editing, labeling, edge-matching, and vector

conversion were done in LT2000.  Check plots of the soils and special

soil features were reviewed by a soil scientist and cartographic staff

at the WIDU.  The soils and special soil features data were run through

a series of LT2000 macros for correctness and completeness.  These

macros smoothed and thinned out line work, added nodes for every 3000

vertices, added corner nodes and snapped nodes across the neatlines.

The soils and special soil features data were then exported as Digital

Line Graph-3 Optional format files (DLGs) in LT2000.  The DLGs were

evaluated with the modified Oct. 1998 ARC/INFO SSURGO Evaluation AMLs

provided by U.S. Department of Agriculture, Natural Resources

Conservation Service, National Cartography and Geospatial Center, Fort

Worth, Texas (NCGC).  The DLG’s were imported to ARC coverages.  The

full quad coverages were merged together into a seamless full county

coverage and projected to NAD83, UTM zone 19.

Source_Used_Citation_Abbreviation: SCS3

Process_Date: 2005

Spatial_Data_Organization_Information:

Direct_Spatial_Reference_Method: Vector

Spatial_Reference_Information:

Horizontal_Coordinate_System_Definition:

Geographic:

Latitude_Resolution: 0.0000001

Longitude_Resolution: 0.0000001

Geographic_Coordinate_Units: decimal degrees

Geodetic_Model:

Horizontal_Datum_Name: North American Datum of 1983

Ellipsoid_Name: Geodetic Reference System 80

Semi-major_Axis: 6378137.0

Denominator_of_Flattening_Ratio: 298.257

Entity_and_Attribute_Information:

Detailed_Description:

Entity_Type:

Entity_Type_Label: Special Soil Features

Entity_Type_Definition:

Special Soil Features represent soil, miscellaneous area, or landform

features that are too small to be digitized as soil delineations

(area features).

Entity_Type_Definition_Source:

Agricultural Handbook 18, Soil Survey Manual, 1993, USDA, SCS.

Attribute:

Attribute_Label: Special Soil Features Codes

Attribute_Definition:

Special Soil Features labels represent specific Special Soil

Features. These features are identified with a descriptive

label. The label is assigned to the point or line assigned

to represent the feature on maps.

Attribute_Definition_Source:

Agricultural Handbook 18, Soil Survey Manual, 1993, USDA, SCS;

National Soil Survey Handbook, Title 430-VI, part 647

(current issue), USDA, NRCS.

Attribute_Domain_Values:

Codeset_Domain:

Codeset_Name:

Classification and Correlation of the Soils of Merrimack and

Belknap County Area, New Hampshire

Codeset_Source:

U.S. Department of Agriculture, Natural Resources

Conservation Service

Overview_Description:

Entity_and_Attribute_Overview:

Map Unit Delineations are closed polygons that may be dominated

by a single soil or miscellaneous area component plus allowable

similar or dissimilar soils, or they can be geographic mixtures

of groups of soils or soils and miscellaneous areas.

The map unit symbol uniquely identifies each closed map unit

delineation. Each symbol corresponds to a map unit name. The

map unit key is used to link to information in the National

Soil Information System tables.

Map Unit Delineations are described by the National Soil

Information System database. This attribute database gives the

proportionate extent of the component soils and the properties for

each soil. The database contains both estimated and measured data

on the physical and chemical soil properties and soil

interpretations for engineering, water management, recreation,

agronomic, woodland, range, and wildlife uses of the soil.

The National Soil Information System database contains static

metadata. It documents the data structure and includes such

information as what tables, columns, indexes, and relationships

are defined as well as a variety of attributes of each of these

database objects. Attributes include table and column

descriptions and detailed domain information.

The National Soil Information System database also contains a

distribution metadata. It records the criteria used for selecting

map units and components for inclusion in the set of distributed

data.

Special features are described in the feature table.  It includes an

area symbol, feature label, feature name, and feature description for

each special and ad hoc feature in the survey area.

Entity_and_Attribute_Detail_Citation:

Soil Taxonomy: A basic system of soil classification for making and

interpreting soil surveys. Agricultural Handbook 436, 1999, USDA, SCS.

Keys to Soil Taxonomy (current issue), USDA, SCS.

National Soil Survey Handbook, Title 430-VI, part 647 (current

issue), USDA, NRCS.

Agricultural Handbook 18, Soil Survey Manual, 1993, USDA, SCS.

Distribution_Information:

Distributor:

Contact_Information:

Contact_Organization_Primary:

Contact_Organization: U.S. Department of Agriculture, Natural

Resources Conservation Service, National

Cartography and Geospatial Center

Contact_Address:

Address_Type: mailing and physical address

Address: 501 West Felix Street, Building 23, P.O. Box 6567

City: Fort Worth

State_or_Province: Texas

Postal_Code: 76115

Contact_Voice_Telephone: 800 672 5559

Contact_TDD/TTY_Telephone: 202 720 2600

Contact_Facsimile_Telephone: 817 509 346

Resource_Description: Merrimack and Belknap County Area, New Hampshire SSURGO

Distribution_Liability:

Although these data have been processed successfully on a computer

system at the U.S. Department of Agriculture, no warranty expressed

or implied is made by the Agency regarding the utility of the data

on any other system, nor shall the act of distribution constitute

any such warranty. The U.S. Department of Agriculture will warrant

the delivery of this product in computer readable format, and will

offer appropriate adjustment of credit when the product is determined

unreadable by correctly adjusted computer input peripherals, or

when the physical medium is delivered in damaged condition. Request

for adjustment of credit must be made within 90 days from the date

of this shipment from the ordering site.

The U.S. Department of Agriculture, nor any of its agencies are

liable for misuse of the data, for damage, for transmission of

viruses, or for computer contamination through the distribution of

these data sets. The U.S. Department of Agriculture (USDA) prohibits

discrimination in all its programs and activities on the basis of race,

color, national origin, sex, religion, age, disability, political

beliefs, sexual orientation, or marital or family status. (Not all

prohibited bases apply to all programs.)

Standard_Order_Process:

Digital_Form:

Digital_Transfer_Information:

Format_Name: ARC/INFO coverage

Format_Information_Content: spatial

Transfer_Size: 25

Digital_Transfer_Option:

Offline_Option:

Offline_Media: CD-ROM

Recording_Format: ISO 9660 Level 2

Digital_Form:

Digital_Transfer_Information:

Format_Name: ArcView shapefile

Format_Information_Content: spatial

Transfer_Size: 1.0

Digital_Transfer_Option:

Offline_Option:

Offline_Media: CD-ROM

Recording_Format: ISO 9660 Level 2

Digital_Form:

Digital_Transfer_Information:

Format_Name: ASCII

Format_Information_Content: keys and attributes

Transfer_Size: 1.0

Digital_Transfer_Option:

Offline_Option:

Offline_Media: CD-ROM

Recording_Format: ISO 9660 Level 2

Fees:

The charge is $50 for a CD-ROM that contains one or more data

sets. A data set is one soil survey area that includes both spatial

and attribute data.

Ordering_Instructions:

Call or write to organizations listed under Distributor. Spatial

line data and locations of special feature symbols are in ARC/INFO

coverage and export formats, and ArcView shapefile format. The

National Soil Information System attribute soil data are available

in variable length, pipe delimited, ASCII file format.

Turnaround: 10 working days

Metadata_Reference_Information:

Metadata_Date: 20050525

Metadata_Contact:

Contact_Information:

Contact_Organization_Primary:

Contact_Organization: U.S. Department of Agriculture, Natural

Resources Conservation Service

Contact_Position: State Soil Scientist

Contact_Address:

Address_Type: mailing address

Address: Federal Building

City: Durham

State_or_Province: New Hampshire

Postal_Code: 03824-2043

Contact_Voice_Telephone: 603 868 7581

Contact_TDD/TTY_Telephone: 202 720 2600

Contact_Facsimile_Telephone: 603 868 5301

Metadata_Standard_Name: Content Standard for Digital Geospatial Metadata

Metadata_Standard_Version: FGDC-STD-001-1998